## Slide 1: EDCA Parameters
Date: 2012-07-16
Authors:

## Slide 4: Introduction I
Traffic may be very different across 11ah STAs [1]
  Sensor / offload traffic
11ah STAs may be very different in capabilities [1]
  Battery powered / Mains powered
Different STAs types/traffic may have to coexist while accessing the medium
Currently, all the STAs in a BSS use same EDCA parameters
We want to improve EDCA, allowing to have different STAs/type of STAs to use different EDCA parameters sets
  E.g. battery-operated /sensor STAs to have different EDCA parameters than the ones of mains-operated/offload STAs, for certain ACs

## Slide 5: Introduction II
One major source of power consumption is due to the time spent in sensing idle medium and decode third party packets while performing backoff.
One way to reduce awake time is to provide high priority (shorter AIFS, CW) to the transmissions to be favored in terms of energy consumption.
  E.g. Using AC_VO for sensor traffic [2,3]
Currently, EDCA parameters are same per STA, hence a battery-operated STA and a mains powered one would have same access priority
  E.g. AC_VO sensor traffic of a small battery-operated sensor has same priority as the AC_VO sensor traffic of a mains powered one
  Not fair in terms of energy consumption
AP
Video
Voice
ACK
ACK
Sensor
ACK
Video
ACK
STA wakes up
RX mode
…

## Slide 6: Multiple EDCA parameters sets
Define an EDCA parameter set per STA or type of STA.
Example of options for defining them
  Define a set per type of STA: specs to define the default values per each set.
  Parameters of each set (per Type of STA) are defined in relative terms, referred to a reference baseline set
    Updates to the value of the reference set results in corresponding updates in the other sets
  AP indicates EDCA parameter set in association response (per STA)
  AP may indicate 2 or more sets in beacon (per STA Type )
Tuning of EDCA parameters is left to the AP implementation/certification

## Slide 7: Multiple EDCA parameters sets
Example: define 2 EDCA parameter sets:
  ‘Legacy’ EDCA parameter set: used by regular STAs as specified by current specs
  ‘Power Save (PS)’ EDCA parameter set: used by STAs with special requirements, E.g. battery operated STAs
For example, possible settings are:
  Set the parameters of ‘PS EDCA set’ so that each AC has higher priority than the corresponding AC in the ‘Legacy EDCA set’
  Give highest priority only to AC_VO in ‘PS EDCA set’ and keep other ACs parameters equal between ‘PS EDCA set’ and ‘Legacy EDCA’ set.
  Give same parameters to all ACs in the ‘PS EDCA set’; parameters provide higher priority than the ones in AC_VO in the ‘Legacy EDCA set’
    This though would give unfair advantage to battery-devices with a lot of e.g. BE traffic, over simple battery-devices with low duty cycle VO traffic
    For STAs of same type, power saving advantage should favor sensor traffic (VO): better preserve differentiation across ACs.

## Slide 8: Conclusions
We propose to define different EDCA parameter sets for different STAs/types of STAs
  Allows prioritization of medium access based on the STA capabilities
  AP under control of the parameters value
  Other details TBD
    Signaling (if any)
    Per STA/ group of STA, how many groups…
    Default values
For further discussion
  Some traffic generated by 11ah STAs (Some sensor traffic) has peculiar characteristics (low duty cycle, small packets)
  Which AC should it use? AC_VO is suggested for highest priority
  Is it OK to lump it together with Voice traffic?

## Slide 9: Straw poll 1
Do you support to include in the TGah specification framework the concept of defining multiple EDCA parameters sets (signaling TBD; per STA/Type/group TBD)?

## Slide 10: References
[1] 11-11-0905-03-00ah-tgah-functional-requirements-and-evaluation-methodology
[2] 1230r1 802.11ah channel access improvement
[3] 1137r9 in R4.2.A