## Slide 1: PHY Overview
Date: 2012-07-16
Authors:

## Slide 2: Outline
Provide high level description of the PHY design for TGaf

## Slide 3: Design Requirements
High ACLR – 55dB at the channel edge for transmission at maximum allowed power
  Much higher than current 802.11 where channel edge is at around -20dBr
Support for 3 basic channel widths – 6,7,8MHz
Support for contiguous and non-contiguous transmission of the basic channel unit (due to scarcity of spectrum in urban area)
  Unlike 11ac where non-contiguous is supported only for the third largest BW
Re-use 11ac with modifications specific to TGaf
Support for longer delay spread outdoor deployments

## Slide 4: PHY Details
The PHY for TVWS channels is based on the 11ac 40MHz PHY as-is with a sampling frequency clock change,
  Sampling clock change increases symbol length and delay spread tolerance to meet 11af requirements
  VHT and non-HT DUP modes are the only supported modes
Signal BW occupies about 81% (compared to 91% in 11ac) of the TVWS channels in 6MHz and 8MHz regulatory domains. 7MHz regulatory domains re-use the 6MHz PHY
  This enable larger guard bands to allow filter roll off to achieve -55dBr
  Same PHY design for 6MHz and 8MHz channels with only a sampling clock change
TVWS channels are divided into an integer and even number of tones. This enables transmission and reception of multiple contiguous channels using one IFFT/FFT as in 11ac. 144 tones were chosen to meet the desired signal BW.

## Slide 5: Cont.
The PHY for multiple channels is based on the PHY for one channel.
  This concept is similar to the 11ac design of 160MHz and 80+80MHz whereby the tone location of DATA and pilots are the same in each case.
  All basic channel units (termed frequency segments in clause 23) are connect via an interleaver to maximized frequency diversity gain.