## Slide 1
Date: 2012-07-16
Authors:
Non-TIM Allocation
Name | Affiliations | Address | Phone | Email
Hyoungjin Kwon | ETRI | 138 Gajeongno, Yuseong-gu, Dajeon, Korea | +82 42 860 5635 | kwonjin@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Minho Cheong | ETRI |  |  | minho@etri.re.kr
Heejung Yu | ETRI |  |  | heejung@etri.re.kr
Jaewoo Park | ETRI |  |  | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  |  | Sk-lee@etri.re.kr
Eric Wong | Broadcom | 190 Mathilda Place, Sunnyvale, CA | +1 408 922 6672 | ewong@broadcom.com
Matthew Fischer | Broadcom |  |  | mfischer@broadcom.com
Minyoung Park | Intel | Hillsboro, OR | +1 503 712 4705 | minyoung.park@intel.com
Tom Tetzlaff | Intel |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel |  |  | emily.h.qi@intel.com
Thomas Kenney | Intel |  |  | 
Yongho Seok | LG Electronics | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jin Sam Kwak | LG Electronics |  |  | 

## Slide 2: Authors:
Name | Affiliations | Address | Phone | Email
Huai-Rong Shao | Samsung Electronics |  |  | hrshao@samsung.com
Chiu Ngo | Samsung Electronics |  |  | Chiu.ngo@samsung.com
Yong Liu | Marvell |  |  | yongliu@marvell.com
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Simone Merlin | Qualcomm | 5775 Morehouse Dr, San Diego, CA | +1 858 845 1243 | smerlin@qualcomm.com
Santosh Abraham | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Alfred Asterjadhi | Qualcomm |  |  | 
Amin Jafarian | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Chittabrata Ghosh | Nokia | Berkeley, CA | +1 650 200 7566 | chittabrata.ghosh@nokia.com
Klaus Doppler | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Osama Aboul-Magd | Huawei |  |  | Osama.AboulMagd@huawei.com
George Calcev | Huawei | Rolling Meadows,IL |  | George.Calcev@huawei.com
Young Hoon Kwon | Huawei |  |  | Younghoon.kwon@huawei.com
Betty Zhao | Huawei |  |  | Betty.Zhao@huawei.com
David Yangxun | Huawei |  |  | David.Yangxun@huawei.com
Bin Zhen | Huawei |  |  | ZhenBin@huawei.com
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn

## Slide 3
Authors:
Name | Affiliations | Address | Phone | Email
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Haiguang Wang | I2R | 1 Fusionopolis Way, #21-01 Connexis Tower, Singapore 138632 | +65-6408 2000 | hwang@i2r.a-star.edu.sg
Shoukang Zheng | I2R |  |  | skzheng@i2r.a-star.edu.sg
Yeow Wai Leong | I2R |  |  | wlyeow@i2r.a-star.edu.sg
Zander Lei | I2R |  |  | leizd@i2r.a-star.edu.sg
Jaya Shankar | I2R |  |  | jshankar@i2r.a-star.edu.sg
Anh Tuan Hoang | I2R |  |  | athoang@i2r.a-star.edu.sg
Joseph Teo Chee Ming | I2R |  |  | cmteo@i2r.a-star.edu.sg
ChaoChun Wang | MediaTek |  |  | chaochun.wang@mediatek.com
James Wang | MediaTek |  |  | james.wang@mediatek.com
Jianhan Liu | MediaTek |  |  | jianhan.liu@mediatek.com
Vish Ponnampalam | MediaTek |  |  | vish.ponnamplam@mediatek.com
James Yee | MediaTek |  |  | james.yee@mediatek.com
Thomas Pare | MediaTek |  |  | thomas.pare@mediatek.com
Kiran Uln | MediaTek |  |  | kiran.uln@mediatek.com

## Slide 4: Introduction
STAs covered by the AID segment are allowed to access channel within Restricted Access Window (RAW) and RAW Parameter Set (RPS) information element can be included in beacon frame for RAW [1,2].
Mechanism to set wake times and intervals for long sleeping low power devices has been proposed [3].
  This Target Wake Time (TWT) mechanism is useful for non-TIM STAs which choose not to have a TIM entry for the DL traffic signalling.
Is there a way to restrict access to assigned STAs only during Target Wake Times (TWTs)?
  AP can protect TWTs by Restricted Access Window (RAW) information included in beacon.

## Slide 5: Further Power Save of non-TIM STA
TWT concept [3] is fitted well for non-TIM STAs because it does not require beacon reception.
  Note that non-TIM STAs may be included in the broad range of long sleeping low power devices (= Z-class STA).
  But, assume that only non-TIM STAs are allowed to support TWT functionality.
AP can group non-TIM STAs supporting TWT in the same group. Then, if assigned TWTs are in the current beacon interval, AP can protect TWTs by RPS IE [2] included in beacon from the channel access of other groups of STAs listening the beacon.
  This minimizes contention between non-TIM STAs and other TIM STAs.
TWTn
TWT1
Beacon Interval
Restricted Access Window (RAW)
TWT2
RAW

## Slide 6: RAW Protection for non-TIM STA : Overlapped Case
Because AP performs TWT assignment in advance of normal UL/DL assignment for TIM STAs through beacon, AP should defer normal assignment until the end of the interval of last TWT.
  For example, if TWT is overlapped to TIM window for PS-Poll, TIM window starts after the interval of last TWT ends.
  However, in some cases, the cases that whole TWT is nested in the other RAW can not be inevitable.
  In the figure below, to protect the RAW1 for non-TIM from group of STAs which are allowed to access in the RAW2, RAW1 is not allowed to access for any TIM STA.
TWT1
Beacon Interval
RAW1 for non-TIM STA
TWT2
RAW
RAW2 for one group of TIM STA
Slot duration

## Slide 7: Summary
We proposed protection method of TWT for non-TIM STA.
  For indicating the TWT to TIM STA listening beacon, RAW for non-TIM STA is defined.
  TIM STA is not allowed to access RAW for non-TIM STA.
  Useful for power save of non-TIM STA

## Slide 8: Straw Poll
Do you support to include, in TGah Spec Framework document, the concept of the following?
  AP may indicate to TIM STAs RAW information during which no TIM STA is allowed to contend
Yes:
No:
Abstain:

## Slide 9: References
[1] “Uplink Channel Access General Procedure,” IEEE 802.11-12/0831r0
[2] “Restricted Access Window Signaling for Uplink Channel Access,” IEEE 802.11-12/0843r0
[3] “Target Wake Time,” IEEE 802.11-12/0823r0