## Slide 1: Active Scanning for 11ah
Date: 2012-07-13
Authors:
Name | Affiliations | Address | Phone | Email
Jae Seung Lee | ETRI | 161 Gajeong-dong, Yuseong-Gu, Daejoen, Korea | +82 42 860 1326 | jasonlee@etri.re.kr
Minho Cheong | ETRI |  | +82 42 860 5635 | minho@etri.re.kr
Hyoungjin Kwon | ETRI |  | +82 42 860 1698 | kwonjin@etri.re.kr
Heejung Yu | ETRI |  | +82 42 860 6204 | heejung@etri.re.kr
Jaewoo Park | ETRI |  |  | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  | +82 42 860 5919 | sk-lee@etri.re.kr
Eric Wong | Broadcom | 190 Mathilda Place, Sunnyvale, CA | +1 408 922 6672 | ewong@broadcom.com
Matthew Fischer | Broadcom |  |  | mfischer@broadcom.com
Minyoung Park | Intel | Hillsboro, OR | +1 503 712 4705 | minyoung.park@intel.com
Tom Tetzlaff | Intel |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel |  |  | emily.h.qi@intel.com
Thomas Kenney | Intel |  |  | 
Yongho Seok | LG Electronics | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jin Sam Kwak | LG Electronics |  |  | 

## Slide 2: Authors:
Jae Seung Lee, ETRI
Name | Affiliations | Address | Phone | Email
Huai-Rong Shao | Samsung Electronics |  |  | hrshao@samsung.com
Chiu Ngo | Samsung Electronics |  |  | Chiu.ngo@samsung.com
Yong Liu | Marvell |  |  | yongliu@marvell.com
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Simone Merlin | Qualcomm | 5775 Morehouse Dr, San Diego, CA | +1 858 845 1243 | smerlin@qualcomm.com
Santosh Abraham | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Alfred Asterjadhi | Qualcomm |  |  | 
Amin Jafarian | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Chittabrata Ghosh | Nokia | Berkeley, CA | +1 650 200 7566 | chittabrata.ghosh@nokia.com
Klaus Doppler | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Osama Aboul-Magd | Huawei |  |  | Osama.AboulMagd@huawei.com
George Calcev | Huawei | Rolling Meadows,IL |  | George.Calcev@huawei.com
Young Hoon Kwon | Huawei |  |  | Younghoon.kwon@huawei.com
Betty Zhao | Huawei |  |  | Betty.Zhao@huawei.com
David Yangxun | Huawei |  |  | David.Yangxun@huawei.com
Bin Zhen | Huawei |  |  | ZhenBin@huawei.com
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn

## Slide 3: Authors:
Jae Seung Lee, ETRI
Name | Affiliations | Address | Phone | Email
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Haiguang Wang | I2R | 1 Fusionopolis Way, #21-01 Connexis Tower, Singapore 138632 | +65-6408 2000 | hwang@i2r.a-star.edu.sg
Shoukang Zheng | I2R |  |  | skzheng@i2r.a-star.edu.sg
Yeow Wai Leong | I2R |  |  | wlyeow@i2r.a-star.edu.sg
Zander Lei | I2R |  |  | leizd@i2r.a-star.edu.sg
Jaya Shankar | I2R |  |  | jshankar@i2r.a-star.edu.sg
Anh Tuan Hoang | I2R |  |  | athoang@i2r.a-star.edu.sg
Joseph Teo Chee Ming | I2R |  |  | cmteo@i2r.a-star.edu.sg
ChaoChun Wang | MediaTek |  |  | chaochun.wang@mediatek.com
James Wang | MediaTek |  |  | james.wang@mediatek.com
Jianhan Liu | MediaTek |  |  | jianhan.liu@mediatek.com
Vish Ponnampalam | MediaTek |  |  | vish.ponnamplam@mediatek.com
James Yee | MediaTek |  |  | james.yee@mediatek.com
Thomas Pare | MediaTek |  |  | thomas.pare@mediatek.com
Kiran Uln | MediaTek |  |  | kiran.uln@mediatek.com

## Slide 4: Introduction
Short Beacon has been introduced in TGah
  Short Beacon in TGah includes Compressed SSID which is a CRC of the full SSID and Optional IE plus Duration to next Full Beacon (can be used in Passive scanning)
In this presentation, we proposed active scanning using Short Probe Response frame
Jae Seung Lee, ETRI

## Slide 5: Background (1/2)
Passive Scanning using Short Beacon in 11ah
  If the full SSID is unknown to the STAs, the STAs have to wait for the next full beacon
  This can increase the passive scanning time
Jae Seung Lee, ETRI
Time
Full Beacon
(with full information
including full SSID)
Short Beacon
Short Beacon
Full Beacon
(with full information
including full SSID)
STA can start association at
this point
STA starts passive scanning

## Slide 6: Background (2/2)
Active Scanning in current 802.11
  Faster than passive scanning, but the size of the Probe Response can be burden to 11ah (similar to full Beacon frame)
  If the STA has no prior knowledge of the APs, it sends probe request with wildcard SSID which causes probe response flooding
Jae Seung Lee, ETRI
Slide 6
Time
Full Beacon
(with full information
including full SSID)
Short Beacon
Short Beacon
Full Beacon
(with full information
including full SSID)
STA starts active scanning
Probe Responses
(with full information
including full SSID)
Probe Request
STA can start association at
this point

## Slide 7: Proposal
Approach: Active Scanning using short Probe Response frame
  Short Probe Response frame is used to achieve reduced overhead in active scanning
  Short Probe Response frame includes minimum information that is required for association
    STA can request optional information to be included in the short Probe Response frame
  Provides fast scanning with reduced traffic caused by Probe Response
Jae Seung Lee, ETRI
Time
Full Beacon
(with full information
including full SSID)
Short Beacon
Short Beacon
Full Beacon
(with full information
including full SSID)
STA starts active scanning
Short Probe Responses
(with minimum information)
Probe Request
STA can start association at
this point

## Slide 8: Short Probe Response format
Format is quite similar to Short Beacon
Short Probe Response frame
  Either Compressed SSID or Full SSID is included – STA can specify which one should be included in the Probe Request
  Other optional fields or optional IEs may be included
    For example: Capability information fields, Country IE, Power Constraint IE, RSN IE, Interworking IE, Roaming Consortium IE, other 11ah capabilities etc..
    STA can specify which optional fields or IEs to be included in the Short Probe Response frame when it sends Probe Request
Frame Control Field
Jae Seung Lee, ETRI
FC | DA | SA | Time stamp | Compressed SSID or full SSID | Duration to Next Full Beacon (option) | Other Optional Fields (TBD) | Optional IEs | FCS
Octets: 2 6 6 4 4 or up to 32 3 var var 4
Protocol Version | Type | Subtype | Next Full Beacon present | Full SSID Present (0: compressed SSID, 1: Full SSID ) | Presence of optional fields (TBD) | BSS BW | Security
Bits: 2 2 4 1 1 2 3 1

## Slide 9: Probe Response Option (1/2)
Probe Response Option field (TBD) is included in the Probe Request frame
  STA can choose which optional information to be included in the short Probe Response frame using Probe Response Option in the Probe Request frame
    STA requests minimum information that is required for association to the APs
  Indication of the optional information in the Probe Request should be done in optimized way
    Using Request element in current spec can increase the size of Probe Request too much
    Request element includes Element IDs of all the requested elements, and each Element ID of the requested element in the Request element consumes 1 octet  If many optional elements are requested using Request element, then the size of the Probe Request can be increased too much
Jae Seung Lee, ETRI
Slide 9
Notes: 삭제

## Slide 10: Probe Response Option (2/2)
Subfields of the Probe Response Option
  Request full SSID: If it is set to 1, full SSID is included in the Short Probe Response frame. Otherwise, compressed SSID is included
  Other requests for TBD optional information to be included in the Probe Response can be included in the Probe Response Option in the Probe Request frame
    For example: Request Capability Info, Request country IE , Request Power Constraint IE, Request RSN IE, Request interworking IE, Request Roaming Consortium, Request 11ah capabilities, etc…
Jae Seung Lee, ETRI
Slide 10
Request full SSID | Other Optional information to be included in the Probe Responses (TBD)
Bits: 1 TBD

## Slide 11: Scanning with Short Probe Response
Short Probe Response frame
    Includes only minimum information that is required by the STA for association
      STA can request which optional information to be included in the Probe Response
    Full SSID is included in the short Probe Response if it is requested by the STA
      If the STA has prior knowledge of the full SSID, then it may not request inclusion of full SSID (Compressed SSID is included instead)
STA can associate immediately after it receives short Probe Response since it contains information required for the STA’s association
  No need to wait for full Beacon for association if it receives the short Probe Response with the requested information
  If additional information on BSS is necessary besides association, the STA may use information included in the next full Beacon
    Duration to the Next Full Beacon can be included in the short Probe Response
  Useful if full beacon is not transmitted frequently or only short beacon is used
Jae Seung Lee, ETRI
Slide 11

## Slide 12: Summary
We proposed active scanning using Short Probe Response frame
  Reduced association delay of passive scanning using short beacon
  Reduced traffic caused by legacy Probe Response frame in active scanning
STA can associate immediately after it receives Short Probe Response
  Useful if full beacon is not transmitted frequently or only short beacon is used
Jae Seung Lee, ETRI

## Slide 13: Straw Poll 1
Do you support to include the following to the spec framework document?
  11ah STA may use short Probe Response frame for active scanning which is a shortened version of Probe Response frame
Yes:
No:
Abstain:
Jae Seung Lee, ETRI

## Slide 14: Straw Poll 2
Do you support to include the following to the spec framework document?
  Short Probe Response frame contains Timestamp, either Compressed SSID or full SSID, optional Duration to Next Full Beacon, other TBD optional fields and optional IEs
  Frame control field of Short Probe Response frame contains Next Full Beacon present field, Full SSID Present field which indicates whether Full SSID or Compressed SSID should be included, BSS Bandwidth field and Security field, and other TBD Presence of optional fields
Yes:
No:
Abstain:
Jae Seung Lee, ETRI

## Slide 15: Straw Poll 3
Do you support to include the following to the spec framework document?
  STA may indicate in the Probe Request which optional information to be included in the short Probe Response frame in optimized way
Yes:
No:
Abstain:
Jae Seung Lee, ETRI