## Slide 1: Uplink Data Delivery
Date: 2012-07-13
Authors:
Betty Zhao, et. al, Huawei
Name | Affiliations | Address | Phone | email
Yanping Jiang | Huawei |  |  | jiangyanping@huawei.com
Betty Zhao | Huawei |  |  | betty.zhao@huawei.com
David Xun Yang | Huawei |  |  | David.yangxun@huawei.com
Osama Aboul-Magd | Huawei |  |  | Osama.Aboulmagd@huawei.com
Young Hoon Kwon | Huawei |  |  | younghoon.kwon@huawei.com
George Calcev | Huawei |  |  | George.calcev@huawei.com
Yongho Seok | LG Electronics |  |  | 
Seunghee Han | LG Electronics |  |  | 
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jinsam Kwak | LG Electronics |  |  | 
Matthew Fischer | Broadcom |  |  | 
Eric Wong | Broadcom |  |  | 
Simone Merlin | Qualcomm |  |  | 
Zhi Quan | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 

## Slide 2
Name | Affiliations | Address | Phone | email
Yong Liu | Marvell |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Raja Banerjea | Marvell |  |  | 
Minyoung Park | Intel Corp. |  |  | 
Tom Tetzlaff | Intel Corp. |  |  | 
Emily Qi | Intel Corp. |  |  | 
Thomas Kenney | Intel Corp. |  |  | 
ChaoChun Wang | MediaTek |  |  | 
James Wang | MediaTek |  |  | 
Jianhan Liu | MediaTek |  |  | 
Vish Ponnampalam | MediaTek |  |  | 
James Yee | MediaTek |  |  | 
Sun, Bo | ZTE |  |  | 
Lv, Kaiying | ZTE |  |  | 
Huai-Rong Shao | Samsung |  |  | 
Chiu Ngo | Samsung |  |  | 
Minho Cheong | ETRI |  |  | 
Jae Seung Lee | ETRI |  |  | 
Heejung Yu | ETRI |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Chittabrara Ghosh | Nokia |  |  | 
Esa Tumaala | Nokia |  |  | 
Authors:
Betty Zhao, et. al, Huawei

## Slide 3: Introduction
So far, most contributions focus on DL data delivery with PS-Poll or trigger frame, such as [1] and [2].
According to the analysis [4, 5], UL data delivery is more problematic than DL data delivery in the real world, especially when sensor STAs and offloading STAs coexist.
- [3] has provided some solutions on the coexistence of Z-class STAs and H-class STAs.
We try to give a solution on the UL data delivery when sensor STAs and offloading STAs contend medium together.
Betty Zhao, et. al, Huawei

## Slide 4: Issues
Sensor STAs consume more power and have longer medium access time when they coexist with offloading STAs, because
- Sensor STAs are more likely to be hidden nodes of offloading STAs and suffer more collisions.
- Offloading STAs occupy the medium much longer than sensor STAs once they own the medium.
Because TIM can indicate the DL data explicitly, AP may reserve a duration of time in each Beacon Interval for the DL data and PS-Poll/trigger frame, such as [1] and [2]. And the remaining time in BI should be mainly for UL data delivery.
- DL/UL window is not restricted strictly for DL/UL data delivery. Actually, for the STAs not listening to beacon, no one can limit their behaviors.
DL window
UL window
Betty Zhao, et. al, Huawei

## Slide 5: Solution
To reduce the interference from offloading STAs on UL data delivery, UL window is divided to two parts:
- Sensor-only Window (SW)
- Mixed Window (MW)
AP indicates T1 and T2 in the beacon. T1 and T2 may vary from beacon to beacon.
- T1 is the time of end of DL window. T1 can be determined based on TIM.
- T2 is the time of end of SW. The estimation method of T2 is TBD. It may depend on AP’s knowledge of the traffic pattern of sensor STAs.
Sensor STAs with UL data may sleep until T1 and try to access the medium between T1 and T2 (SW). If its medium accessing or data delivery failed during SW, it still can retry during MW.
Offloading STAs are restricted to access the medium after T2 (MW).
DL window
UL window
SW
MW
sensor STAs
offloading STAs
T1
T2
Sensor STAs may sleep between beacon and T1, and then choose a time between T1 and T2 to wake up.
Betty Zhao, et. al, Huawei

## Slide 6: Benefits
Sensor STAs can save power by avoiding contending medium with offloading STAs.
Sensor STAs can reduce collision and medium access time, because most medium contentions are limited between sensor STAs.
Significantly alleviate the hidden node problem between sensor STAs and offloading STAs.
Betty Zhao, et. al, Huawei

## Slide 7: Straw Poll
Do you support that AP may indicate a window in beacon, and during that window offloading STAs can not access medium to send uplink data?
Betty Zhao, et. al, Huawei

## Slide 8: References
[1] 20120503r0_LGE-INTEL-Marvell-Nokia-Uplink-Channel-Access-Follow-Up
[2] 20120402r0-Qualcomm-Enhanced PS-Poll-Mechanism
[3] 20120101r0-Broadcom-TargetWakeTime
[4] SG Network System Requirements Specification v4.1-draft6, OpenSG Users Group
[5] SG-NET-diagram-r0.6Di , OpenSG Users Group
Betty Zhao, et. al, Huawei