## Slide 1: Probe Request Filtering Criteria
Date: 2012-07-06

## Slide 2: Abstract
We propose Probe Request filtering criteria considering STA’s capabilities and STA’s preference on AP to reduce unnecessary Probe Responses
Approach:
  Filter the Probe Request by the responding STAs based on preference and capabilities information of the STA in the Probe Request frame
    We propose the filtering information that should be included in the Probe Request frame for filtering
Jae Seung Lee, ETRI

## Slide 3: Background (1/2)
Jae Seung Lee, ETRI
This contribution is based on the following documents that have been presented at the previous IEEE 802.11 meeting
  11-12/0572r0 Selective transmission of the Probe Response for 11ai Spec Framework
  11-12/265r7 Spec Framework Proposal – Selective transmission of the Probe Response
  11-12/0063r1 Selective transmission of the Probe Response
  11-12/0064r0 Text for Selective transmission of the Probe Response
  11-12/0151r8 Specification Framework for TGai

## Slide 4: Background (2/2)
This contribution proposes text for TGai Specification Framework Document regarding scanning enhancement for fast network discovery
This contribution proposes the next level of detail of Section 6.1.6 Omission of Probe Response of the SFD
(11-12/0655r5) Probe request may contain new information that would enable an AP to make the decision whether to respond to a probe request. Examples of this kind of information include:
      Link Quality parameters
      AP Capabilities
      QoS Requirement
      Address/ID
Proposed Spec Framework text is included in the Motion section at the end of this contribution
Jae Seung Lee, ETRI
Slide 4

## Slide 5: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Jae Seung Lee, ETRI

## Slide 6: Probe Request Filtering Criteria
APs respond to the Probe Request even if the requesting STA cannot or will not be associated with the APs
  Sending Probe Response to such STAs is not necessary, so it is better to filter out the Probe Request
  Need to define what information should be included in the Probe Request for filtering
Jae Seung Lee, ETRI

## Slide 7: STA’s preference on AP (1/3)
STA’s preference on AP’s capabilities
  If the STA is a VHT STA, then it may not want to be associated with legacy APs and may only want to be associated with VHT APs or HT APs
  AP may not send Probe Response to the STA if it cannot satisfy the capability preference of the requesting STA
Jae Seung Lee, ETRI
Slide 7

## Slide 8: STA’s preference on AP (2/3)
STA’s preference on Internet Access
  If Internet access is required by the STA, but the AP cannot provide it, then the STA will not request association to the AP
  Better to filter out the Probe Request in this case
Jae Seung Lee, ETRI
Slide 8

## Slide 9: STA’s preference on AP (3/3)
STA’s preference on data confidentiality
  A STA will require data confidentiality if it wants to access services that require privacy such as Internet banking or online shopping
  A STA may not want to use encryption if the privacy is not so important to the service such as streaming service and it requires better throughput
    Such preference information will be helpful for the AP for Probe Request filtering
Jae Seung Lee, ETRI
Slide 9

## Slide 10: STA Capability related information (1/2)
Security Capabilities
  A STA should have certain security capabilities that can satisfy the responding AP’s security policy
    For example, if the requesting STA does not support the Cipher Suite required by the AP, or if the STA is not Management Frame Protection Capable but the AP requires Management Frame Protection, the AP refuses the association request from the AP
    In “10.3.5.3 AP association receipt procedures” in current spec, it is specified “In an RSNA, the AP shall check the values received in the RSNE to see whether the values received match the AP’s security policy. If not, the association shall not be accepted.”
    Better to filter out the Probe Request from such STAs that will not be accepted by AP in association process due to lack of such security capability
Jae Seung Lee, ETRI
Slide 10

## Slide 11: STA Capability related information (2/2)
Supported Credential Types
  A STA should support certain credential types required by the AP or a service provider for authentication
    For example, if the service provider requires USIM for authentication but the STA cannot provide it, it cannot be associated with the AP deployed by the service provider
    It will be beneficial if supported credential type information is included in the Probe Request for filtering
Jae Seung Lee, ETRI
Slide 11

## Slide 12: AP Preference Information in Probe Request
Jae Seung Lee, ETRI
Slide 12
July 2012
Bits: 1 1 1 1 1 1 2
An example of indicating STA’s preference on AP
Indicates STA’s preferences on data confidentiality
Indicates which type of AP the STA wants to be associated with
  Preference on HT AP, or VHT AP, or both, or non-HT, etc.
  For example: 110 means the STA requires HT or VHT AP and does not want non-HT AP
Indicates STA’s requirement on Internet Access
      This bit is set to 1 if the STA requires Internet access
Require Privacy | Require No Privacy | Require HT | Require VHT | Require non-HT | Require Internet Access | Reserved

## Slide 13: Filtering Information in Probe Request
An example of indicating filtering information
Supported Credential Type
    Indicates supported credential types by STAs, such as Pre-Shared Key, X.509 Certificate, Username/Password, USIM, or etc.
STA security capability
    One option is to included RSN IE or just include RSN capabilities field
    Modified or optimized RSN IE can be considered to be used
    Not only security capabilities, but RSN capabilities field also indicate some security requirement such as Management Frame Protection Required (MFPR)
Element ID | Length | AP Preference | Supported Credential Type | STA security capability | Other TBD optional elements
Octets: 1 1 1 1 2 or more TBD
Jae Seung Lee, ETRI
Slide 13

## Slide 14: Conclusion
We proposed the filtering information that should be included in the Probe Request frame
  STA’s preference on AP: Preference on AP’s capabilities, Internet Access, and data confidentiality
  STA Capability related information: STA’s Security Capabilities, and Supported Credential Types
The information will help to filter out the unnecessary Probe Responses, and also help to select appropriate AP to be associated with
Jae Seung Lee, ETRI

## Slide 15
Straw Poll #1
Do you support to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its preferences on association with HT, VHT, or non-HT STA in the Probe Request frame for omission of Probe Response.
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 16
Straw Poll #2
Do you support to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its requirement on internet access in the Probe Request frame for omission of Probe Response.
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 17
Straw Poll #3
Do you support to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its requirement on data confidentiality in the Probe Request frame for omission of Probe Response.
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 18
Straw Poll #4
Do you support to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its security capability information in the Probe Request frame for omission of Probe Response.
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 19
Straw Poll #5
Do you support to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its supported credential types in the Probe Request frame for omission of Probe Response.
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 20
Motion #1
Move to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its preferences on association with HT, VHT, or non-HT STA in the Probe Request frame for omission of Probe Response.
Moved:
Seconded:
Yes No Abstain
Jae Seung Lee, ETRI

## Slide 21
Motion #2
Move to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its requirement on internet access in the Probe Request frame for omission of Probe Response.
Moved:
Seconded:
Yes No Abstain
Jae Seung Lee, ETRI

## Slide 22
Motion #3
Move to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its requirement on data confidentiality in the Probe Request frame for omission of Probe Response.
Moved:
Seconded:
Yes No Abstain
Jae Seung Lee, ETRI

## Slide 23
Motion #4
Move to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its security capability information in the Probe Request frame for omission of Probe Response.
Moved:
Seconded:
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 24
Motion #5
Move to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its supported credential types in the Probe Request frame for omission of Probe Response.
Moved:
Seconded:
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 25
References
Jae Seung Lee, ETRI
11-12/0063r1 Selective transmission of the Probe Response
11-12/0064r0 Text for Selective transmission of the Probe Response
  11-12/265r7 Spec Framework Proposal – Selective transmission of the Probe Response
  11-12/0572r0 Selective transmission of the Probe Response for 11ai Spec Framework
  11-12/0151r8 Specification Framework for TGai