## Slide 1: 11af Interleaver Parameters
Date: 2012-07-16
Authors:

## Slide 2: Introduction
Motions passed in Atlanta define the basic PHY structure for 11af.
Interleaver parameters need to be selected based for the following modes
  2 contiguous and non-contiguous channels
  4 contiguous and non-contiguous channels
Interleaver depth is determined by Ncol
      For 2 segment, Nsd = 216, so potential values for Ncol are: 2, 3, 4, 5, 6, 8, 9, 12, 18, 24, 27, 36, 54, 72, 108
      For 4 segment, Nsd = 432, so potential values for Ncol are: 2, 3, 4, 5, 6, 8, 9, 12, 18, 24, 27, 36, 48, 54, 72, 108, 144, 216
    Nrot is the third permutation applied to spatial streams
      For 2 segment, potential values Nrot = 1:54
      For 4 segment, potential values Nrot = 1:108
    11ac Ncol values are 18 for VHT40 (single segment 11af) and 26 for VHT80. 11ac Nrot values are 29 for VHT40 (single segment 11af) and 58 for VHT80

## Slide 3: Methodology
1000 bytes per packets, 5000 realizations
We consider the following channel models
  802.11n D channel model
  SCM Urban Micro
  SCM Urban Macro
MCS 0, MCS 3, MCS 5 and MCS 7 are simulated.
For each channel model and MCS, the best three Ncol values are found.
The Ncol value that is in best three for most of the time is selected.
The simulations/analysis is repeated for contiguous and non-contiguous two segments and four segments modes
Once Ncol is fixed, repeat the same procedure for finding best Nrot value.
  We considered 2x2 system with Nss=2 and 4x4 system with Nss=4.
Appendix-A gives some exemplary PER results for Ncol
Appendix-B gives some exemplary PER results for Nrot

## Slide 4: Proposed Ncol Values
Simulation outputs
  2-segment Modes
    Best = 27, Second Best = 36, Third Best = 24
  4-segment Modes
    Best = 48, Second Best = 54, Third Best = 36
Based on the results above we proposed to use Ncol=27 for two segment operation and Ncol=48 for four segment operation.

## Slide 5: Proposed Nrot Values
Simulation outputs
  2-Segment Modes
    Best = 46, Second Best = 54, Third Best = 50
  4-Segment Modes
    Best = 78, Second Best = 94, Third Best = 101
Based on the results above we proposed to use Nrot=46 for two segment operation and Nrot=78 for four segment operation.

## Slide 6: Summary
Number of rows and columns in the interleaver:
Parameter | TVHT_MODE_1 | TVHT_MODE_2C TVHT_MODE_2N | TVHT_MODE_4C TVHT_MODE_4N
N_COL | 18 | 27 | 48
N_ROW | 6*N_BPSCS | 8*N_BPSCS | 9*N_BPSCS
N_ROT | 29 | 46 | 78

## Slide 7: Strawpoll - 1
Do you agree to adapt Ncol=27 for two channel operation and Ncol=48 for four channel operation?
  Y:
  N:
  A:

## Slide 8: Strawpoll -2
Do you agree to adapt Nrot=46 for two channel operation and Nrot=78 for four channel operation?
  Y:
  N:
  A:

## Slide 9
APPENDIX A: Ncol Simulations
Example Results
(Only MCS=3 is shown, other MCSs have similar behavior)

## Slide 10
2-Channel Cases

## Slide 15
4-Channel Cases

## Slide 20
APPENDIX B: Nrot Simulations
Example Results
(Only MCS=3 is shown, other MCSs have similar behavior)

## Slide 21: Sample Plot With all Nrot Values