## Slide 1: Access Control Mechanism for FILS
Date: 2012-07-06
Authors:
Name | Affiliations | Address | Phone | email
Fang Xie | China Mobile | Beijing | +86-13910630612 | xiefang@chinamobile.com

## Slide 2: Abstract
This document proposes an access control mechanism for FILS scenario.
Fang Xie

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Background
In FILS scenario, there maybe a lot of mobile stations trying to access to the network simultaneously, if there is no access control, the resources of the 802.11 network would be exhausted and hence all the user experience would be affected.

## Slide 5: Access control in FILS
When AP is overloaded, in beacon or probe response, or…, carry the access control information:
  E.g. access control probability P and access distribution factor M
  After receiving the access control info., STA draws a random number n and compares it with the received probability P
    If n<P, STA will use the new AIFSN (optional ), CWmin & CWmax (optional):
    NAIFSN=M×NAIFSN, NCWmin=2M× (CWmin+1)-1, NCWmax=2M× (CWmax+1)-1
    otherwise, the current AIFSN, CWmin and CWmax will be used
  For example: P=0.3, M=2, current AISFN=2, CWmin=3, CWmax=7:
    For STA A, it draws a random number n=0.2, then new AISFN and CW will be used:
    NAIFSN=2×2=4, NCWmin =22 ×(3+1)-1=15, NCWmax=22× (7+1)-1=31
    For STA B, it draws a random number n=0.7, then the current parameters will be used
  STA can based on the results to determine which AP it wants to associate, and then initiate an access:
    Choose AP with lower AISFN and CW

## Slide 6: Access control in FILS
AP1:CH1
Passive Scan
AP2:CH2
Beacon: probability 0.6, access distribution factor M =4
Beacon: probability 0.3, access distribution factor M =2
Active Scan
STA
AP
Probe Request
Probe Response: probability 0.5, access distribution factor M =3

## Slide 7: Straw Poll 1
Do you support to introduce the access control mechanism into 11ai when a large number of STAs try to access AP simultaneously?
Result
Yes No Abstain_______________

## Slide 8: Straw Poll 2
Do you support to introduce the access control probability and access distribution factor M into 11ai when a large number of STAs try to access AP simultaneously?
Result
Yes No Abstain_______________