## Slide 1: A proposal for next generation security in 802.11 built on changes in 802.11ac
16 July 2012
Authors:
Name | Company | Phone | email
Joe Salowey | Cisco | +1 206 3100596 | jsalowey @cisco.com
Stephen Orr | Cisco | +1 408 8948756 | sorr@cisco.com
Brian Hart | Cisco | +1 408 5253346 | brianh@cisco.com
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com
Dan Harkins | Aruba | +1 408 227 4500 | dharkins at arubanetworks dot com

## Slide 2: LB188 contains comments requesting the inclusion of updated security options in 802.11ac
Comment
Proposed change
11ac does not seem to have a sufficiently rich set of security options to meet Suite-B requirements
Define a sufficient security toolkit for 11ac so that 11ac can meet Suite B requirements, including any transitional measures if required
Number
6198 from Brian Hart (Cisco)
Add support for GCM-256 and Suite B
Adopt the changes specified in document 11-12/0711rX, where X is any revision (currently at zero)
6513 from Dan Harkins (Aruba)
Now at r1

## Slide 3: It is proposed that TGac consider inclusion of “Suite B-like” security features in 802.11ac in Sept
Security mechanisms are evolving due to advances in computing & cryptographic science
802.11 is missing “Suite B–like” security mechanisms that will be required in the near future
802.11ac should include new mechanisms that support “Suite B-like” requirements
The inclusion of features like AES-GCMP will align 802.11ac with mechanisms used by other standards
The integrity of 802.11 & interoperability will be threatened unless the work is undertaken by 802.11
A two step process that defines
  a “transitional” set of mechanisms
  A “Suite B-like” set of mechanisms
Two “minimum Levels of Security” (mLoS) for each step to meet different security needs
The proposed path for approval is discussion until September and consideration for inclusion into D4.0 at the Palm Springs meeting

## Slide 4: Security mechanisms are evolving due to advances in computing & cryptographic science
  Security mechanisms are not static – they evolve over time due to advances in computing and cryptographic science
    e.g. DES was deprecated and replaced by AES
    e.g. SHA-1 will be disallowed by NIST after 2013, MD5 already is disallowed
  The “Suite B” profile defined by the USG NSA defines a consistent set of cryptographic algorithms to provide one of two levels of security
    128-bit: SHA256 for hashing, P256 for key derivation, AES-128 for encryption
    192-bit: SHA384 for hashing, P384 for key derivation, AES-256 for encryption
  Similar profiles are likely be demanded by others in the near future
    Governments, e.g. US, Canadian and other governments are all known to want a higher bar
    Security orgs, e.g. NATO, military
    Industry orgs, e.g. financial services & health

## Slide 5: 802.11 is missing “Suite B–like” security mechanisms that will be required in the near future
MAC
Hash for PRF
HMAC-SHA1, AES-128-CMAC
HMAC-SHA-1 &
SHA-256 (only for 11r)
Encryption
AES-CCMP-128
Feature
IEEE 802.11-2012
AES-128-GMAC for “128” security
AES-256-GMAC for “192” security
HMAC-SHA-256 for “128” security
HMAC-SHA-384 for “192” security
AES-128-GCMP for “128” security
AES-256-GCMP for “192” security
Note: 802.11ad D8.0 only defines the use of AES-128-GCMP, not AES-256-GCMP
What is required for “Suite B-like” security?

## Slide 6: The inclusion of features like AES-GCMP will align 802.11ac with mechanisms used by other standards
IETF RFC 6460
“Suite B Profile for TLS1.2”
IETF RFC 6380
“Suite B Profile for IPSec”
Standard
Defines two minimum Levels of Security (mLoS)
  128 & 192 bit security using AES-GCM
Defines a transitional mechanism using AES-CBC
Defines two minimum Levels of Security (mLoS)
  128 & 192 bit security using AES-GCM
Description
IEEE 802.1AE
“MACsec”
Defines use of AES-GCMP 128 and 256
  Using AES-GCMP 128 and 256
IEEE 802.11ad D8.0
“60GHz”
Defines use of AES-GCMP 128

## Slide 7: The integrity of 802.11 & interoperability will be threatened unless the work is done by 802.11
  The 802.11 WG could decide to not undertake this work
  The “world will not end” because 802.11i based security will still be sufficient for many use cases
  However, increasingly it will not be sufficient in some use cases.
  In these situations there is a risk, if “Suite B like” features are not included in 802.11ac, that:
    Other organisations will attempt to define variants of the 802.11 standard to meet this need … … threating the integrity of the 802.11 standard
    Some companies will define proprietary solutions … … threatening the on-going interoperability of 802.11 based systems

## Slide 8: 802.11ac should include new mechanisms that support “Suite B-like” requirements
Encryption
Feature
AES-128-GCMP
mLOS 128
MAC
AES-128-GMAC
Hash for PRF
SHA256
AES-256-GCMP
mLOS 192
AES-256-GMAC
SHA384
minimum Levels of Security
Cannot “mix & match” features

## Slide 9: A transition to “Suite B-like” requirements should support improved security on older hardware
  Not all hardware in existing APs or clients (802.11a/b/g/n) can support “Suite B-like” requirements …
  … and yet there is a desire to support “better” security in even these devices
  A precedent for this type of support was established in the transition from WEP to TKIP to AES after the “WEP debacle” 
  It is known that some existing hardware can support AES-CCMP-256, and the standard should take advantage of this as part of a transition path

## Slide 10: 802.11ac should include mechanisms that support a transition to “Suite B-like” requirements
Encryption
Feature
AES-128-CCMP
mLOS 128
MAC
AES-128-CMAC
Hash for PRF
SHA-256
AES-256-CCMP
mLOS 192
AES-256-CMAC
SHA384
minimum Levels of Security
Cannot “mix & match” features

## Slide 11: The proposed path forward is discussion until Sept & consideration for inclusion into D4.0 in Palm Springs
D3.0 LB
Brian Hart comments
San Diego
Socialisation of proposal
Teleconferences
Discussion & straw polls
Palm Springs
Motion on inclusion
We are here
Overview of draft changes in 11-12-0946r0 & 11-12-711r1
Let’s select a slot convenient for all interested security folk for discussion