## Slide 1: A proposal for next generation security in 802.11 built on changes in 802.11ac
23 August 2012
Authors:
Name | Company | Phone | email
Joe Salowey | Cisco | +1 206 3100596 | jsalowey @cisco.com
Stephen Orr | Cisco | +1 408 8948756 | sorr@cisco.com
Brian Hart | Cisco | +1 408 5253346 | brianh@cisco.com
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com
Dan Harkins | Aruba | +1 408 227 4500 | dharkins at arubanetworks dot com

## Slide 2: LB188 contains comments requesting the inclusion of updated security options in 802.11ac
Comment
Proposed change
11ac does not seem to have a sufficiently rich set of security options to meet Suite-B requirements
Define a sufficient security toolkit for 11ac so that 11ac can meet Suite B requirements, including any transitional measures if required
Number
6198 from Brian Hart (Cisco)
Add support for GCM-256 and Suite B
Adopt the changes specified in document 11-12/0711rX, where X is any revision (currently at zero)
6513 from Dan Harkins (Aruba)
Now at r1

## Slide 3: It is proposed that TGac consider inclusion of next generation security features in 802.11ac in Sept
Security mechanisms are evolving due to advances in computing & cryptographic science
802.11 is missing next generation security mechanisms that will be required in the near future
802.11ac should include new mechanisms that support next generation requirements
The inclusion of features like AES-GCMP will align 802.11ac with mechanisms used by other standards
The integrity of 802.11 & interoperability will be threatened unless the work is undertaken by 802.11
Two suites of mechanisms
  A set of mechanisms to expedite delivery of strong security to the industry (important for transition)
  A set of mechanisms to align with NSA suite B
The proposed path for approval is discussion until September and consideration for inclusion into D4.0 at the Palm Springs meeting

## Slide 4: Security mechanisms are evolving due to advances in computing & cryptographic science
  Security mechanisms are not static – they evolve over time due to advances in computing and cryptographic science
    e.g. DES was deprecated and replaced by AES
    e.g. SHA-1 will be disallowed by NIST after 2013, MD5 already is disallowed
  The “Suite B” profile defined by the USG NSA defines a consistent set of cryptographic algorithms to provide one of two levels of security
    128-bit: SHA256 for hashing, P256 for key derivation, AES-128 for encryption
    192-bit: SHA384 for hashing, P384 for key derivation, AES-256 for encryption
  Similar profiles are likely be demanded by non-governmental and governmental organizations in the near future
    Governments, e.g. US, Canadian and other governments are all known to want a higher bar
    Security orgs, e.g. NATO, military
    Industry orgs, e.g. financial services & health

## Slide 5: The inclusion of next generation security will align 802.11ac with mechanisms used by other standards
TLS
IPSEC
Standard
AES-CBC-256, AES-CBC-128 (RFC 5246)
AES-GCM-256, AES-GCM-128 (RFC 5288)
AES-CBC-256, AES-CBC-128 (RFC 3602)
AES-GCM-256, AES-GCM-128 (RFC 4106)
Algorithms
IEEE 802.1AE
AES-GCM-256, AES-GCM-128

## Slide 6: 802.11ac should include new mechanisms that support next generation security requirements
Encryption
Algorithm Set
AES-256-CCMP
Transition
MAC
AES-256-CMAC
Hash for PRF
SHA384
AES-256-GCMP
Suite B alignment
AES-256-GMAC
SHA384
AES-128-CCMP
IEEE 802.11-2012
AES-128-CMAC
SHA256
Same mode as 802.11-2012.
Can be enabled on some existing hardware.
Next Generation Security for Industry
  There are efficiency arguments for GCMP at the highest 802.11ac rates

## Slide 7: A transition to next generation requirements should support improved security on older hardware
  Not all hardware in existing APs or clients (802.11a/b/g/n) can support new cipher mode (GCM) requirements …
  … and yet there is a desire to support next generation security in even these devices
  It is known that some existing hardware can support AES-CCMP-256, and the standard should take advantage of this as part of a transition path

## Slide 8: The integrity of 802.11 & interoperability will be threatened unless the work is done by 802.11
  The 802.11 WG could decide to not undertake this work
  The “world will not end” because 802.11i based security will still be sufficient for many use cases
  However, increasingly it will not be sufficient in some use cases.
  In these situations there is a risk, if next generation security features are not included in 802.11ac, that:
    Other organisations will attempt to define variants of the 802.11 standard to meet this need … … threating the integrity of the 802.11 standard
    Some companies will define proprietary solutions … … threatening the on-going interoperability of 802.11 based systems

## Slide 9: The proposed path forward is discussion until Sept & consideration for inclusion into D4.0 in Palm Springs
D3.0 LB
Brian Hart comments
San Diego
Socialisation of proposal
Teleconferences
Discussion & straw polls
Palm Springs
Motion on inclusion
We are here
Overview of draft changes in 11-12-0946r0 & 11-12-711r1
A slot convenient for all interested security folk for discussion
Revise draft based on community input for inclusion in 802.11ac

## Slide 10: Q&A
  A BSS advertises the “Advanced Security” suite but my client HW doesn’t support this suite. What happens?
    This capability is enabled by IT departments with stringent security requirements, so the only devices that support the advanced security capabilities would gain access to the BSS.
    The AP’s physical box may advertise multiple BSSs with different levels of security and access. Your client HW would still have access to a lower security (perhaps guest) SSID for instance.
  Why doesn’t 11-12/0711r1 include support for 11r?
    This is under discussion