## Slide 1: Aggregated Probe Response
Date: 2012-08-30
Authors:

## Slide 2: Abstract
The presentation describes an improvement to the Active Scanning mechanism to reduce the delay on unused channels during the AP discovery phase.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | Yes
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Recap, Active Scanning Procedure
Active scanning procedure is defined in 10.1.4.3.3 and is very effective in certain environments:
  Where coverage is known to be present.
  Where the procedure is user triggered.
  Where the number of scanned channels is not great.
G1
ACK
Probe
Req
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G3
T
T
Probe
Response
Probe
Response
G3
G1
ACK
Min_Probe_Response_Time
Max_Probe_Response_Time
MAC Action message
Time uncertainty <
Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS

## Slide 5: Recap, Active Scanning Procedure
Active scanning procedure is defined in 10.1.4.3.3 and has the following properties:
  Minimum duration of procedure 5msec (STA perspective) per channel.
  Normal length of Probe Req transmission duration aprox. 0.35msec.
  To cover the 2.4Ghz and 5Ghz bands if No Coverage scenario would take:
  Scan Total time = Number channels * Min duration per channel
G1
ACK
Probe
Req
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G3
T
T
Probe
Response
Probe
Response
G3
G1
ACK
Min_Probe_Response_Time
Max_Probe_Response_Time

## Slide 6: Recap, Active Scanning Procedure
How much does it adds up to? :
  Scan Total time = Number channels * Min duration per channel =
  = number channels * (Probe Req + Min_Probe_Response_Time)
  To cover the complete 2.4Ghz and 5Ghz bands in Korea would take a minimum of:
  = (11+25) * (0.05 + 0.35+5) = 194.4msec
  To cover the complete 2.4Ghz and 5Ghz bands in Japan would take a minimum of:
  = (11+12) * (0.05+0.35+5) = 124.2msec
G1
ACK
Probe
Req
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G3
T
T
Probe
Response
Probe
Response
G3
G1
ACK
Min_Probe_Response_Time
Max_Probe_Response_Time

## Slide 7: Recap, Active Scanning Procedure
How much does it adds up to? :
  Scan Total time = Number channels * Min duration per channel =
  = number channels * (Probe Req + Min_Probe_Response_Time)
  To cover the complete 2.4Ghz and 5Ghz bands in Korea would take a minimum of:
  = (11+25) * (0.05 + 0.35+5) = 194.4msec
  To cover the complete 2.4Ghz and 5Ghz bands in Japan would take a minimum of:
  = (11+12) * (0.05+0.35+5) = 124.2msec
G1
ACK
Probe
Req
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G3
T
T
Probe
Response
Probe
Response
G3
G1
ACK
Min_Probe_Response_Time
Max_Probe_Response_Time
Conclusion: Active Scan as is defined today is
not fast enough for the 11ai use case scenario.

## Slide 8: Problem Identified
The scan duration to identify AP coverage where most channels are unused adds up to a substantial delay:
  Use case reference document IEEE 802.11-11/0238 gives multiple scenarios where the complete link setup of <100msec is required with no prior knowledge:
    Scanning and performing Active Scan alone is simply not feasible.
    Neighbor messages transmitted during long interval either beacon or FILS beacon is not good enough on their own – delay too large.
  Use cases requiring complete setup time of 100msec or below:
    3.1.3 Hot-Spot Pass-Through Internet Access
    3.2.2 Traveller Information
    3.2.2 Multi-modal Real-Time Traveller Information
    3.2.2 Dynamic Speed Harmonization

## Slide 9: Problem Identified (con.)
Example of possible 24hr usage:
Night time
Early morning
Day time
Rush hour
Evening
Static
Low/No coverage
High/Low/No coverage
Rural and urban
Urban
High and low mobility
Static/low mobility
Urban
High coverage
High/low mobility
High/Low/No coverage
Low/No coverage
Urban
Static/Low mobility
24hr

## Slide 10: Problem Identified (con.)
Conclusion:
  11ai use cases needs an inherent support for long durations of no/low coverage as well as provide support for efficient and fast discovery of AP coverage over a multiple channels and bands.

## Slide 11: Suggested Improvement
Divide the AP coverage discovery and AP identity discovery to two phases:
  STA attempts AP coverage discovery using a very fast AP discovery phase.
  STA attempts AP identity discovery if AP coverage found.
Enable a shorter listening duration by non AP STA for each channel by:
  Transmitting an APs discovery broadcast message in search for AP coverage.
  AP responds using an ACK after a period of an SIFS.
  STA detects the ACK or if more than one STA responds, detects channel usage using its CCA function. Process completes within 170usec.
  STA than able to perform Active or Passive scanning over the channel to discover the identity of the AP.

## Slide 12: Suggested Improvement
Probe
Response
Multiple APs respond after SIFS and identified by STA’s CCA
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
G1
G3
STA sends a Rapid Scan Request
MAC Action message
Rapid Scan Ack
Probe Response ACK
Time uncertainty < Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
AP coverage discovery
Existing Active Scan procedure – AP identity discovery
~180usec
~5-10msec

## Slide 13: Flavors of Rapid Scan
The Rapid Scan Request message Sep. be:
  A new message either action frame or other – thus much smaller and optimized for its use.
  A Probe Request message (less optimized).
Assumptions:
  Probe Request transmission duration: 350usec
  Rapid Scan Req transmission duration: 100usec.
  Min_Probe_Response_Time: 5msec.
  No AP coverage scenario.
  Number of channels to scan: 35 (Korea), 23 Japan
  Rapid Scan Total time = Number channels * Min duration per channel = (2.4Ghz ch. + 5Ghz ch.) * (Rapid Scan Req + SIFS + ACK duration)
  Korea = (11+25) * (50+100usec+10usec+ 70usec) = 8.28 msec
  Japan = (11+12) * (50+100usec+10usec+70usec) = 5.29 msec

## Slide 14: Key Performance Indicators
Comparing the proposed and existing methods in two aspects:
  Time to discover AP coverage within n channels.
  PWR invested in discovering AP coverage within n channels to directly derive polling rate.
Compared scenarios:
  IDLE channels – no AP coverage on STA geographical vicinity.
  Heavily dense deployment – AP coverage on every 1:4 channels for all bands.
These parameters sets the following limits to actual products:
  The discovery delay when user triggered action is performed.
  The discovery delay when automatic polling method is performed.
  Rate of the discovery attempts due to PWR limitations.

## Slide 15: KPI comparison – Scan Time Idle Channel
  Active Scan Total time w/o Rapid Scan = Number channels * (Probe Req + Min_Probe_Response_Time)
  Active Scan Total time w/ Rapid Scan = Number channels * (Rapid Scan Req + SIFS + ACK)
Chart: 
Active scan delay w/o Rapid [msec] | 5.4 | 10.8 | 16.2 | 21.6 | 27 | 32.4 | 37.8 | 43.2 | 48.6 | 54 | 59.4 | 64.8 | 70.2 | 75.6 | 81 | 86.4 | 91.8 | 97.2 | 102.6 | 108 | 113.4 | 118.8 | 124.2 | 129.6 | 135 | 140.4 | 145.8 | 151.2 | 156.6 | 162 | 167.4 | 172.8 | 178.2 | 183.6 | 189
Active scan delay w/ Rapid [msec] | 0.23067 | 0.46133 | 0.692 | 0.92267 | 1.1533 | 1.384 | 1.6147 | 1.8453 | 2.076 | 2.3067 | 2.5373 | 2.768 | 2.9987 | 3.2293 | 3.46 | 3.6907 | 3.9213 | 4.152 | 4.3827 | 4.6133 | 4.844 | 5.0747 | 5.3053 | 5.536 | 5.7667 | 5.9973 | 6.228 | 6.4587 | 6.6893 | 6.92 | 7.1507 | 7.3813 | 7.612 | 7.8427 | 8.0733

## Slide 16: KPI comparison – Scan Time Idle Channel
  Full scan Korea = 8.30msec full scan w/ Rapid Scan vs. 194.4msec w/o Rapid Scan.
  Full scan Japan = 5.31msec full scan w/ Rapid Scan vs. 124.2msec w/o Rapid Scan.
Chart: 
Active scan delay w/o Rapid [msec] | 5.4 | 10.8 | 16.2 | 21.6 | 27 | 32.4 | 37.8 | 43.2 | 48.6 | 54 | 59.4 | 64.8 | 70.2 | 75.6 | 81 | 86.4 | 91.8 | 97.2 | 102.6 | 108 | 113.4 | 118.8 | 124.2 | 129.6 | 135 | 140.4 | 145.8 | 151.2 | 156.6 | 162 | 167.4 | 172.8 | 178.2 | 183.6 | 189
Active scan delay w/ Rapid [msec] | 0.23067 | 0.46133 | 0.692 | 0.92267 | 1.1533 | 1.384 | 1.6147 | 1.8453 | 2.076 | 2.3067 | 2.5373 | 2.768 | 2.9987 | 3.2293 | 3.46 | 3.6907 | 3.9213 | 4.152 | 4.3827 | 4.6133 | 4.844 | 5.0747 | 5.3053 | 5.536 | 5.7667 | 5.9973 | 6.228 | 6.4587 | 6.6893 | 6.92 | 7.1507 | 7.3813 | 7.612 | 7.8427 | 8.0733

## Slide 17: KPI comparison – Scan PWR Idle Channel
  Active Scan PWR w/o Rapid Scan = Number channels * (Probe Req + Min_Probe_Response_Time)
  Active Scan PWR w/ Rapid Scan = Number channels * (Rapid Scan Req + SIFS + ACK)
Chart: 
Active Scan PWR w/o Rapid [mJ/scan] | 0.3375 | 0.675 | 1.0125 | 1.35 | 1.6875 | 2.025 | 2.3625 | 2.7 | 3.0375 | 3.375 | 3.7125 | 4.05 | 4.3875 | 4.725 | 5.0625 | 5.4 | 5.7375 | 6.075 | 6.4125 | 6.75 | 7.0875 | 7.425 | 7.7625 | 8.1 | 8.4375 | 8.775 | 9.1125 | 9.45 | 9.7875 | 10.125 | 10.4625 | 10.8 | 11.1375 | 11.475 | 11.8125
Active Scan PWR w/ Rapid [mJ/scan] | 0.028534 | 0.057068 | 0.085601 | 0.11414 | 0.14267 | 0.1712 | 0.19974 | 0.22827 | 0.2568 | 0.28534 | 0.31387 | 0.34241 | 0.37094 | 0.39947 | 0.42801 | 0.45654 | 0.48508 | 0.51361 | 0.54214 | 0.57068 | 0.59921 | 0.62774 | 0.65628 | 0.68481 | 0.71335 | 0.74188 | 0.77041 | 0.79895 | 0.82748 | 0.85602 | 0.88455 | 0.91308 | 0.94162 | 0.97015 | 0.99868

## Slide 18: KPI comparison – Scan PWR Idle Channel
  Single full scan Korea = 1.14mJ/scan with Rapid Scan vs. 12.24mJ/full w/o Rapid Scan
Chart: 
Active Scan PWR w/o Rapid [mJ/scan] | 0.34 | 0.68 | 1.02 | 1.36 | 1.7 | 2.04 | 2.38 | 2.72 | 3.06 | 3.4 | 3.74 | 4.08 | 4.42 | 4.76 | 5.1 | 5.44 | 5.78 | 6.12 | 6.46 | 6.8 | 7.14 | 7.48 | 7.82 | 8.16 | 8.5 | 8.84 | 9.18 | 9.52 | 9.86 | 10.2 | 10.54 | 10.88 | 11.22 | 11.56 | 11.9
Active Scan PWR w/ Rapid [mJ/scan] | 0.031533 | 0.063067 | 0.0946 | 0.12613 | 0.15767 | 0.1892 | 0.22073 | 0.25227 | 0.2838 | 0.31533 | 0.34687 | 0.3784 | 0.40993 | 0.44147 | 0.473 | 0.50453 | 0.53607 | 0.5676 | 0.59913 | 0.63067 | 0.6622 | 0.69373 | 0.72527 | 0.7568 | 0.78833 | 0.81987 | 0.8514 | 0.88293 | 0.91447 | 0.946 | 0.97753 | 1.0091 | 1.0406 | 1.0721 | 1.1037

## Slide 19: KPI comparison – dense deployment delay
  Full scan Korea = 91.46msec full Rapid Scan vs. 239.4msec for full Active Scan with APs deployed at every 1 out of 4 channel
Chart: 
Active Scan PWR w/o Rapid [mJ/scan] | 0.34 | 0.68 | 1.02 | 1.61 | 1.95 | 2.29 | 2.63 | 3.22 | 3.56 | 3.9 | 4.24 | 4.83 | 5.17 | 5.51 | 5.85 | 6.44 | 6.78 | 7.12 | 7.46 | 8.05 | 8.39 | 8.73 | 9.07 | 9.66 | 10 | 10.34 | 10.68 | 11.27 | 11.61 | 11.95 | 12.29 | 12.88 | 13.22 | 13.56 | 13.9
Active Scan PWR w/ Rapid [mJ/scan] | 0.031533 | 0.063067 | 0.0946 | 0.68463 | 0.71616 | 0.7477 | 0.77923 | 1.3693 | 1.4008 | 1.4323 | 1.4639 | 2.0539 | 2.0854 | 2.117 | 2.1485 | 2.7385 | 2.7701 | 2.8016 | 2.8331 | 3.4232 | 3.4547 | 3.4862 | 3.5178 | 4.1078 | 4.1393 | 4.1709 | 4.2024 | 4.7924 | 4.824 | 4.8555 | 4.887 | 5.4771 | 5.5086 | 5.5401 | 5.5717

## Slide 20: KPI comparison – dense deployment PWR
  Full scan Korea = 6.16mJ/Scan full Scan w/ Rapid vs. 14.49mJ/Scan w/o Rapid APs deployed at every 1 out of 4 channels
Chart: 
Active Scan PWR w/o Rapid [mJ/scan] | 0.34 | 0.68 | 1.02 | 1.61 | 1.95 | 2.29 | 2.63 | 3.22 | 3.56 | 3.9 | 4.24 | 4.83 | 5.17 | 5.51 | 5.85 | 6.44 | 6.78 | 7.12 | 7.46 | 8.05 | 8.39 | 8.73 | 9.07 | 9.66 | 10 | 10.34 | 10.68 | 11.27 | 11.61 | 11.95 | 12.29 | 12.88 | 13.22 | 13.56 | 13.9
Active Scan PWR w/ Rapid [mJ/scan] | 0.031533 | 0.063067 | 0.0946 | 0.68463 | 0.71616 | 0.7477 | 0.77923 | 1.3693 | 1.4008 | 1.4323 | 1.4639 | 2.0539 | 2.0854 | 2.117 | 2.1485 | 2.7385 | 2.7701 | 2.8016 | 2.8331 | 3.4232 | 3.4547 | 3.4862 | 3.5178 | 4.1078 | 4.1393 | 4.1709 | 4.2024 | 4.7924 | 4.824 | 4.8555 | 4.887 | 5.4771 | 5.5086 | 5.5401 | 5.5717

## Slide 21: Comparison
Advantages:
  Shorter procedure yields substantial shorter delay.
  Separates the 11ai and non 11ai APs enables to focus on the important channels.
  Purpose built AP coverage message is shorter duration and enables higher polling rate without hindering the mobile device power consumption.
  Fully backwards compatible - a combination of legacy and 11ai APs, both APs gain shorter discovery.
  Reduces WM usage on a non 11ai deployments by transmitting shorter message with shorter still reply.
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
Probe
Response
G1
G3
AP coverage discovery
Existing Active Scan procedure – AP identity discovery

## Slide 22: Comparison
Disadvantages:
  Additional procedure adds ~180usec if channel is already pre-known (procedure is optional).
  Adds <1.8% medium usage to an IDLE AP and substantially less to the Tokyo metro station scenario.
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
Probe
Response
G1
G3
AP coverage discovery
Existing Active Scan procedure – AP identity discovery

## Slide 23: Backup

## Slide 24: Motion
Insert the following text on clause 6 of the SFD (11-12/0151r12):
The amendment will define a mechanism to reduces the AP coverage discovery duration using a newly or existing message. The procedure will enable the STA to identify AP coverage within SIFS plus ACK message delay. The mechanism will use the CCA for identifying AP coverage.
Do you agree to make changes to the TGai framework specification as described above.
Yes:
No:
Abstain: