## Slide 1: Enhanced scanning procedure for FILS
Date: 2012-09-03
Authors:

## Slide 2: Abstract
This proposes to reduce the frame length of probe response frame during scanning procedures

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4: Background
Active scanning procedure
  Probe request/response exchanges for finding the AP/network[1]
  Legacy probe response frame includes all system information elements supported by AP
    Size of probe response frame is similar to beacon frame except TIM IE (e.g., more than 240 bytes [2])
  A STA may send the unicast probe request for scanning the preferred /target AP (BSSID of the AP is included in MAC header )
  In case of actively scanning the preferred/target AP, if the STA stores the system information of the AP which the STA was previously associated to, the target AP does not need to send the probe response including full system information elements
Use cases
  Preferred APs (e.g., Home AP, Office AP, preferred shop AP, etc.) may be selected by users or be selected automatically (e.g., based on the association number)

## Slide 5: Proposal (1/2)
For fast initial link setup, the 802.11ai STA will store the system information elements of some preferred APs which the STA was associated with
  To reduce the information to store, the STA may restrict the number of preferred APs
Whenever the AP changes the system parameters, the AP will store the old configuration change count and the changed system information element ID (1byte) for the change count
  E.g.,) In case of the current configuration change count = ‘3’, the stored information by AP. [change count = 0, ID = ‘x’], [change count = 1, ID = ‘y’], [change count = 2, ID = ‘Z’]
  If one parameter is changed in one change count and the change count size is 8 bits, the maximum size of the stored information is 512 bytes

## Slide 6: Proposal (2/2)
During the active scanning procedure to a target AP, a STA may include the configuration change count of target AP in the probe request frame
When AP receives the probe request frame including the configuration change count, the AP may send to the STA the optimized probe response frame including only the system information elements which need to be received by the STA based on the received configuration change count and the current configuration change count

## Slide 7: Analysis (1/2)
Size of Probe response frame is similar to size of full beacon frame except for TIM IE
  The size of beacon frame/probe response[2]
    > 100 byte(typical 802.11 BSS), > 230 bytes (enterprise environment)
    Mandatory fields: Timestamp (8bytes(B)), Beacon Interval (2B), Capability (2B)
The following system information elements can be changed in legacy system [1]
  Channel Switch Announcement (5B)
  Extended Channel Switch Announcement (6B)
  EDCA parameters (20B)
  Quiet element (8B)
  DSSS Parameter Set (3B)
  CF Parameter Set (8B)
  FH Parameter Set (7B)
  HT Operation element (24B)

## Slide 8: Analysis (2/2)
Comparison between legacy probe response size and optimized probe response
  Size of mandatory fields: 12 bytes
  Best case: > 83% (typical BSS), > 92% (enterprise environment)
  Worst case: > 64% (typical BSS), > 84% (enterprise environment)
Updated IE | Legacy probe response (>100B) in typical 802.11BSS |  | Legacy probe response (>230B) in enterprise environment | 
 | Optimized Probe Response | Gain (%) | Optimized Probe Response | Gain (%)
Channel Switch Announcement (5B) | 17 B | > 83% | 17 B | > 92 %
Quiet element (8B) | 20 B | > 80% | 20 B | > 91%
EDCA parameters (20B) | 32 B | > 68% | 32 B | > 86%
HT Operation element (24B) | 36 B | > 64% | 36 B | > 84%

## Slide 9: References
[1] IEEE Std 802.11™-2012
[2] IEEE 802.11-11/1503r2, Short beacon
[3] IEEE 802.11-12/0741r1, Discussions about 802.11ai FILS Discovery Frame (DF) Content Design
[4] IEEE 802.11-12/0151r12, Specification Framework for TGai

## Slide 10: Straw Poll 1
Do you support that for fast initial link setup, the 802.11ai STA may store the system information elements of the APs which the STA was associated with?
  Y:
  N:
  Abstain:

## Slide 11: Straw Poll 2
Do you support that whenever the AP changes the system parameters, the AP may store the old configuration change count and the changed system information element ID corresponding to the configuration change count?
  Y:
  N:
  Abstain:

## Slide 12: Straw Poll 3
Do you support that during the active scanning procedure of target/preferred AP, if the STA has the system information elements of the target AP, the STA may send the probe request frame including the configuration change count of the target AP?
  Y:
  N:
  Abstain:

## Slide 13: Straw Poll 4
Do you support that when AP receives the probe request frame including the configuration change count, the AP may send to the STA the optimized probe response frame including only the system information elements which need to be received by the STA and the current configuration change count?
  Y:
  N:
  Abstain: