## Slide 1: Multi-channel information for AP discovery
Name | Affiliations | Address | Phone | email
Jing-Rong Hsieh | HTC Corp. | 1F, 6-3 Baoqiang Road, Xindian district, New Taipei City, Taiwan |  | jing_hsieh@htc.com
Authors:
Date: 2012-09-06

## Slide 2: Abstract
This contribution introduces further considerations regarding “6.2.4 BSS Information on other channels” in TGai SFD.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Fast Network Discovery (12/0157r12)
6.2.4 BSS Information on other Channels
  802.11ai shall have mechanism to include information of the responding AP and other APs to the Probe Response
Examples of information presented previously
  11/1521r2: Multiband Operation
    List of channel, TBTT timing
  11/1523r4: Multiple Channel Searching
    Load level, BSSID, Anonce
  12/0056r0: Comprehensive probe response
    Information of multiple APs at the same band
    Neighbor list

## Slide 5: BSS Information on other Channels
Existing info such as AP channel Report or Neighbor Report helps STA know the “existence” of other APs in other channels
  However, they may not be superior to the one it just scanned
  PHY info such as signal quality is not conveyable
To reduce unnecessary scans and distribute BSS loading to facilitate FILS, it may help if the “suitability” or “difference” between the scanned ones and the remaining ones is known to the STA
  If the BSS has many properties in common,
  Provide reason for the STA to continue scan for better channel, skip some of the channels, or even stop after obtaining good enough result
    whether the remaining ones are likely to be better or not

## Slide 6: Proposal
In addition to AP Channel Report, AP can attach the loading information of BSSs on other channels in the probe response and beacon for STA’s reference
  A condensed and aggregated loading information
    Use a coarser unit to represent info such as BSS load, BSS Avg access delay, BSS Available Admission Capacity
  A comparison (helpful in ESS case)
    A signed value of condensed loading information;
    A signal bit for a certain information (like a scoreboard)

## Slide 7
Bits: | B0 B7 | B0 B7 | B0 B7 | B0 B7 | B0 B7 | variable | variable |  | variable
 | Element ID | Length | Operating Class | Channel Number | BSS Status Control/Bitmask | BSS Status field #1 | BSS Status field #2 (optional) | … | BSS Status field #n (optional)
Octets: | 1 | 1 | 1 | 1 | 1 | variable | variable |  | variable
Scoreboard (TBD) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BSS Load |  |  | BSS Average Access Delay |  |  |  | BSS Available Admission Capacity |  |  |  |  |  |  |  | Reserved
STA Count | Channel Utilization | Available Admission Capacity | Avg Access Delay for AC_BE | Avg Access Delay for AC_BK | Avg Access Delay for AC_VI | Avg Access Delay for AC_VO | UP 0 | … | UP 7 | AC 0 | AC 1 | … | AC 3 | Reserved | …
TBD | TBD | TBD
BSS load | Admission Capacity | BSS Average Access Delay
TBD | TBD | TBD

## Slide 8: Proposal
STA, by the scan result, can include “STA Channel Report” in Association Request when it has decided to join certain BSS
  Report to the APs with the existence of BSSs on other channels
    BSSs of the same SSID are more viable
  A condensed and aggregated loading information
  A comparison (helpful in ESS case)

## Slide 9: Conclusion
In addition to existence, more information can be provided to reduce unnecessary scan
The information can be a comparison
  For ESSs with common capabilities, most recent information such as loading and access delay
  The notion of Multiple BSSID can be reused (only coding the different part based on a reference)
For scanning STAs obtained this info can decide to continue scanning in the indicated better channels or even stop scanning
  Some of channels remaining in ChannelList of MLME-SCAN.request can be omitted based on
    Existence of BSSs
    Suitability and availability of BSSs

## Slide 10: Straw Poll-1
Do you support the concept to include condensed loading-related information for other channels to reduce unnecessary scan in the probe response, beacon, or FD frame? Yes: No: Abstain:

## Slide 11: Straw Poll-2
Do you support the concept to include performance comparison information between channels to reduce unnecessary scan in the probe response, beacon, or FD frame? Yes: No: Abstain:

## Slide 12: Appendix

## Slide 13: Available information to attach in probe responses/beacons
AP Channel Report (3 to 257 octets)
  Operating Class/Channel
  A list of channels where a STA is likely to find an AP
Neighbor Report (15 to 257)
  BSSID/BSSID Info/Operating Class/Channel/PHY Type/Subelements
  Enable STA to optimize aspects of neighbor service set transition and ESS operation.
Multiple BSSID (3 to 257)
  BSSID Index/DTIM Period/DTIM Count
BSS Load (7)
  Station Count/Channel Utilization/Available Admission Capacity
  May be used by the STA for AP selection algorithm when roaming
BSS Average Access Delay (3)
BSS Access Category Access Delay (6)
BSS Available Admission Capacity (4 to 28)
  Available Admission Capacity Bitmask/Available Admission Capacity List
  Assist STAs in making service set transition decisions
Notes: 47 octets

## Slide 14: 8.3.3.10 Probe Response frame format (12/1053r0)
Table 8-27—Probe Response frame body
Order | Information | Notes
55 | NeighborReport | The NeighborReport is optionally present if dot11FILSActivated is true.

## Slide 15: 6.3.3.3.2 Semantics of the service primitive in 12/1028r1
Neighbor AP Information | Neighbor AP Information field | TBD | The information of neighbor BSSs of the found BSS. This parameter is optional.
MLME-SCAN.confirm(
BSSDescriptionSet,
BSSDescriptionFromMeasurementPilotSet,
BSSDescriptionFromFDSet,
ResultCode,
VendorSpecificInfo
)