## Slide 1: Estimated battery life improvement by TFM2P
Date: 2012-09-17
Authors:
Name | Affiliations | Address | Phone | email
Shusaku Shimada | Yokogawa Electric Co. | 2-9-32 Nakacho Musashinoshi, Tokyo 180-8750 Japan | +81-422-52-5558 | shusaku@ieee.org
Kei Sakaguchi | Osaka University | 2-1 Yamada-oka Suita-shi Osaka, 565-0871 Japan | +81-6-6879-7716 | sakaguchi@comm.eng.osaka-u.ac.jp
Fei Tong | CSR | 4187346 Churchill House, Cambridge Business Park, Cowley Road, Cambridge, CB4 0WZ, United Kingdom |  | Fei.Tong@csr.com
Stefan Aust | NEC Communication Systems, Ltd. | 1753 Shimonumabe, Nakahara-ku, Kawaski, Kanagawa 211-8666 Japan | +81-44-435-1177 | Aust.st@ncos.nec.co.jp
Ken Mori | Panasonic Corp | 1 Kotari-yakemachi, Nagaokakyo, Kyoto 617-8520 Japan |  | Mori.ken1@jp.panasonic.com
Mitsuru Iwaoka | Yokogawa Electric Co. | 2-9-32 Nakacho Musahinoshi, Tokyo 180-8750 Japan | +81-422-52-5558 | Mitsuru.Iwaoka@jp.yokogawa.com

## Slide 2: Abstract
Estimated battery life improvement by reduced wake-up timing margin using TFM2P (Time-Freq. Measurement Mechanism & Procedure) is shown.
For sensor scenarios with long communication interval, an accurate wake-up timing control using TSF of which frequency is compensated by TFM2P, may deserve.

## Slide 3: Previous submission & Sensor usage scenario
AP may provide its TSF timer accuracy information (11-12/130r0 by Seunghee Han, et. al., already in SFD).
Previous submission (11-12/872r1) introduced TFM2P, which is imperative to minimize unnecessary wake-up time margin.
Use case 1 (sensors and meters) suggests various type of battery operated scenarios, where 11ah is going to provide quick communication with very long sleep/hibernating periods.

## Slide 4: Principle tactics of battery life improvement
Wake-up (TSF) time of sensors to synchronize with AP
Schedule for sensor nodes to wake-up
Sleep as long as possible while data can be stored in sensors
Awake as short as possible by communicating quickly
Accuracy of TSF frequency measurement sets the duty ratio including wake-up margin which can be minimized by using TFM2P.
; for small
c.f. Wake-up timing margin △= 40ppm, (20ppm X’tals at each peer)

## Slide 5: Reduction of wake-up timing margin
Wake-up Scheduling and required timing margin;
△=±20@AP ±20@STA=±40ppm;
Wasting battery power , PW(average) ∝ △ ; for deployed sensors PW(worst case) ∝ 2△ ; for possible worst case
(2) TFM2P may improve above wake-up margin, approx. 1/10 reduction.
wake-up timing margin △
due to timer freq. accuracy
TSF master
(AP)
TSF slave
(STA)
wake-up
sleep again
scheduled wake-up time
actual sleep duration
(Communication interval)

## Slide 6: Accurate wake-up by TFM2P
Compensated TSF timer reduces required wake-up margin;
△compensated = 3.5ppm, which is required for residual tolerance.
(2) For instance, △compensated = ±1.5ppm@AP ± 2ppm@STA; Temperature stability of TSF timer and residual tolerance of TFM2P
scheduled wake-up time
less wake-up margin using compensated TSF timer
only for residual tolerance
TSF master
(AP)
TSF slave
(STA)
Wake-up
sleep again
actual sleep duration
(Communication interval)

## Slide 7: Estimated battery life improvement w/t TFM2P An example using Li Coin Cell*
Comm. interval (hour)
Battery condition: Cell capacity ~90mAh, Self discharge ~1% of full capacity/year
Tx Power : 20mW
Tx Data size: 463 octet @ 150kbit/s and 1500 octet @ 3Mbit/s
Data rate : 150kbit/s (MCS0 rep2) and 3Mbit/s (MCS9)
TSF Timer Oscillator supply current : 1uA (continuous)
*note : e.g. Panasonic Li coin cell CR2016
[ Use case 1a,1c,1d,1e/f ]
Portable sensor
which dumps
queued data
a few times a day
Battery
Life
(year)
Chart: 
| 0.1 | 0.2 | 0.5 | 1 | 2 | 3 | 4 | 6 | 8 | 12 | 24 | 36 | 48
(40ppm 150kbit/s) | 1.02 | 1.61 | 2.46 | 2.99 | 3.34 | 3.48 | 3.55 | 3.63 | 3.67 | 3.71 | 3.75 | 3.76 | 3.77
(3.5ppm 150kbit/s) | 1.14 | 1.92 | 3.25 | 4.22 | 4.97 | 5.28 | 5.45 | 5.64 | 5.73 | 5.83 | 5.94 | 5.97 | 5.99
(40ppm/3Mbit/s) | 1.98 | 2.6 | 3.21 | 3.47 | 3.63 | 3.68 | 3.71 | 3.74 | 3.75 | 3.76 | 3.78 | 3.78 | 3.79
(3.5ppm 3Mbit/s) | 2.46 | 3.49 | 4.68 | 5.27 | 5.63 | 5.76 | 5.83 | 5.9 | 5.93 | 5.97 | 6.01 | 6.02 | 6.02

## Slide 8: Estimated battery life improvement w/t TFM2P An example using AAAA ZnMnO2 Cell**
Comm. interval (hour)
Battery condition: Cell capacity ~300mAh, Self discharge ~4% of full capacity/year
Tx Power : 250mW
Tx Data size:@ 250 octet
Data rate : 150kbit/s (MCS0 rep2) and 3Mbit/s (MCS9)
TSF Timer Oscillator supply current : 1uA (continuous)
**note : AAAA ZnMnO2 Cell, of which capacity is depending on discharge current
[ Use case 1a,1c,1d,1h ]
Fixed sensor deployed
in wide area or indoor
which send out
set of data hourly
Chart: 
| 1.6666666666666666E-2 | 3.3333333333333333E-2 | 8.3333333333333329E-2 | 0.16666666666666666 | 0.33333333333333331 | 0.5 | 1 | 1.5 | 2 | 4 | 6
(40ppm 150kbit/s) | 0.33 | 0.64 | 1.44 | 2.46 | 3.83 | 4.7 | 6.08 | 6.74 | 7.13 | 7.8 | 8.05
(3.5ppm 150kbit/s) | 0.33 | 0.65 | 1.5 | 2.65 | 4.31 | 5.45 | 7.41 | 8.41 | 9.02 | 10.1 | 10.6
(40ppm 3Mbit/s) | 1.16 | 2.04 | 3.76 | 5.24 | 6.52 | 7.09 | 7.78 | 8.04 | 8.18 | 8.39 | 8.46
(3.5ppm 3Mbit/s) | 1.2 | 2.17 | 4.23 | 6.19 | 8.06 | 8.96 | 10.1 | 10.5 | 10.8 | 11.1 | 11.3
Battery
Life
(year)

## Slide 9: Estimated battery life improvement w/t TFM2P An example using Li Button Cell***
Comm. interval (hour)
Battery
Life
(day)
Battery condition: Cell capacity ~35mAh, Self discharge ~1% of full capacity/year
Tx Power : 1mW
Tx Data size:@ 16 octet
Data rate : 150kbit/s (MCS0 rep2) and 3Mbit/s (MCS9)
TSF Timer Oscillator supply current : 1uA (continuous)
***note : e.g. Panasonic Li button Cell BR1220
[ Use case 1c,1d,1e/f, 1h ]
Temporal sensor
which send out
a raw or stored data
several times an hour
Chart: 
| 3.3333333333333335E-3 | 8.3333333333333332E-3 | 1.6666666666666666E-2 | 3.3333333333333333E-2 | 0.05 | 8.3333333333333329E-2 | 0.16666666666666666 | 0.25 | 0.5 | 1 | 2
(40ppm 150kbit/s) | 51.2 | 112 | 187 | 279 | 334 | 397 | 461 | 488 | 518 | 534 | 543
(3.5ppm 150kbit/s) | 53.1 | 122 | 214 | 345 | 434 | 546 | 677 | 736 | 806 | 847 | 868
(40ppm 3Mbit/s) | 69.5 | 146 | 231 | 326 | 377 | 432 | 484 | 505 | 527 | 539 | 545
(3.5ppm 3Mbit/s) | 73 | 162 | 275 | 420 | 510 | 615 | 728 | 775 | 829 | 859 | 875

## Slide 10: Frequency Measurement Mechanism
            dot11MgmtOptionFrequencyMsmtActivated (New)
t1=ToD(M1)
t4=ToA(Ack)
t5=ToD(M2)
t8=ToA(Ack)
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2=ToA(M1)
t3=ToD(M1)
t6=ToA(M1)
t7=ToD(M1)
t1and t4 are known
t5and t8 are known
offset1=[(t2-t1)-(t4-t3)]/2
offset2=[(t6-t5)-(t8-t7)]/2
Sending STA(f1)
Receiving STA(f2)
f1= 1/k(t5-t1)
f2= 1/k(t6-t2)
PHY assisted time-stamp may help.
Properly apart two time measurements may result substantially
different results as shown.

## Slide 11: Prerequisite for Procedure: An stability example of tuning fork crystal
ºC (Degree Centigrade )
Frequency
Deviation
(ppm)
X’tal frequency accuracy : ±20ppm
Sensor node (TSF Slave) : 3.5ppm @ 25±10 ºC -0.035 ppm / (change in ºC)2 max parabolic curve
AP (TSF Master): Temperature stabilized timer may be used
1.5ppm for -10 ~ 60 ºC
Information exchange
(before performing FM2 )
- Stability (My side) and/or
- Achievable minimum
tolerance (your side)

## Slide 12: Open issue: Procedure (1)
AP may advertise possible worst accuracy before TFM2P
  Worst TSF accuracy (11-12/0130r0; already in SFD)
In addition, AP may advertise best tolerance by TFM2P
  Achievable minimum tolerance and/or TSF timer stability (to be used for TFM2P interval calculation) as well.
STA may inform its own residual tolerance to AP after compensation performed, if requested.
Either STA or AP select appropriate TFM2P scheme;
  Initiates explicit TFM2P handshake with specific interval between two time measurements by STA if needed.
  perform implicit TFM2P at every wake-up time as well.

## Slide 13: Open issue: Procedure (2)
AP may collect information below;
  STA’s TSF frequency tolerance
  STA’s TSF timer stability
AP may broadcast information below to all STAs;
  TSF frequency tolerance of worst STA
  TSF timer stability of worst STA

## Slide 14: Straw Poll (1)
Do you agree that the enhanced power saving mechanism of 11ah should provide any frequency measurement procedure of TSF timer to improve the battery life?
  Yes
  No
  Abstain

## Slide 15: Straw Poll (2)
Do you agree to explore more on TFM2P (Time-Freq. Measurement Mechanism & Procedure) in slide 10 to be included finally in SFD of 11ah?
  Yes
  No
  Abstain

## Slide 16: References
[1] 11-12/130r0 “beacon reception of long sleeper”
[2] IEEE802.11 -2012 Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications
[3] 11-12/0872r1 “time frequency measurement mechanism and procedure”