## Slide 1: 1MHz SIG Field Discussions
Date: 2012-09-17
Authors:

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:

## Slide 4: Current 1MHz SIG Field in SFD
SIG Field | Bits | Comments
STBC | 1 | Same as in 11ac
Num SS | 2 | Number of spatial streams for SU
SGI | 1 | Short Guard Interval
Coding | 2 | 1st bit is coding type (LDPC/BCC), 2nd bit is for LDPC Nsym ambiguity
MCS | 4 | MCS
Aggregation bit | 1 | Signals use of AMPDU
Length | 9 | Length field (in symbols when aggregation is ON, is in bytes when aggregation is OFF, Mandate AMPDU for packet sizes > 511 bytes
ACK Indication | 2 | 00: Ack; 01: BA; 10: No Ack; 11: a frame not ACK, BA or CTS
Reserved | 4 (TBD) | Some possible uses are MAC bits or any other new features etc. Details TBD
CRC | 4 | 4 bits of CRC should be enough
Tail | 6 | 
Total | 36 | 

## Slide 5: Proposal-1: SM Signaling in SIG
Two terms are defined for spatial multiplexing (SM) signaling in SFD
  NSS: number of spatial streams
  NSTS: number of space-time streams
Maximum of the number of space-time streams (NSTS) shall be less than or equal to 4.
NSS | NSTS | STBC
1 | 1 | 0
2 | 2 | 0
3 | 3 | 0
4 | 4 | 0
NSS | NSTS | STBC
1 | 2 | 1
2 | 4 | 1

## Slide 6: Motivation
Observation on the current SFD:
For 1MHz: NSS (2 bits) is used in the SIG field (maximum of space-time streams = 4).
For ≥ 2MHz: it follows 11ac with NSTS (2 bits) in the SIGA field (maximum of space-time streams = 4).
Remark:
Inconsistency in spatial multiplexing signaling for 1MHz and ≥ 2MHz.
If NSTS is adopted for ≥ 2MHz based on 11ac spec, 1MHz should use the same signaling NSTS

## Slide 7: Proposed Change on the SM Signaling
Adopt NSTS instead of NSS for the spatial multiplexing signaling in 1MHz SIG field to make it consistent with >=2MHz and 11ac.

## Slide 8: Proposal—2: Add Smoothing Bit
Unify with the convention of 11n/11ac, and also 2MHz short and long (SU/MU modes) SIG(A) fields.
  >=2MHz SIG(A) field has smoothing or beam-change bit.
  Receiver has the same channel smoothing check as in >=2MHz preambles.
Possible that NDP and feedback were in >=2MHz, but the steered packets rate dropped to 1MHz rates.
  Similar to 40/20 scenario in 11n, or 80/40/20 scenario in 11ac.

## Slide 9: Proposal—3: MCS
We never decided which MCS index is used for MCS0-Rep2 in 1MHz.
Propose to use MCS10:
  MCS0~9, same constellation sizes and coding rates as defined in 11ac
  MCS10, BPSK, rate ½, and 2x repetition
  Similar to the convention in 11n, i.e. MCS32

## Slide 10: Straw Poll 1
Do you agree to change NumSS field to NumSTS field in the 1MHz SIG field, which indicates number of space time streams for SU ?

## Slide 11: Straw Poll 2
Do you agree to add one smoothing bit in the 1MHz SIG field?

## Slide 12: Straw Poll 3
Do you agree to define 1MHz MCS field as below:
  MCS0~9, same constellation sizes and coding rates as defined in 11ac
  MCS10, BPSK, rate ½, and 2x repetition