## Slide 1: Frame Classification Based on MAC Header Content
Date: 2012-09-13
Authors:

## Slide 2
Simone Merlin | Qualcomm | 5775 Morehouse Dr, San Diego, CA | 8588451243 | smerlin@qualcomm.com
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com
Alfred Asterjadhi | Qualcomm |  |  | 
Amin Jafarian | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Minho Cheong | ETRI | 138 Gajeongno, Yuseong-gu, Dajeon, Korea | +82 42 860 5635 | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Hyoungjin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Heejung Yu | ETRI |  |  | heejung@etri.re.kr
Jaewoo Park | ETRI |  |  | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  |  | Sk-lee@etri.re.kr
Sayantan Choudhury | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Chittabrata Ghosh | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 

## Slide 3
Name | Affiliations | Address | Phone | email
Shoukang Zheng | I2R | 1 Fusionopolis Way, #21-01 Connexis Tower, Singapore 138632 | +65-6408 2000 | skzheng@i2r.a-star.edu.sg
Haiguang Wang | I2R |  |  | hwang@i2r.a-star.edu.sg
Wai Leong Yeow | I2R |  |  | wlyeow@i2r.a-star.edu.sg
Zander Lei | I2R |  |  | leizd@i2r.a-star.edu.sg
Jaya Shankar | I2R |  |  | jshankar@i2r.a-star.edu.sg
Anh Tuan Hoang | I2R |  |  | athoang@i2r.a-star.edu.sg
Joseph Teo Chee Ming | I2R |  |  | cmteo@i2r.a-star.edu.sg
George Calcev | Huawei | Rolling Meadows, IL USA |  | George.Calcev@huawei.com
Osama Aboul Magd | Huawei |  |  | Osama.AboulMagd@huawei.com
Young Hoon | Huawei |  |  | Younghoon.Kwon@huawei.com
Betty Zhao | Huawei |  |  | Betty.Zhao@huawei.com
David Yangxun | Huawei |  |  | David.Yangxun@huawei.com
Bin Zhen | Huawei |  |  | ZhenBin@huawei.com
ChaoChun Wang | MediaTek |  |  | chaochun.wang@mediatek.com
James Wang | MediaTek |  |  | james.wang@mediatek.com
Jianhan Liu | MediaTek |  |  | jianhan.liu@mediatek.com
Vish Ponnampalam | MediaTek |  |  | vish.ponnampalam@mediatek.com
James Yee | MediaTek |  |  | james.yee@mediatek.com
Thomas Pare | MediaTek |  |  | thomas.pare@mediatek.com
Kiran Uln | MediaTek |  |  | kiran.uln@mediatek.com

## Slide 4: Overview
To improve the power save performance, a STA can request to establish a traffic classification and filtering agreement with a peer STA (e.g., AP-STA) so that the initiating STA only receives the traffic that matches the classification parameters.
IEEE Std 802.11-2012 [1] specifies a mechanism to classify and subsequently filter frames based on a frame’s MAC Payload content. However, classification cannot be performed based on the MAC Header content of the frames being processed.
In this submission, we introduce a mechanism to enable frame classification based on the MAC Header content of the frames being processed.

## Slide 5: Current Frame Classification Mechanism (1)
In [1], the TCLAS IE contains the classification parameters, and a TLCAS element is included in a management frame (i.e., TFS Request frame), which is used to establish a classification agreement between a non-AP STA and an AP-STA, as illustrated on slide~4--7.
[1] enables the classification and subsequent filtering of only Data frames, but not other frame types.

## Slide 6: Current Frame Classification Mechanism (2)
Element ID
Length
TFS ID
TFS Action Code
Subelement ID
Length
TCLAS Element(s)
Fig.2: TFS Request element format in [1]
Fig.3: TFS Subelement format in [1]
TFS Request Subelement(s)
One or more TFS Request Subelements
TCLAS Processing Element (optional)
Variable
1
1
0 or 3
Octets:
One or more TCLAS elements
Category
Action
Dialog Token
Fig.1: TFS Request frame body format in [1]
TFS Request Element
Variable
1
1
1
Octets:
1
1
1
1
Variable
One or more TFS Request elements

## Slide 7: Current Frame Classification Mechanism (3)
Classifier Type | Classifier Parameters
0 | Ethernet parameters
1 | TCP/UDP IP parameters
2 | IEEE 802.1Q parameters
3 | Filter Offset parameters
4 | IP and higher layer parameters
5 | IEEE 802.1D/Q parameters
6-255 | Reserved
Table 1 -- Frame classifier type in [1]
Element ID
Length
User Priority
Frame Classifier
Classifier Type
Classifier Mask
Classifier Parameters
Fig.4: TCLAS element format in [1]
Fig. 5: Frame Classifier field in [1]
Octets:
1
1
1
Variable
Octets:
1
1
1 - 252

## Slide 8: Current Frame Classification Mechanism (4)
As an example, the Frame Classifier subfield of Classifier Type 4 for traffic over IPv6 (included in TCLAS IE) is shown in Fig. 6.
Classifier Type (4)
Classifier Mask
Source IP Address
Destination IP Address
Octets:
1
1
1
16
Version (6)
16
Source Port
Destination Port
Next Header
Flow Label
Octets:
2
2
1
3
DSCP
1
Fig.6: Frame Classifier subfield of Classifier Type 4 for traffic over IPv6 in [1]

## Slide 9: Current Frame Classification Mechanism (5)
Element ID
Length
Processing
Octets:
1
1
1
Fig.7: TCLAS Processing element format in [1]
Processing subfield value | Meaning
0 | Incoming MSDU’s higher layer parameters have to match to the parameters in all the associated TCLAS elements.
1 | Incoming MSDU’s higher layer parameters have to match to at least one of the associated TCLAS elements.
2 | Incoming MSDUs that do not belong to any other TS are classified to the TS for which this TCLAS processing elements is used. In this case, there are not any associated TCLAS elements.
3-255 | Reserved
Table 2 – Encoding of Processing subfield in [1]

## Slide 10: Classification Based on MAC Header Content (1)
Frame Classification based on the MAC Header content is needed to enable:
  Classification of Management frames, Control frames, or Extension frames.
  Classification of frames based on the information (e.g., address1, address 2) in the MAC Header.
New Classifier Type(s) for the TCLAS IE are needed to contain classification parameters that are based on the MAC Header content;
  Table 3 illustrates a revised table containing the frame classifier types.
  An example of new classifier type is given in Fig. 8.

## Slide 11: Classification Based on MAC Header Content (2)
Classifier Type | Classifier Parameters
0 | Ethernet parameters
1 | TCP/UDP IP parameters
2 | IEEE 802.1Q parameters
3 | Filter Offset parameters
4 | IP and higher layer parameters
5 | IEEE 802.1D/Q parameters
6 | IEEE 802.11 MAC parameters (new)
7-255 | Reserved
Table 3 – Revised frame classifier types
Note: one or more new Classifier Types can be defined for various types of classification.

## Slide 12: New Frame Classifier Based on MAC Header Content- An example
Classifier Type
(New index number)
Classifier Mask
(B0-B6 used, B7 reserved)
Address1
Match Specification
Fig.8: New Frame Classifier field of the TCLAS element format – an example
Frame Control Match Specification
Address2 Match Specification
Address3 Match Specification
Address4 Match Specification
QoS Control Match Specification
HT Match Specification
Octets
1
1
1 or 2 or other value
6
6
6
6
2
4
Type Match Spec
ToDS Match Spec
Frame Control Filter Mask
Fig.8-1: Frame Control Match Specification subfield format – an example
FromDS Match Spec
B0
Subtype Match Spec
B1
B2
B5
B6
B7
B8
B15
Bits:
B11
B12
Reserved
Containing match specifications for one or more subfields of Frame Control field of MAC Header
value of Classifier Type determines which fields are present
Decides which match specifications need to be compared

## Slide 13: Classification Based on MAC Header Content (3)
The User Priority field of the TCLAS IE and the TCLAS Processing element need to be revised to accommodate the MAC Header content based classification.
  E.g. reserved and ignored for MGMT and Extension
MAC Header content based frame classification can either be performed separately or be performed together with the existing MAC Payload content based classification.
  For example, a TFS subelement can include multiple TCLAS elements, each containing classification parameters based on either the MAC Header content or the MAC Payload content.
  A TCLAS element can also possibly contain a new Frame Classifier Type which includes classification parameters based on both the MAC Header and MAC Payload contents.
In addition to traffic filtering, other special processing can potentially be performed on the matched frames.

## Slide 14: Straw Polls
Straw Poll~1: “Do you agree to add to the 802.11ah spec a frame classification mechanism to enable classification and the subsequent processing (e.g., filtering) based on the MAC Header content?”

## Slide 15: Reference
[1] IEEE Std 802.11-2012, IEEE Standard for Information Technology – Telecommunications and information exchange between systems, local and metropolitan area networks – Specific requirements, Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications