## Slide 1: 4-bit CRC Revisited
Date: 2012-09-17
Authors:

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:

## Slide 4: Introduction
Current 4-bit CRC calculation has Hamming distance=1, as pointed out in [1]
  Randomly pick values of 26 bits prior to “CRC” in 1 MHz SIG
  2nd sequence: Pick 1 of those 26 bits and flip it
  11.5% chance that both sequences have same CRC field using current algorithm – 4 LSB bits of 8-bit CRC.
Many options for picking this calculation that has Hamming distance=2
  7 options for picking different selection of 4 bits from 8-bit CRC calc
  Use 4-bit polynomial: x4 + x + 1
  Many other possibilities
Tom Tetzlaff, et. al.

## Slide 5: Performance Implications
As pointed out in [2], the algorithm choice for the Check Sequence has little performance impact in AWGN case
  At high error levels, all “sane” Check Sequence algorithms will trend towards a 6.25% false-positive rate on SIG fields with errors. (Assumes 4b Check Sequence, 1/16 = 6.25%)
  At low error levels, false-positive rate differences only can affect the low percentage of SIG fields with errors, most SIG fields are correct.
Tom Tetzlaff, et. al.

## Slide 6: Viterbi Decoder AWGN behavior
Viterbi Decoder output tends to have multi-bit errors
Distribution of number of errors in a 30-bit sequence (1 MHz SIG) with AWGN such that the PER is 0.15%:
Chart: Error Counts per Packet with Error
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19+
Number of Bit Errors | 0.06525 | 0.1288 | 0.25134 | 0.16005 | 0.1182 | 0.10994 | 0.053615 | 0.037765 | 0.027808 | 0.016108 | 0.01056 | 0.0075917 | 0.0045163 | 0.003269 | 0.0022367 | 0.0014839 | 0.00081724 | 0.00038711 | 0.00025808
Tom Tetzlaff, et. al.
Notes: This is a graph of only those packets that have errors. So, the total of the bars is 100%. The packet is just the 30-bit SIG field, plus 6 tail bits. (Errors in tail bits are not considered to be packet errors.)

## Slide 7: Catching Single-bit Errors
Why choose Hamming distance = 2?
  It is exceptionally easy to do. The complexity difference between a check sequence algorithm that has this property and one that does not is negligible.
  There might be some relatively common set of channel conditions, equalizer implementations, and Viterbi Decoder implementations that significantly increase the likelihood of single bit errors
  Instead of trying to cover all possible scenarios, simply pick a Check Sequence algorithm that has a Hamming distance = 2.
Tom Tetzlaff, et. al.

## Slide 8: False Check Sequence Match for Given Algorithms
Algorithms Checked:
  4 LSBs of 8-bit CRC (currently in SFD)
  4-bit CRC using x4 + x + 1 Generator
  Best performer of selecting 4 bits of 8-bit CRC such that all single-bit errors are detected
  Concatenation of 4 parity bits using every 4th input bit at offsets of 0,1,2 and 3.
Also checked various combinations of XOR of 4 selected bits of 8-bit CRC with remaining 4 bits of 8-bit CRC
  Dropped due to poor performance
Tom Tetzlaff, et. al.

## Slide 9: False Positive Check Sequences for AWGN
Chart: False Positive Percentage
| LSB | bits 1467 | 4x 1b CRC | 4b CRC
PER=3.4% | 4.61 | 4.27 | 4.11 | 3.45
PER=.15% | 3.74 | 2.77 | 2.75 | 2.22
Packet is 26 random data bits + 4 CRC + 6 tail bits = same size as 1 MHz SIG
“LSB” is current spec – 4 LSB of 8-bit CRC calculation
4b CRC uses x4+x+1 generator polynomial
Tom Tetzlaff, et. al.
Notes: The False positive percentage is percentage of packets that have a good Check Sequence out of the packets that have errors. False positive will approach 6.25% as noise increases, since it is 4 bits long.

## Slide 10: Recommendations
Use a Check Sequence calculation that has a Hamming distance > 1, to guarantee catching single-bit errors
  Even if performance difference is small
Complexity is sufficiently low, that using a 4-bit CRC using x4 + x + 1 as the generator is the desired choice.
  2 2-input MUXs and 1 2-input XOR inserted into 8-bit CRC circuit
Tom Tetzlaff, et. al.

## Slide 11: Current SFD text
R.3.2.1.C: The draft specification shall use the 4 LSB of the 11n HTSIG field 8-bit CRC for the 4-bit CRC in 11ah 2MHz and 1MHz SIG(A) fields, and use the same 11n HTSIG field 8-bit CRC in SIGB field of the >=2MHz long preamble [36, 39].
Proposal on next page is to change the 4-bit CRC field to use a normal 4-bit CRC procedure using the x4 + x + 1 generator polynomial
Tom Tetzlaff, et. al.

## Slide 12: Straw Poll
Do you agree that the 4-bit CRC calculation should change as follows:
The 4-bit CRC in 11ah 2MHz and 1MHz SIG(A) fields will be calculated using the same procedure as the 11n HTSIG field 8-bit CRC, except that the generator polynomial G(D) = D4 + D + 1. The draft specification shall use the same 11n HTSIG field 8-bit CRC in SIGB field of the >= 2MHz long preamble.
Tom Tetzlaff, et. al.

## Slide 13: References
[1] 11-12-0800-01-00ah-4-bit-crc-for-1-mhz-and-2-mhz-modes.ppt
IEEE 11-12/0800r1, InterDigital
[2] 11-12-0596-01-00ah-sig-field-4-bit-crc.pptx
IEEE 11-12/0596r1
Tom Tetzlaff, et. al.