## Slide 1: Reserve Channel List in 802.11ah
Date: 2012-09-17
Authors:

## Slide 2: Abstract
This presentation further discusses the channel switch in 802.11ah Sensor / Smart Meter use cases
  Continuation of the submission 12/878r0 (on-channel-switching-in-11ah)
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 3: Introduction
Agreed channelization in the 11ah Specification Framework
  26 1MHz channels, 13 2MHz channels
Current operating channel may become unusable due to sudden interference and AP may need change the operating channel without being able to reach all the STAs
With large number of available channels a STA may have uncertainty of the AP’s new operating channel
  Excessive scanning may consume relatively big amount of energy

## Slide 4: Concept of Reserve Channel List
AP maintains a list of potential operating channels
  AP will try to first to deploy itself to these channels if the current operating channel cannot support the required operation quality
  AP indicates the preferred channels to STAs
If STAs lose the connection to the AP and no more detect its presence on the current channel they are able to scan specific set of channels

## Slide 5: AP Channel Selection
AP may perform periodic channels scans to find good back up channel candidates
AP may also use blind channel selection
  E.g. indicate that every third channel would be the 1st alternatives
In practice it would be up to implementation how the AP selects the reserve channels

## Slide 6: Indicating the Channel List
Channel list is maintained and signaled by AP
Reserve List could be signaled in the association phase
Updates could be broadcasted e.g. in a full beacon
  Update period could be several full beacon intervals
  Unicast delivery could be considered if needed.

## Slide 7: Channel Scanning Priority
AP may list multiple channels in the reserve list
It can be agreed that e.g. the priority order which to scan the channels is implicit:
  First channel in the list has highest priority
  Next one has the second highest etc..
Both AP and STA have common understanding of the channel priority order
  AP tries to deploy first to the highest priority channel
  This is also the first channel that the STA scans

## Slide 8: Conclusions
In a worst case situation without any assistant information a STA may need to scan e.g. all the 1 Mhz (excluding the current one) channels in order to re-connect with the AP
AP may choose the reserve channels
  Blindly: select specific set of channels
  Utilize active selection mechanism (e.g. background scanning) to scan suitable channels
Priority order for the channels can be defined to speed up the scanning
Even if the Reserve Channel List is not fully up to date there are no significant negative effects

## Slide 9: Motion 1
Do you support to include the concept of “AP maintaining a Reserve Channel List to enhance connectivity and reduce the channel scanning time of the STAs in case of sudden channel switch (message formats/details TBD)” in the specification framework
Y:
N:
A: