## Slide 1: Active Polling
Date: 2012-09-17
Authors:

## Slide 4: Current 802.11 PS STA operations
A PS STA can wake up periodically before beacons to check possible DL data from AP
For pending UL data, a PS STA can wake up and send the data immediately as the medium access allows

## Slide 5: Clock drift over long sleeping period
ppm | 1us | 1ms | 1s | 1m | 1h | 1d
1 | 1.00E-06 | 0.001 | 1 | 60 | 3600 | 86400
5 | 5.00E-06 | 0.005 | 5 | 300 | 18000 | 432000
10 | 1.00E-05 | 0.01 | 10 | 600 | 36000 | 864000
20 | 2.00E-05 | 0.02 | 20 | 1200 | 72000 | 1728000
40 | 4.00E-05 | 0.04 | 40 | 2400 | 144000 | 3456000
Clock drift (us)
In order to capture a desired beacon, a PS STA needs to wake up far in advance after a long sleep to avoid possible clock drift

## Slide 6: Passive checking vs. active polling
Active polling mode allows a low-power STA to poll AP immediately after waking up for information, instead of keeping awake for a long period to track beacons
Passive checking
Active polling

## Slide 7: Active polling types
Scheduled active polling (refer to 11-12-0823-00-00ah-targetwaketime)
  AP schedules STAs’ wakeup times
  STAs wake up at scheduled times for UL/DL transmissions
  STAs need not track beacons
Unscheduled active polling (refer to 11-12-0831-00-00ah-uplink-channel-access-general-procedure)
  AP may allow a STA/group-of-STA to transmit an uplink frame anytime upon waking up
  STAs need not track beacons

## Slide 8: Active polling information
Without tracking beacons, an active polling STA may miss the following information
  Updated information elements in beacons
  Timestamp – esp. useful to scheduled active polling STAs
It is desired that an active polling STA can request the AP to provide the above information upon waking up
AP can provide the requested information immediately or suggest the STA to check next beacon for the requested information
  AP can provide a timer toward next beacon (refer to11-12-0409-06-00ah-supporting-low-power-operation)

## Slide 9: Straw poll / Pre-motion 1
Do you support to include in SFD that:
  An active polling STA can solicit the BSS change sequence (one byte) from an AP upon waking up.
  AP may provide the information immediately or suggest the STA to check beacons.

## Slide 10: Straw poll / Pre-motion 2
Do you support to include in SFD that:
  An active polling STA can solicit the current timestamp from an AP upon waking up
  AP may provide the information immediately or suggest the STA to check beacons