## Slide 1: Sectorized beam Operation
Date: 2012-09-17
Authors:

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:

## Slide 4: Objectives
This proposal presents some enhancement to the sectorized beam operation
The objective is to provide a simple mechanism for
  Reduce OBSS interference
  Increase spatial re-use of the wireless medium

## Slide 5: Sectorized Beam Operation
Sectorized beam/antenna operation are generally used in outdoor wide area network to provide spatial re-use.
It is very effective in reducing OBSS interference (as was proven successfully in the cellular system)
  Transmit EIRP into OBSSs is significantly reduced.
  Reduced OBSS interference with the sectorized receive beam
Hidden nodes within the same BSS is reduced because the sectorized beam reduces the number of active nodes during a specific sector (Ref 1, Huawei)
Assume only AP use sectroized beam in the presentation
Ref 1: 11-12-0852-00-00ah Sectorization for Hidden Node Mitigation

## Slide 6: Benefits of the Sectorized Beam Operation
Sectorized Beam transmission reduces interference to the neighboring AP and stations
Sectorized Beam reception reduces interference from the neighboring AP
Allow higher spatial re-use of the medium
BSS1
BSS2
Reduced
Interference
to adjacent BSS
via Sectorized
Beam Transmission
AP1
AP2
Sectorized
Beam
STA1
STA2
Reduced
Interference
from adjacent BSS
via Sectorized
Beam Reception

## Slide 7: Transmit Sectorized Beam
AP can maintain or increase the peak transmit EIRP in the sector beam direction (vs omni-direction).
If the sectorized pattern is formed using multiple omni-directional antennas, the OBSS interference can be reduced
  > 3 dB if 2 antennas are used
  > 5 dB if 3 antennas are used
  > 6 dB if 4 antennas are used
Omni Pattern
Sectorized Pattern (wider beam)
Sectorized Pattern (Narrower Beam)
OBSS Interference is achieved statistically without requiring coordination between OBSS

## Slide 8: Receiving with Sectorized Beam
Channel access by AP is highly affected if OBSS interference is high due to high probability of OBSS interference
With the sectorized receive beam the OBSS interference is reduced greatly due to narrower beamwidth.
Omni Pattern
Sectorized Pattern (wider beam)
Sectorized Pattern (Narrower Beam)

## Slide 9: Sectorization for hidden node reduction (Huawei’s proposal 11-12-0852-00-00ah)
AP divides the space in multiple sectors and use a TDM approach to allow STA transmissions in one sector at the time
Stations are allowed to transmit and receive data only in the time interval corresponding with their sector (called as Sector Interval in the drawing)
Some time interval can be left for channel access of all sectors at the same time
Example of channel access:
Beacon
Sector 1
Access STAs in Sector 1
Beacon
Sector 2
Access STAs in sector 2
Beacon
Sector 3
Access STAs in sector 3
Omni
Beacon
Access all STAs in the BSS
Sector Interval 1
Sector Interval 2
Sector Interval 3
BSS Interval

## Slide 10: Sectorization for hidden node reduction (Huawei’s proposal 11-12-0852-00-00ah )
Open Issues
  TIM group should match the best (AP) sector for the STA (Otherwise, it can cause more problems)
  Accommodation of the Non-TIM long sleeper stations (after long sleep, it can drift off more than one beacon period to the wrong sector/beacon interval)
  Accommodation of the mobile stations (move from sector to sector)
AP needs to know which sector the station has best reception
  Avoid the trial and error approach

## Slide 11: Proposed Sectorized Beam Training/Feedback
To allow AP to learn the best sector for the STA, we propose to employ sectorized beam training/feedback
AP transmits sectorized beam with the sector/group IDs
STA observes which sector is the best and feedback the sector/group ID to the AP.
For stationary STA, the best sector is very stable so only once or infrequent feedback is required.
AP knows a STA’s best sector, it associates the STA with a specific (TIM) group based on its sector.

## Slide 12: Proposed Sectorized Beam Operation
We propose a more flexible way to use sectorized beam operation, i.e., AP decides when it is appropriate to use the sectorized beam
  AP can switch back and forth between sectorized beam(s) and omni beam
  Sectorized beam is used only when AP is aware of the STA’s best sector or in scheduled transmission such as RAW or during TXOP of a STA. AP switch back to omni otherwise.
  Sectorized transmit beam is used in conjunction with the sectorized receive beam
  AP associate STA with a specific group (same sector/group ID) based on STA best sector

## Slide 13: Sectorized Beam Operation Example (similar to Huawei but with sector beam/group ID feedback)
AP transmits with sectorized beacons and maintains sectorized beam operation during some portion of the beacon interval.
The STA trains on beacons and feedback the best sector/group ID to AP. If STA detects link loss or degradation, it can re-train on beacons and inform the AP of the best sector/group
AP associates each sector with a specific group
AP uses STA’s best sector to communicates with a STA during RAW or TXOP, the rest of the beacon interval can be Omni
AP needs to indicate the sector/group ID with group ID associated with the STA’s sector in the beacon with TBD format. STA provides the sector/group feedback with TBD format
Beacon
Beacon
Omni
Sector 1
Beacon
AP
STA
RAW1
RAW1
RAW2
RAW2
RAW3
Sector 2
S. FB
Omni
Sectorized
Omni
Sectorized

## Slide 14: Conclusions
We propose a flexible sectorized beam operation which works for TIM-group, non-TIM, mobile stations for improved spatial re-use and reduced interference to OBSS
To enhance sectorized beam operation, an example beam training and feedback operation is discussed.

## Slide 15: Pre-Motion
Do you support the concept of STA to optionally feed back sector/group ID to AP and AP to associate the STA with a specific group based on STA’s sector

## Slide 16: Motion
Move to include the support for the STA to optionally feed back sector/group ID to AP and AP to associate the STA with a specific group based on STA’s sector in SFD