## Slide 1: A Short-Header Frame Format
Date: 2012-09-14
Authors:

## Slide 4: Abstract
This submission introduces an additional short-header frame format for IEEE 802.11ah

## Slide 5: Background
The subject of short-header frame has been discussed in the TG [1]
  The TG has already added support for short-header format based on the use of AIDs for addressing [1]
This submission proposes a two-address short-header format that utilizes the full 6-byte MAC address.
  All other header fields discussed in [1], i.e. Frame Control and Sequence Control are left unchanged.

## Slide 6: The Proposed Format
The proposed format is signaled by using a bit or a code point in the FC field
  Determination of the bit or the code point is TBD.
The proposed format is useful when AID info is not available or cannot be used
  Before and during association
  Multicast transmissions
  When Src MAC address is used to form CCMP nonce.
FC
Dest MAC
Address
Src MAC
Address
Sequence
Control
FCS
2
6
6
2
4
Body
variable
Octets:

## Slide 7: Straw Poll
Do you support adding to the specification Framework;
  “The draft specification shall define a frame format for the Short MAC Header as shown below. The indication of the format is tbd.”?
FC
Dest MAC
Address
Src MAC
Address
Sequence
Control
FCS
2
6
6
2
4
Body
variable
Octets:

## Slide 8: Motion
Move to add to the specification Framework;
  “The draft specification shall define a frame format for the Short MAC Header as shown below. The indication of the format is tbd.”
FC
Dest MAC
Address
Src MAC
Address
Sequence
Control
FCS
2
6
6
2
4
Body
variable
Octets:
Move:
Second:

## Slide 9: References
[1] 11-12/0857r1, “Short MAC Header “, Simone Merlin, et. al.