## Slide 1: Short MAC Header Signaling
Authors:

## Slide 3
Name | Affiliations | Address | Phone | Email
Ken Mori | Panasonic |  |  | 
Rojan Chitrakar | Panasonic |  |  | 
Haiguang Wang | I2R |  |  | 
Shoukang Zheng | I2R |  |  | 
Yeow Wai Leong | I2R |  |  | 
Zander Lei | I2R |  |  | 
Jaya Shankar | I2R |  |  | 
Anh Tuan Hoang | I2R |  |  | 
Joseph Teo Chee Ming | I2R |  |  | 

## Slide 4: Introduction
The MAC header is a significant overhead for short MPDUs [1, 2]
  30-36 octets in 11n, without security
  This is inefficient for short-packet applications
    E.g., the FR-EM document includes traffic specifications for sensors (256Bytes), and industrial process automation (64Bytes) [3]. Several other applications with very short transmit packets can be envisioned
Shortening the MAC header has advantages for 11ah
    Prolonged battery lifetime
    Reduced medium occupancy
Motions that define the structure of the Short MAC header have passed [5]
  See next slide for details on the structure
This presentation follows up on the details for
  Short MAC header indication

## Slide 5: Short MAC Header Format – Recap
Order of Address fields
  From AP to STA: 2 byte AID of receiver followed by BSSID (From-DS = 1)
  From STA to AP: 6 byte BSSID followed by 2 byte AID of STA (From-DS=0)
  From STA to STA: 6 byte destination STA MAC address followed by 2 byte source STA AID (From-DS=0)
A3 is optionally present
Frame format is already approved [5, 6]
From-DS = 1
From-DS = 0
(also STA 2 STA)
2B | 2B | 6B | 2B | 6B
FC | A1 (AID) | A2 (BSSID) | Sequence Ctrl. | A3 (Optionally present)
2B | 6B | 2B | 2B | 6B
FC | A1 (BSSID/RA ) | A2 (AID ) | Sequence Ctrl. | A3 (Optionally present)

## Slide 6: Short MAC Header indication
11ah devices will support both short and normal MAC headers
  Need to differentiate between the two
Short header indication tells receiver the format of received frames
  Propose to use Protocol version
    A very clean solution which differentiates 11ah from other protocols
      802.11ah networks may be deployed in other frequencies in the future
      A new value of protocol version (e.g., pv=1) will indicate short MAC Header
Short MAC Header is structurally different from normal MAC header
  There is no Duration field
  Address 1 field can be 2 bytes or 6 bytes depending on link direction (UL/DL)
Use of type/subtype in FC field or bits in the SIG field not very efficient
    Scarce number of bits in the SIG field which may be used for PHY mechanisms
    Type/subtype field already occupies 8 bits of the frame control field
      Limits the number of reusable bits in Frame Control

## Slide 7: Conclusions
Following up on the design of short MAC header [5], we propose to use a new value of the protocol version to indicate short MAC header
  A very clean solution which allows to differentiate 11ah from other protocols
  Allows to re-define frame control to include required features otherwise not available

## Slide 8: References
[1] 11-12-0365-01-00ah-mac-header-compression
[2] 11-12-0110-06-00ah-frame-header-compression
[3] 11-11-0905-03-00ah-tgah-functional-requirements-and-evaluation-methodology
[4] 11-12-0324-00-00ah-short-ack
[5] 11-12-0365-02-00ah-mac-header-compression
[6] 11-12-0857-00-00ah-mac-header-compression

## Slide 9: Straw Poll 1
Do you support to include in the spec framework that the short MAC header is indicated by a new value of the Protocol Version field?

## Slide 10: Motion 1
Move to include in the spec framework that the short MAC header is indicated by a new value of the Protocol Version field?

## Slide 11: Appendix

## Slide 12: Performance Evaluation
Assumptions
  Tx Power=19 dBm/BW=1 MHz
  STA sends one packet/receives short ACK every 0.1s/1s, and sleeps for the rest of the time
  Tx power consumption: 250 times of the sleeping power consumption (for MPDU)
  Rx power consumption: 40 times of the sleeping power consumption (for ACK)
  MAC header reduced from 30 bytes to 12 bytes, Payload = 32/64/128 bytes
Performance
  Energy consumed per Interval = TTX x 250 + TRX x 40 + Tsleep x 1
  Energy saved = 1 - energy consumed for short header / energy consumed for long header
  Medium occupancy reduced = 1-(TTX +TRX) for short header / (TTX +TRX) for long header
PHY Rate | 32B | 64B | 128B
MCS0-rep2 | 32% | 24% | 16%
MCS0 | 26% | 21% | 15%
PHY Rate | 32B/100ms | 64B/100ms | 128B/100ms | 32B/1s | 64B/1s | 128B/1s
MCS0-rep2 | 23% | 17% | 11% | 13% | 10% | 8%
MCS0 | 19% | 16% | 10% | 8% | 7% | 6%