## Slide 1: Multi-Access Link Model
Date: 2012-09-18
Authors:
Name | Address | Affiliations | Phone | Email
Donald Eastlake | Huawei Technologies | 155 Beaver Street, Milford, MA 01757 USA | +1-508-333-2270 | d3e3e3@gmail.com

## Slide 2: Abstract
This presentation discusses the modelling of an AP with associated stations as a multi-access shared link that can be used as a transit link inside networks.

## Slide 3: Multi-Access Link Model for GLK
This presentation just talks about the case people are most interested in: An AP with associated STAs.
Radio “links” are inherently multi-access. You broadcast and, in general, multiple stations can receive.
Network connectivity in such cases is currently provided by pretty much just saying that the AP can have one portal.
  Clearly there are mechanisms required to get this to work well – particularly in the case of an ESS – which are mostly left out of scope in the current 802.11 standard.

## Slide 4: Usual Diagram of an AP with two STAs
STA1
STA2
Portal
AP

## Slide 5: But Radio Links are Inherently Multi-Access
AP
STA1
STA2
Portal

## Slide 6: Multi-Access Link Model for GLK
Why not just say that STAs can have a portal?
AP
STA1
STA2
Portal
Portal
Portal

## Slide 7: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  Loop prevention.
  Multi-destination frame reflection.
  Actual link costs are poorly reflected to the outside so routing may be pretty far from least cost.
  Some protocols are inefficient on multi-access links or don’t support them at all.
  How does the STA/AP decide whether to send frames over the air or over the portal or both?

## Slide 8: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  Loop prevention.
    Not always a problem, for example when the STA portal leads to an IP router.
    When it is a potential problem, just put a loop preventing device, such as an 802.1 bridge. at the end of the portal.
    If bridges added to all portals, previous example look like this:
STA1
Bridge1
Bridge2
STA2
Bridge3
AP

## Slide 9: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  Multi-destination frame reflection.
    This problem with STA originated multi-destination frames reflected by the AP affects all the models and the solutions are the same:
    More Addresses: 4-address format, 5-address format, 802.11n aggregated frame format, …
    Special destination address indicating intended STAs: Probably limited to 24 STAs. May require additional control protocol for bit assignment.
    Sequence number matching or the like.

## Slide 10: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  Actual link costs are poorly reflected to the outside so routing may be pretty far from least cost.
    At least for IS-IS and some other protocols that understand multi-access links, a pseudo-node is created to model the link which permits better reflection of costs:
STA1
Bridge1
Bridge2
STA2
Bridge3
AP
Pseudo Node

## Slide 11: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  Some protocols are inefficient on multi-access links or don’t support them at all.
    Fix them

## Slide 12: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  How does the STA/AP decide whether to send frames over the air or over the portal or both?
    For the single AP with single portal case, it is easy. STAs just send to the AP. The AP knows the MAC addresses of the associated STAs, so unicast is send to the right station or sent out the portal. And multi-destination frames are sent to both.
    Add a portal to the STA makes this much more complex.
      The AP may have to send a frame to a STA so the STA can send it out the STA’s portal.
      A STA does not always just send to the AP. It may need to send out its portal.
      No simple rule is possible at the AP. Some form of address table appears necessary

## Slide 13: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  How does the STA decide whether to send frames over the air or over the portal or both? (continued)
    Without portal, STA just sends everything to the AP.
    With portal, STA needs to decide between sending frame to AP, sending frame out the portal, or both.
    No simple rule is possible at the STA. Some form of address table appears necessary.

## Slide 14: Multi-Access Link Model for GLK
Why not just say that STAs can have a portal?
  You need to say more at least about how frames are forwarded at the AP and STAs. This necessarily makes that STAs and AP, at least in the aggregate, at least a little bit “bridge like”.
AP
STA1
STA2
Portal
Portal
Portal

## Slide 15: Multi-Access Link Model for GLK
Therefore, you can’t really have
But you could have
STA1
Bridge1
Bridge2
STA2
Bridge3
AP
STA1
STA2
AP