## Slide 1: Masters, Slaves and Clients
Slide 1
Date: 2012-09-11
No changes from r1 yet
Notes: Month Year
        John Doe, Some Company
Page 1

## Slide 2: Executive Summary
  “…radio equipment shall be so constructed that it effectively uses the spectrum allocated to terrestrial/space radio communications and orbital resources so as to avoid harmful interference.”
This document considers a range of issues related to master devices, slaves and client devices
  Regulations are getting more complicated with other primary services in the same band, co-channel and on adjacent channels
  Regulations are updated more frequently in anticipation of future issues and in response to difficulties experienced
  In general, devices are certified as master, client (slave) or both depending on their operational characteristics, and without reconfiguration operate legally within a regulatory domain
    The lowest common denominator master could work worldwide in 2.4 GHz bands, but there is no common denominator for 5 GHz bands
  Slaves and client devices operate under control of their master, and system operation is tested before regulatory approval is received

## Slide 3: 802.11ac is changing the information that client devices use to configure transmission
12/297r0 has detailed review of issues with managing BSS emissions footprint
  https://mentor.ieee.org/802.11/dcn/12/11-12-0297-00-00ac-tpc-operating-classes-and-channel-switching.pptx
  This presentation builds on 11ac Draft 3.0 and the client control text of 12/379r6
  https://mentor.ieee.org/802.11/dcn/12/11-12-0379-06-00ac-tpc-operating-classes-and-channel-switching.docx

## Slide 4: Executive Summary
This document considers a range of issues related to master devices, slaves and client devices
  Regulations are getting more complicated with other primary services in the same band, co-channel and on adjacent channels
  Regulations are updated more frequently in anticipation of future issues and in response to difficulties experienced
  In general, devices are certified as master, client (slave) or both depending on their operational characteristics, and without reconfiguration operate legally within a regulatory domain
    The lowest common denominator master could work worldwide in 2.4 GHz bands, but there is no common denominator for 5 GHz bands
  Slaves and client devices operate under control of their master, and system operation is tested before regulatory approval is received

## Slide 5: DFS and TPC are broad UNII requirements in FCC Part 15
And further regulations in subpart C
i.e.
This is the clause that lets you know that the gov’t can knock on the end-user’s door. For the manufacturer, the products had better be in compliance with Part 15 . For the end-user, hopefully there is a channel and/or a TPC level that avoids harmful interference , else no operation.
The AP has the right and the responsibility to select the channels and the max TX power of the clients within legal limits
Which in turn refer us to more regulations
Which in turn refer us to more regulations in subpart A
And which also refers us to other subparts
Which defines TX power, etc
Part 15 has a subpart for UNII
1
2

## Slide 6: FCC UNII-band rules evolve
47 CFR 15 Subpart E—Unlicensed National Information Infrastructure Devices – triennial review
FCC KDB 443999 removing operation in 5600-5650 MHz (2010-10)
FCC KDB 594280 restating master and client rules (2011-02)
  Section 2.931 requires the grantee to ensure that the product as sold continues to comply with the conditions of the grant.
FCC KDB 848637 UNII client devices without radar detection (2011-04)
FCC KDB 442821 Software Defined Radio Application Guide (2012-04)

## Slide 7: EU 5 GHz bands and rules evolved
EN 301 893 v1.5.1 (2008-12) added 40 MHz occupied bandwidths while protecting other services
  Changes to permit 802.11n operation
EN 301 893 v1.6.1 (2011-12) added wider occupied bandwidths while protecting other services
  Changes to permit 802.11ac operation
EN 301 893 v1.7.1 (2012-06) added politeness requirements in technology neutral form
  Listen Before Talk with listening proportional to transmit power, higher power requires more silence than lower power
  EN 300 440, 5.725-5.875 GHz band, ERC 70-03 Short Range Device rules permit transmissions up to 25 mW

## Slide 8: Current view/existing 5 GHz spectrum: channelization for 20/40/80 MHz
20/40/80 MHz channelization (802.11 Global table)
  Consists of two adjacent IEEE 20/40 MHz channels
  Non-overlapping channelization
*FCC KDB 443999 Restricting U-NII devices from 5600-5650 MHz https://apps.fcc.gov/oetcf/kdb/index.cfm
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
IEEE channel #
20 MHz
40 MHz
80 MHz
5170
MHz
5330
MHz
5490
MHz
5710
MHz
5735
MHz
5835
MHz
144
Currently available channels
TDWR unavailable channels*

## Slide 9: Band plan with new spectrum Importance of Additional Spectrum
Wide bandwidth channels desired to support high throughput requirements
At the same time, large number non-overlapping channels desired to support high QoS requirements
  To avoid co-channel interference
Current UNII spectrum allows only
  Six 80 MHz channels
  Two 160 MHz channels
Additional unlicensed use of 5.35-5.47 GHz and 5.85-5.925 GHz would allow
  Nine 80 MHz channels
  Four 160 MHz channels
144
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
IEEE channel #
20 MHz
40 MHz
80 MHz
160 MHz
UNII-1
UNII-2
UNII-2
UNII-3
5250
MHz
5350
MHz
5470
MHz
5725
MHz
NEW
96
92
88
84
80
76
72
68
169
173
177
181
5825
MHz
5925
MHz
NEW
Currently available channels
New channels

## Slide 10: 5 GHz radio SKUs that come from regulations continue to evolve
Some of the 5 GHz SKUs come from different OOBE filter and amplifier requirements, others come from channels to remain unused.
The following slides show a county’s 2011 GDP ranking and its 5 GHz allowed channels.

## Slide 11: 5 GHz channels allowed by EU (#1)
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
20 MHz
40 MHz
80 MHz
160 MHz
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.875 GHz
17
8
4
2
# of non-overlapping channels

## Slide 12: 5 GHz channels allowed by China (#2)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40 or 80 MHz)
Maybe by 2014 China will add lower 5 GHz bands
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.850 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
5
2
1
0

## Slide 13: 5 GHz channels allowed by India (#3), Mexico (#11) & others
Regulatory
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.875 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
13
6
3
1

## Slide 14: 5 GHz channels allowed by Japan (#4)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
140
136
132
128
124
120
116
112
108
104
100
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
19
9
4
2

## Slide 15: 5 GHz channels allowed by Russia (#6)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.875 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
16
8
4
1
144

## Slide 16: 5 GHz channels allowed by Brazil (#7) & Taiwan (#19)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40 or 80 MHz)
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.850 GHz
20 MHz
40 MHz
80 MHz
160 MHz Channels Currently Not Possible For Taiwan
# of non-overlapping channels
17
7
3
0
144

## Slide 17: 5 GHz channels allowed by Korea (#12)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.825 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
19
9
4
1

## Slide 18: Master Devices Background
  In 5 GHz radar bands, master devices must perform Initial Channel Availability Check before transmitting
    Current FCC rules require 1 minute channel availability check (CAC)
    Current EU rules require 1 minute channel availability check; or 10 minute channel availability check if all or part of emissions bandwidth is within the 5600-5650 MHz band
  Master devices set constrained transmit power to control emissions footprint of BSS as required by law
    “…radio equipment shall be so constructed that it effectively uses the spectrum allocated to terrestrial/space radio communications and orbital resources so as to avoid harmful interference”. [Directive 1999/5/EC of the European Parliament and of the Council of 9 March 1999 (R&TTE Directive)]
    “(10) Efficient use of the radio spectrum, according to the state of the art, shall be ensured so as to avoid harmful interference.” [COM(2012) 584 final, 2012/0283 (COD), 17 October 2012 (R&TTE Directive)]

## Slide 19: More regulatory background
  Each client’s manufacturer is responsible for ensuring that the client meets the regulations for which it was homologated
  More importantly, the default unlicensed radio frequency device regulatory approval is as a master device; to be approved as a client device the manufacturer must show that the frequencies and transmit powers the client device uses conform to regulations:
    client devices are required to operate as controlled by the master
    The client needs to get enough current-channel permissions from the Beacon that it can transmit to the AP (bootstrap) and preferably select one AP over another
    The client needs to get all current-channel permissions from the Probe/(Re)Assoc Response that it can participate fully in the BSS
    The client needs to get the next-channel permissions before/inside the channel switch

## Slide 20: Current 2.4 and 5 GHz rules
FCC
2.4 GHz 47 CFR 15 Subpart C-Intentional Radiators, 47 CFR Part 15.247
5.15-5.85 GHz 47 CFR 15 Subpart E—Unlicensed National Information Infrastructure Devices
5.725-5.85 GHz 47 CFR Part 15.247
EU
2.4 GHz EN 300 328 v1.7.1
5.15-5.725 GHz EN 301 893 v1.5.1
5.725-5.875 GHz EN 300 440

## Slide 21: Open Discussion

## Slide 22: Backup Slides
http://en.wikipedia.org/wiki/List_of_WLAN_channels
CEPT SE24 on 5725-5875 MHz:
http://www.cept.org/Documents/se-24/5943/M65_26R0_SE24_WI39_way_forward_f-inaldoc
R&TTE Directive 17 October 2012
http://ec.europa.eu/enterprise/sectors/rtte/documents/legislation/review/index_en.htm

## Slide 23: Some non-Wi-Fi product vendors have not maintained our level of care – and we want to continue avoiding their path
i.e. it is serious business with timebound requirements - and promptness: actions have consequences
Re-engineering; and/or restricted orderability of products (fewer sales channels)
Development personnel training
It requires a senior compliance officer
  E.g. FCC enforcement: 22 companies named, shamed and/or fined at: http://www.fcc.gov/encyclopedia/weather-radar-interference-enforcement
  For one large corporation, the Consent Decree included:
    a. Compliance Officer. LargeCorp will designate a senior corporate manager ("Compliance Officer") who is responsible for administering the Compliance Plan.
    c. Compliance Reports. LargeCorp will file compliance reports with the Commission 90 days after the Effective Date, 12 months after the Effective Date, and 24 months after the Effective Date. Each report shall include a compliance certificate from the Compliance Officer stating that the Compliance Officer has personal knowledge that LargeCorp has established operating procedures intended to ensure compliance with this Consent Decree, together with an accompanying statement explaining the basis for the Compliance Officer's compliance certification.
    b. Training. LargeCorp will train and provide materials concerning Section 302(b) of the Act and Parts 2 and 15 of the Rules pertaining to U-NII devices and the requirements of the Consent Decree to those of its employees who are involved directly in the development and marketing of U-NII devices imported, marketed and sold by LargeCorp in the United States.

## Slide 24: WISPA Links
Are you near TDWR?
  http://wispa.cms.memberfuse.com/tdwr-locations-and-frequencies
  // starting to list two frequencies per TDWR
If so, register here
  http://www.spectrumbridge.com/udia/home.aspx
  “This tool allows a user (network operator or installer) to:
  • Search and confirm if their device is operating within 35 km proximity of TDWR site(s)
  • Voluntarily register certain technical information into the online database”

## Slide 25: US Non-DFS

## Slide 26: US 5 GHz

## Slide 27: US U-NII-4

## Slide 28: EMEA

## Slide 29: EU 5 GHz

## Slide 30: EU ITS channels and RLANs