## Slide 1: WG11 Review of Nov 2012 Proposed PARs
Date: 2012-11-12
Authors:

## Slide 2: Abstract
Review of 10 PARs and 5Cs presented for Consideration during the 2012 November Plenary and a review of Proposed changes to the defined 5Cs and the responses.
802.1ACby - amendment for Support by Ethernet over Media Oriented Systems Transport (MOST) PAR and 5C
802.1Qbz - amendment for Enhancements to Bridging of 802.11, PAR and 5C
802.1Qca - amendment for Path Control and Reservation, PAR and 5C
802.16r - amendment for Small Cell Backhaul (SCB) Applications, PAR and 5C
802.11ak - amendment for Global Link, PAR and 5C
802.11aq - amendment for Pre-association Discovery (PAD), PAR and 5C
802.15.4q - amendment for Ultra Low Power, PAR and 5C
802.22.1a - amendment for Advanced Beaconing, PAR and 5C
802.3bj - PAR modification request & Updated 5C
802.3bp - amendment for 1 Gb/s Operation over Fewer than Three Twisted Pair Copper Cable, PAR and 5C
802.21 - revision PAR for IEEE Std 802.21-2008, PAR.
802.21.1 - standard for Media Independent Services, PAR and 5C

## Slide 3: 5C Feedback to 802
1.5 Economic Feasibility
replace the 2nd sentence with “The proposed project shall provide a summary of the “cost for performance” analysis, showing the assessment factors including, at a minimum, the affect of installation costs.
Remove a), b) and c)
Rationale: State the metrics, then use them in assessments (in b) with a single question and allow WG to provide assessments.)

## Slide 4: 802.1Qbz
Thanks for working with 802.11.
Response was received:
“Thanks for the comment - and thanks to 802.11 for working with us too!”

## Slide 5: 802.3bj
The Note for Item 0 is not necessary in 8.1.
Suggest that you don’t add the 5.2 comment in 8.1.
Include in 8.1 an explanation of the changes being requested.
5C: Suggest that you change the answer to the Compatibility question from Yes to No, and delete “The P802.3bj PAR mandates that” from the start of that bullet.
Addressing the compatibility in one place should be sufficient.

## Slide 6: Response from 802.3bj
Accept all comments
• Remove Note in 8.1 for Item 0
• Remove Note in 8.1 for Item 5.2b
• Add the following note in 8.1 “Item 5.2b – scope has been expanded to allow the addition of optional Energy Efficient Ethernet (EEE) for 40 Gb/s and 100 Gb/s operation over backplanes and copper cables.”
• In 5C Compatibility Response –
  – Change “The P802.3bj PAR mandates that the amendment shall comply with IEEE Std 802, IEEE Std 802.1D and IEEE Std 802.1Q.” to “The amendment shall comply with IEEE Std 802, IEEE Std 802.1D and IEEE Std 802.1Q.”

## Slide 7: 802.3bp
2.1 Title: suggest that the “amendment:” is missing.
Typically a title for an amendment has “amendment” in the title. E.g. the base title followed by “amendment: “ and then the amendment title.
8.1 – Delete the 5.2 note.
5C- in Compatibility, delete last bullet.

## Slide 8: Response from 802.3bp
Our response was worked out in a meeting with Jon Rosdahl, 1st Vice Chair of 802.11 and NesCom Chair: The PAR title actually does contain the word "Amendment," and no change has been made to the PAR. Please see below, or the PDF of the PAR which is attached to this email: 2.1 Title: Approved Draft Standard for Ethernet Amendment Physical Layer Specifications and Management Parameters for 1Gb/s Operation over Fewer than Three Twisted Pair Copper Cable The colon is missing, but we have no control over that, as you know. We accept both of your changes: 8.1 - Delete the 5.2 note. This has been done. Please see the attached PDF of the P802.3bp PAR. 5C- in Compatibility, delete last bullet. This has been done. Please see the attached PDF of the P802.3bp 5C. This returns our PAR and 5C to the version we had in July. We believe this also addresses the comment from Peter Balma of NesCom.

## Slide 9: 802.15.4q
5C – 3a – Suggests that some existing 15.4 devices can operate with coin cell batteries. This would imply that the existing standard is sufficient for building compliant devices operating with coin cell batteries.
Q1: Why do you need a new Standard? How is it “unique” from the existing standard?
5C – 3a seems to infer that the problem being solved is related to pulse current, while 3b suggests the problem is average current.
Q2: What is the actual problem?

## Slide 10: Response from 802.15 Q1:
Q: Why do you need a new Standard? How is it “unique” from the existing standard?
A: 5C 3a says the current standard cannot be used to power the majority of the existing 802.15.4 chipsets in these applications. The operative word is majority. Addressing only a small subset is missing a big market opportunity. This amendment addresses a solution enabling a far broader set of applications than is currently possible. The clause: --in a much broader set of applications-- is being added to the end of the sentence: --This 802.15.4 PHY amendment allows the use of smaller battery form factors such as coin cell batteries.-- to enhance clarity on this point.

## Slide 11: 802.15 Response Q2:
Q: What is the actual problem?
A: 5C 3b says: The proposed amendment to IEEE 802.15.4 will provide a unique solution for ultra low power applications. This is the entire statement under 3b. It makes no reference to average power, nor is average power mentioned anywhere in the 5C so we are at a bit of a loss to understand the question. Clearly average power is important in achieving long battery life so the lower the average power the better. The primary issue with energy constrained sources, like coin cells, is their inability to deliver high peak power so that is also of primary interest here. If that can be achieved at lower average power too, so much the better.

## Slide 12: 802.16r
PAR 5.2b – suggest that you do not need the phrase “particularly below 6 GHz” or change to say that this is just below 6 GHz.
General Question: What is the expected data rate that you are looking to define?
What is the new standard providing that is not being provided by LTE?

## Slide 13: Response from 802.16r
802.16 appreciates comments on the draft IEEE P802.16r PAR received from 802.11 and from Paul Nikolich. Responses are provided here:
IEEE 802.16-12-0677-00
http://doc.wirelessman.org/16-12-0677-00
The draft P802.16r PAR, as revised in accordance with these comments and with others raised to the attention of the 802.16 WG, is here:
IEEE 802.16-12-0587-03
http://doc.wirelessman.org/16-12-0587-03

## Slide 14: 802.21 and 802.21.1 general comment
We cannot support either of the 802.21 proposed PARS in the current state.
In both, 5.2 – Scope does not specify what you are really going to produce.
Not certain what are the overall goals of the two PARs.
Do you really have an Architecture vs Framework?
How will your Framework fit into the 802 O&A?
The proposed Scope seems to be too broad/ open ended

## Slide 15: 802.21 Scope
5.2 This standard defines an extensible IEEE 802(R) media access independent services framework that facilitates handover and related services (e.g., discovery) between heterogeneous IEEE 802 networks. It also facilitates handover between IEEE 802 networks and cellular networks.
Make the scope more specific to a clear focus and direction.

## Slide 16: 802.21 Purpose
5.4 Change the purpose to “The Purpose of this standard is to improve the user experience of mobile devices by describing a framework that provides the necessary services to facilitate handover between heterogeneous IEEE 802 networks. This framework is also applicable for interworking between IEEE 802 networks and Cellular networks.”
Makes the Purpose in harmony with the new scope.

## Slide 17: 802.21 Response
802.21 appreciates comments on the draft IEEEP802.21-revision and IEEEP802.21.1 PARs received from 802.11. Comment responses are available at:
https://mentor.ieee.org/802.21/dcn/12/21-12-0169-00-0000-par-comments-response.pptx
PARs and 5C are accordingly revised and are available at:
https://mentor.ieee.org/802.21/dcn/12/21-12-0088-03-0000-p802-21-revision-par.pdf
https://mentor.ieee.org/802.21/dcn/12/21-12-0089-04-0000-802-21-1-par.pdf
https://mentor.ieee.org/802.21/dcn/12/21-12-0126-02-0000-proposed-802-21-1-5c.docx

## Slide 18: 802.22.1a
In the current form, we cannot support the approval of the proposed PAR.
The Title 2.1 and Scope 5.2b does not communicate clearly the substance of the project.
Unable to differentiate what alternate systems you will be actually communicating with.
Which of the communication devices are 802.22, and which are some other 3rd party device operating in the frequency band mentioned.
What types (quantities) of information will you convey in the proposed beaconing scheme?
Are the Beacons adhering to the existing 802.22 definitions?
Why is there a new PHY? What is new and different that you need in the PHY world?
Is this a complementary Radio communicating with some other existing non-802 device, then that communication is already defined by the other device
5.4, the purpose is supposed to be what is in the final Standard, not the Amendment, so you should either not change the purpose statement, or the new statement should address what is in the final resultant standard. The proposed Purpose Statement seems to try to address the amendment only.

## Slide 19: 802.22 Response
Your comment on the Title of the Amendment were valid.
So based on the suggestion from Jon and Bruce we took an action to convert the PAR to a Revision PAR rather than an amendment PAR. This way we can make modifications to the Title and Scope of the document. We worked with Lisa (Perry and Yacone) this AM and they said that this was doable.
Based on your comments, her is the PAR and 5C as well as our responses to the comments in the Powerpoint. Since now this is a revision, we do not need to send a 5C, but it is still attached for reference. The documents containing track changes can be found on the Mentor at: https://mentor.ieee.org/802.22/dcn/12/22-12-0083-05-0001-advanced-beaconing-par.docx https://mentor.ieee.org/802.22/dcn/12/22-12-0084-05-0001-advanced-beaconing-5c.docx https://mentor.ieee.org/802.22/dcn/12/22-12-0102-00-0001-802-22-responses-to-comments-on-the-802-22-1-par.pptx
Please let us know if you have any further inputs on the PAR.

## Slide 20: 802.22 Rebutal
We would suggest that the following Sentence be deleted “The beacon may also be used for applications such as search and rescue amongst others. “ from the PAR Scope statement.
The rationale is that this leaves the PAR Scope too broad.