## Slide 1: Further Discussions about FILS Discovery (FD) Frame Format Design
Date: 2012-11-03
Authors:

## Slide 2: Abstract
This document is intended to continue the discussions about the FILS Discovery (FD) Frame format Design, through an analysis among the two candidates, a new Extension frame and a new Public Action frame.
This contribution provides supporting materials to the detailed text proposal for the TGai draft Specification document, as proposed in Contribution 12/1236.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | ??
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4
Background
The FILS Discovery (FD) frame format design has been discussed in previous TGai meetings, e.g., in September meeting with the following contributions:
  12/1029: FILS Discovery Frame format;
  12/1130: Scanning Ad Hoc Group Report.
  12/1148: further discussion about FD frame format
  Two candidates are still under considerations:
  A new Extension frame
    Smaller MAC framing overhead, then resulted in a smaller frame size;
    A preferred option based straw poll;
    Concerns with implementation complexity.
  A new Public Action frame
    Larger MAC framing overhead, then resulted in a larger frame size;
    Concerned with overall overhead introduced by FD frame, due to “more frequent transmissions”.
Further work is needed to narrow down the FILS Discovery frame format design.

## Slide 5
The focus of this Contribution
Detailed FD frame format designs, with two options:
  Designed as a new Extension frame;
  Designed as a new Public Action frame.
A comparison study of wireless medium occupancy with the two format options.

## Slide 6: Option-1: FD Frame as a New Extension Frame
Framing overhead = 13 bytes, including
  3 bytes Frame control; 6 bytes BSSID; and 4 bytes FCS

## Slide 7: Option-2: FD Frame as a New Public Action Frame
Framing overhead = 32 bytes, including
  24 bytes MAC header; 1 byte Category; 1 byte Public Action; 2 bytes FD Frame control; and 4 bytes FCS

## Slide 8: A Comparison Study of Wireless Medium Occupancy
FD Frame Body Size Considerations
Timing Diagram of Frame Transmission
FD frame transmission pattern / interval
Case Studies of FD Frame WM Occupancy Analysis
Observations and Discussions

## Slide 9: FILS Discovery (FD) Frame Body Size Considerations
The Content Items listed below are based on 802.11ai SFD, 12/0151r13;
The sizes are based on Sept-meeting discussions and the proposals in Contribution 12/1238;
With 8-byte typical FD SSID and 9-byte typical Neighbour AP info, typical sizes of FD frame body:
  Typical_Min: 8 bytes, with no optional content items;
  Typical_Max: 27 bytes, with all optional content items.
Index | Information | size (bytes) | Notes
1 | FD SSID | 1 to 32 | Mandatory, typical size of 6 to 8 bytes
2 | FD Capability | 3 | optional
3 | Access Network Options | 1 | optional
4 | FD Security | 4 | optional
5 | AP Configuration Change Count | 1 | optional
6 | AP’s next TBTT | 1 | optional
7 | Neighbor AP Info | variable, >=4 | Optional, typical size of 4 to 9

## Slide 10: Timing Diagram of Frame Transmission (11g-based WLAN)
PSDU: MPDU, or MMPDU
FD frame: MMPDU
Assuming FD frame transmitted at the same date rate as Beacon:
  Contribution 11/1031r0: 300s measurement during 802.11 Mid-week plenary
    ~30% Tx at 1 Mbps and ~70% Tx at 11 Mbps;
  Contribution 11/1413r2: 300s measurement, 6:00pm, Shinjuku station (Keio line), Tokyo
    ~ 99.93% Tx at 1 Mbps.

## Slide 11: FD Frame Transmission Patterns and Intervals
Case 1
Case 2
Case 3
T1
T2
time
time
time
FILS Discovery Frame
Beacon
Based on Section 6.3.1 in 802.11ai SFD, 12/0151r13,
The FILS Discovery Frame may be transmitted periodically and/or non-periodically.
If transmitted periodically, the periodicity of the FILS Discovery Frame may be changed.
The interval between regular beacon and FILS Discovery Frame shall be no less than dot11aiFILSBeaconMinimumInterval.

## Slide 12: Case Studies: FD Frame Wireless Medium (WM) Occupancy
Purpose: comparisons between the two options for FD frame format design, with a reference to Beacon frame
  FD frame format option-1: a new Extension frame, with a framing overhead of 13 bytes;
  FD frame format option-2: a new public action frame with a framing overhead of 32 bytes.
Performance measures:
  WM Occupancy: Percentage of FD frame(s) / Beacon frame occupied time over the Beacon Interval
  MAC Frame occupancy: the percentage of the MAC frame, i.e., MPDU or MMPDU, WM occupied time over the entire frame transmission WM occupied time
Study two cases:
  Case-1: One AP on the channel
  Case-2: Multiple APs on the channel
Parameters:
  Beacon Interval (BI): 100ms
  Transmission Data Rates: 1 Mbps and 11Mbps;
  Number of FD frames per BI: 1, 2, 3, and 4
  Beacon frame body size (bytes): 130
  FD Frame Body Sizes (bytes): 8 and 27
  Average backoff time: 61us and 702 us

## Slide 13: Case-1: WM Occupancy when One AP on the Channel
WM Occupancy: percentage of frame time over a BI (Beacon Interval)
  BI = 100 ms;
  Frame Time: overall WM occupied time for transmitting a frame, including:
  DIFS + AveBackoff+ aPreamble + aPLCPHeader + MAC frame Time
  MAC frame time: WM occupied time for transmitting an MPDU/MMPDU, i.e.,
  (MPDU/MMPDU size (bits))/Tx_Rate) rounded up to multiple of PHY symbols
With One AP on the channel:
  One Beacon frame per BI, then Beacon Frame WM occupancy is:
  Beacon_Frame_Time / BI
  1, 2, 3, or 4 FD frames per BI, the FD frame WM occupancy is:
  (#_of_FD_frames * FD_Frame_Time) / BI

## Slide 14: Case-1: WM Occupancy when One AP on the Channel –Con’t
 |  | average backoff 61us, for 20% load |  |  |  |  | average backoff 702us, for 50% load |  |  |  | 
 |  | FILS Discovery Frame |  |  |  | beacon | FILS Discovery Frame |  |  |  | beacon
 |  | extension frame |  | public action frame |  |  | extension frame |  | public action frame |  | 
 | framing overhead (bytes) | 13 | 13 | 32 | 32 | 28 | 13 | 13 | 32 | 32 | 28
 | frame body size (bytes) | 8 | 27 | 8 | 27 | 130 | 8 | 27 | 8 | 27 | 130
 | MAC frame size (bytes) | 21 | 40 | 40 | 59 | 158 | 21 | 40 | 40 | 59 | 158
Tx at 1Mbps | 1 FD frame per BI | 0.471% | 0.623% | 0.623% | 0.775% | 1.567% | 1.112% | 1.264% | 1.264% | 1.416% | 2.208%
 | 2 FD frames per BI | 0.942% | 1.246% | 1.246% | 1.550% | 1.567% | 2.224% | 2.528% | 2.528% | 2.832% | 2.208%
 | 3 FD frames Per BI | 1.413% | 1.869% | 1.869% | 2.325% | 1.567% | 3.336% | 3.792% | 3.792% | 4.248% | 2.208%
 | 4 FD frames per BI | 1.884% | 2.492% | 2.492% | 3.100% | 1.567% | 4.448% | 5.056% | 5.056% | 5.664% | 2.208%
Tx at 11Mbps | 1 FD frame per BI | 0.319% | 0.335% | 0.335% | 0.347% | 0.419% | 0.960% | 0.976% | 0.976% | 0.988% | 1.060%
 | 2 FD frames per BI | 0.638% | 0.670% | 0.670% | 0.694% | 0.419% | 1.920% | 1.952% | 1.952% | 1.976% | 1.060%
 | 3 FD frames Per BI | 0.957% | 1.005% | 1.005% | 1.041% | 0.419% | 2.880% | 2.928% | 2.928% | 2.964% | 1.060%
 | 4 FD frames per BI | 1.276% | 1.340% | 1.340% | 1.388% | 0.419% | 3.840% | 3.904% | 3.904% | 3.952% | 1.060%

## Slide 15: Case-2: WM Occupancy when Multiple APs on the Channel
Multiple APs on the Channel
  4 APs, chosen based on the measurements of 4 to 5 times more Probe Response frames than Probe Request frames.
  FD frames and Beacon frames:
    25% transmitted at 1 Mbps; and 75% transmitted at 11 Mbps.
  One Beacon frame per AP per BI, then Beacon Frame WM occupancy is:
  (#_of_APs * Beacon_Frame_Time )/ BI
  1, 2, 3, or 4 FD frames per AP per BI, the FD frame WM occupancy is:
  (#_of_APs * #_of_FD_frames * FD_Frame_Time )/ BI

## Slide 16: Case-2: WM Occupancy when Multiple APs on the Channel –Con’t
 |  | average backoff 61us, for 20% load |  |  |  |  | average backoff 702us, for 50% load |  |  |  | 
 |  | FILS Discovery Frame |  |  |  | beacon | FILS Discovery Frame |  |  |  | beacon
 |  | extension frame |  | public action frame |  |  | extension frame |  | public action frame |  | 
 | framing overhead (bytes) | 13 | 13 | 32 | 32 | 28 | 13 | 13 | 32 | 32 | 28
 | frame body size (bytes) | 8 | 27 | 8 | 27 | 130 | 8 | 27 | 8 | 27 | 130
 | MAC frame size (bytes) | 21 | 40 | 40 | 59 | 158 | 21 | 40 | 40 | 59 | 158
25% Tx at 1Mbps; 75% Tx at 11Mbps | 1 FD frame per BI | 1.428% | 1.628% | 1.628% | 1.816% | 2.824% | 3.992% | 4.192% | 4.192% | 4.380% | 5.388%
 | 2 FD frames per BI | 2.856% | 3.256% | 3.256% | 3.632% | 2.824% | 7.984% | 8.384% | 8.384% | 8.760% | 5.388%
 | 3 FD frames Per BI | 4.284% | 4.884% | 4.884% | 5.448% | 2.824% | 11.976% | 12.576% | 12.576% | 13.140% | 5.388%
 | 4 FD frames per BI | 5.712% | 6.512% | 6.512% | 7.264% | 2.824% | 15.968% | 16.768% | 16.768% | 17.520% | 5.388%

## Slide 17: FD Frame WM Occupancy Observations and Discussions
FD frame format options: new extension frame vs. new public action frame:
  19-byte framing overhead difference between FD frame format options, i.e., 13-byte for new Extension frame vs. 32-byte for new Public Action frame;
  No significant impact on FDM frame WM occupancy:
    Only 0.01% to 0.61% differences, when one AP on the channel, i.e., additional 12us to 610us per BI is needed if using public action frame;
    Only 0.188% to 0.8% differences, when 4 APs on the channel, i.e., additional 188us to 800us per BI is needed, if using public action frame;
FD frame body sizes: without vs. with-all optional content items
  Also 19-byte difference, i.e., 8-byte typical min vs. 27-byte typical max;
  The same, i.e., No significant impact on the FD frame WM occupancy.
Frame Size impact on frame WM Occupancy:
  Is not significant within 19-byte difference in both Case-1 and Case-2;
  Becomes more significant, as the Tx Rates decreases, and/or the media load decreases.

## Slide 18: FD Frame WM Occupancy Observations and Discussions – con’t
Numbers of FD Frames per BI, when one AP on the Channel:
  Beacon frame WM occupancy: 0.419% to 2.208%
  If using 2.208% as a reference for the max allowed FD frame occupancy, then:
    3 or 4 FD frames per BI, i.e., 20ms or 25ms FD frame interval, could be used, when 20% media load, depending Tx rates;
    Only 2 FD frames per BI, i.e., 33ms FD frame interval, could be used, when 50% media load.
Numbers of FD Frames per BI, when 4 APs on the Channel:
  Beacon frame WM occupancy: 2.824% to 5.388%
  If using 5.388% as a reference for the max allowed FD frame occupancy, then:
    3 FD frames per BI, i.e., 25ms FD frame interval, could be used, when 20% media load;
    Only 1 FD frame per BI, i.e., 50ms FD frame interval, could be used, when 50% media load.
Two aspects regarding the number of FD frames per BI:
  Should be constrained by a max allowed frame occupancy to limit the overhead;
  Can be used to implicitly indicate the media load on the channel.

## Slide 19: MAC Frame Occupancy in Overall Frame Time
MAC Frame Occupancy in Overall frame time:
  Defined as the percentage of the MAC Frame time over the overall frame time;
  An indication of the significance of the MAC frame size in the overall WM occupancy for transmitting the MAC frame.
Overall Frame Time
  The total WM occupancy time used to transmit an MAC frame, e.g., MPDU or MMPDU, including:
  DIFS + AveBackoff+ aPreamble + aPLCPHeader + MAC frame Time
  MAC frame time:
  The time used to transmit the MPDU or MMPUD, i.e.,
  (MPDU/MMPDU size (bits))/Tx_Rate) rounded up to multiple of PHY symbols

## Slide 20: MAC Frame Occupancy in Overall Frame Time – con’t
 |  | average backoff 61us, for 20% load |  |  |  |  | average backoff 702us, for 50% load |  |  |  | 
 |  | FILS Discovery Frame |  |  |  | beacon | FILS Discovery Frame |  |  |  | beacon
 |  | extension frame |  | public action frame |  |  | extension frame |  | public action frame |  | 
 | framing overhead (bytes) | 13 | 13 | 32 | 32 | 28 | 13 | 13 | 32 | 32 | 28
 | frame body size (bytes) | 8 | 27 | 8 | 27 | 130 | 8 | 27 | 8 | 27 | 130
 | MAC frame size (bytes) | 21 | 40 | 40 | 59 | 158 | 21 | 40 | 40 | 59 | 158
 | Average Backoff time (us) | 61 | 61 | 61 | 61 | 61 | 702 | 702 | 702 | 702 | 702
Tx at 1 Mbps | Frame Tx overall WM time (us) | 471 | 623 | 623 | 775 | 1567 | 1112 | 1264 | 1264 | 1416 | 2208
 | MAC frame Tx time (us) | 168 | 320 | 320 | 472 | 1264 | 168 | 320 | 320 | 472 | 1264
 | MAC frame Occupancy | 35.67% | 51.36% | 51.36% | 60.90% | 80.66% | 15.11% | 25.32% | 25.32% | 33.33% | 57.25%
Tx at 11 Mbps | Frame Tx overall WM time (us) | 319 | 335 | 335 | 347 | 419 | 960 | 976 | 976 | 988 | 1060
 | MAC frame Tx time (us) | 16 | 32 | 32 | 44 | 116 | 16 | 32 | 32 | 44 | 116
 | MAC frame Occupancy | 5.02% | 9.55% | 9.55% | 12.68% | 27.68% | 1.67% | 3.28% | 3.28% | 4.45% | 10.94%

## Slide 21: MAC Frame Occupancy Observations and Discussions
The MAC frame occupancy:
  Increases as the media load decreases, due to shorter average backoff time;
  Increases as the Tx rate deceases, due to longer MAC frame time.
Effectiveness of MAC frame size reduction:
  Increases as the MAC frame occupancy increases;
  Becomes important when the MAC frame occupancy is significant, e.g.,
    With 1 Mbps Tx rate and 20% media load, the FD frame occupancy can go up to over 60%, i.e., the majority of the overall frame time is used to transmitting MPDU/MMPDU.
  Becomes trivial when the MAC frame occupancy is low, e.g.,
    With 11 Mbps Tx rate and 50% media load, the MAC frame occupancies of all the considered FD frame sizes are below 5%, i.e., >=95% of overall frame time is used for medium access control and PHY framing.

## Slide 22: MAC Frame Occupancy Observations and Discussions – Con’t
FD frame size reduction is still very important, particularly for the use cases with low Tx rates for FD frame, considering:
  99.93% Beacon Tx at 1 Mbps, based on 11ai contribution 11/1413r2;
  FD frame may accommodate the additional framing overhead of Public Action frame, comparing at Extension frame, particularly, considering:
  11ai functional requirement: Solutions shall demonstrate that they can provide a link set-up for media loads of at least 50%.
  Future development: higher min data rates.
  FD frame size reduction considerations:
  Framing overhead reduction, e.g., using FD frame control field to indicate optional field presences, instead of using information element;
  Compressed content design: 8 to 27 bytes, comparing to 130-byte beacon.

## Slide 23: Comparison Study Summary
FD frame size optimization is still very important, particularly when:
  the transmission rate of FD frame is low;
  Multiple FD frames are transmitted per Beacon Interval (BI); and/or
  Multiple APs on the channel.
Due to the relatively high overheads of medium access control and PHY framing:
  The MAC frame occupancy in overall frame time could be relatively low, particularly, when with a higher Tx rate and/or a higher media load;
  The 19-byte frame size difference between FD frame format options, Public Action frame and Extension frame, does not cause a significant difference in the FD frame WM occupancy.
  The number of FD frames per BI:
    Should be constrained, in order to control the introduced overhead;
    Can be used to implicitly indicate the channel media load.

## Slide 24: Straw Polls about FILS Discovery Frame Format
Straw-Poll-1: Do you support the FILS Discovery frame is designed as a new Public Action frame as shown in slide 7 of this contribution?
Result Yes No Abstain_______________

## Slide 25: Straw Polls about FILS Discovery Frame Format
Straw-Poll-2: Do you support the FILS Discovery frame is designed as a new Extension Action frame as shown in slide 6 of this contribution??
Result Yes No Abstain_______________

## Slide 26
References:
IEEE Std 802.11™-2012
Draft-P802.11ad_D9.0
11-12-0151-13-00ai-proposed-specification-framework-for-tgai
11-11-1137-10-00ah-specification-framework-for-tgah
11-11-1503-02-00ah-short-beacon
11-12-0129-03-00ah-short-beacon
11-11-1031-00-00ai-air-time-consumption-by-beacon-and-probe
11-11-1413-02-00ai-real-air-time-occupation-by-beacon-and-probe
11-12-1029-02-00ai-further-discussion-about-fils-discovery-frame-format
11-12-1130-03-00ai-paasive-scanning-ad-hoc-report
11-12-1148-01-00ai-further-discussions-about-fd-frame-format-design
11-12-1236-00-00ai-spec-text-for-FD-Frame-Definition
11-12-1238-00-00ai-FD-Frame-capability-security-neighbor-info