## Slide 1: Rapid Scanning Procedure
Date: 2012-11-14
Authors:

## Slide 2: Abstract
The presentation describes an improvement to the Active Scanning mechanism to reduce the delay on unused channels during the AP discovery phase.
This presentation will focus on comparing the enhancement of Rapid Scan to Active Scan compared to the current status of only using Active Scan.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | Yes
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Recap, Active Rapid Scanning
Rapid Scanning was presented during the last meeting:
Benefits include:
  Major latency improvement.
  Major power improvement.
  Does not needlessly load channels without 11ai support.
MAC message
Time uncertainty <
Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
Rapid Scan
Request
T
STA performing
Rapid Scan
G1
~230usec
Probe Req
STA performing
Active Scan
G3
Min_Probe_Response_Time
~5.350msec
STA waits 5msec for AP to response than switch to next channel
No response identified STA goes to next channel within < 80usec

## Slide 5: Recap, Active Rapid Scanning
Probe Rsp
Rapid Scanning was presented during the last meeting:
Benefits include:
  Major latency improvement.
  Major power improvement.
  Does not needlessly load channels without 11ai support.
MAC message
Time uncertainty <
Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
Rapid Scan
Request
T
STA performing
Rapid Scan
G1
~230usec
Probe Req
STA performing
Active Scan
G3
Min_Probe_Response_Time
STA waits 10-15msec only to discover non 11ai APs on channel.
No response by non 11ai AP. STA goes to next channel within < 80usec
Probe Rsp
ACK
ACK
Max_Probe_Response_Time

## Slide 6: Recap, Active Rapid Scanning
Concerns raised on the following:
  Creation of a new control message (action frames are too slow to analyze and acknowledge).
  Replying on ACK for a group broadcast address.
We propose to answer these by using an acknowledged existing Probe Request message to achieve same goal of decreased scan duration.

## Slide 7: Using Probe Request for Rapid Scan
By using a OUI and Probe Request
  The OUI indicates a unicast address allocated to indicate FILS capable AP (same as in 11ae).
  The Probe Request message indicates an ACK.
  FILS capable AP acknowledges the Probe Request (non FILS capable AP ignores it).
  STA identifies the ACK frame and continues to decode the medium for at least Min_Probe_Response_time; enabling the receiving of a Probe Response.
  STA acknowledges the Probe Response.
Probe
Req
Probe
Response
ACK
T
STA performing
Rapid Scan
FILS capable
AP # 1
SIFS
T
ACK
Min_Probe_Response_Time
SIFS
MAC message
Time uncertainty <
Min_Probe_Response_Time

## Slide 8: Using Probe Request for Rapid Scan
If a single FILS capable AP operates over the channel:
Probe
Req
Probe
Response
ACK
T
STA performing
Rapid Scan
FILS capable
AP # 1
SIFS
T
ACK
Min_Probe_Response_Time
SIFS
MAC message
Time uncertainty <
Min_Probe_Response_Time

## Slide 9: Using Probe Request for Rapid Scan
If multiple FILS capable APs operates over the channel:
Probe
Req
Probe
Response
ACK
T
STA performing
Rapid Scan
FILS capable
AP # 1
SIFS
T
ACK
Min_Probe_Response_Time
FILS capable
AP # 2
ACK
DIFS
SIFS
Probe
Response
Max_Probe_Response_Time
MAC message
Time uncertainty <
Min_Probe_Response_Time

## Slide 10: Using Probe Request for Rapid Scan
If only non FILS capable APs operates over the channel:
Probe
Req
Non related
MPDU
T
STA performing
Rapid Scan
Non FILS
Capable AP
SIFS
T
DIFS
After SIFS + preamble STA switches to another channel.
MAC message
Time uncertainty <
Min_Probe_Response_Time

## Slide 11: Using Probe Request for Rapid Scan
If no AP operates over the channel:
Probe
Req
T
STA performing
Rapid Scan
Non FILS
Capable AP
SIFS
T
After SIFS + preamble STA switches to another channel.
MAC message
Time uncertainty <
Min_Probe_Response_Time

## Slide 12: Summary
Benefits of using Probe Request/Response for Rapid Scanning:
  Reuse of existing resources and procedures (management message, ACK procedure).
  Fast separation between regular and FILS capable (~1/10-1/20 of current duration).
  Power efficient procedure enables more frequent polling supporting the faster automatic discovery.
References:
  11-12-1261-00-00ai-probe-request-based-rapid-scan-text.docx
  11-12-1033-02-00ai-rapid-scan.pptx
  11-12-1040-01-00ai-rapid-scan-amendment-text.docx

## Slide 13: Motion
Insert the following text on clause 6 of the SFD (11-12/0151r12):
The amendment should define a mechanism to reduce the FILS capable AP presence discovery duration. The procedure will enable the STA to identify FILS capable AP coverage within SIFS plus ACK message delay post request by STA by using decoding an ACK message or using CCA in case of a collision.
Yes:
No:
Abstain:

## Slide 14: Backup

## Slide 15: Rapid Scan using dedicated message
Probe
Response
Multiple APs respond after SIFS and identified by STA’s CCA
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
G1
G3
STA sends a Rapid Scan Request
MAC message
Rapid Scan Ack
Probe Response ACK
Time uncertainty < Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
AP coverage discovery
Existing Active Scan procedure – AP identity discovery
~230usec
~5-10msec

## Slide 16: Rapid Scan using dedicated message
Probe
Response
Multiple APs respond after SIFS and identified by STA’s CCA
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
G1
G3
STA sends a Rapid Scan Request
MAC message
Rapid Scan Ack
Probe Response ACK
Time uncertainty < Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
AP coverage discovery
Existing Active Scan procedure – AP identity discovery
~230usec
~5-10msec

## Slide 17: Dedicated RSR – clear channel case
No response identified STA goes to next channel within ~80usec
Rapid Scan
Request
T
STA performing
Rapid Scan
G1
MAC message
Time uncertainty <
Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
~230usec
Probe Req
STA performing
Active Scan
G3
Min_Probe_Response_Time
~5.350msec
STA waits 5msec for AP to response than switch to next channel

## Slide 18: Dedicated RSR – in case of non 11ai capable APs
No response identified STA goes to next channel within ~80usec with minimal impact on medium
RSR
T
STA performing
Rapid Scan
G1
10usec
~230usec
G1
ACK
Probe
Req
T
STA performing
Rapid Scan
G3
T
T
Probe
Response
Probe
Response
G3
G1
ACK
Min_Probe_Response_Time
Max_Probe_Response_Time = ~10msec
STA takes up substantial medium resource.
Procedure takes 10msec to identify no 11ai support.

## Slide 19: Suggested Improvement – mix of 11ai and non 11ai APs
Probe
Response
Multiple APs respond after SIFS and identified by STA’s CCA
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
G1
G3
STA sends a Rapid Scan Request
MAC message
Rapid Scan Ack
Probe Response ACK
Time uncertainty < Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
AP coverage discovery
Existing Active Scan procedure – AP identity discovery
~230usec
~10msec
~
~
~
~
~
~

## Slide 20: AWGN, Probability of Miss-Detection Fixed timing offsets, without freq-offset
Addition of P2 increases the received power, and hence P-miss curves detection in negative SNR.
When P1 and P2 are completely aligned it has 6dB improvement compared to a single packet
No symmetry is observed among time delays due to addition of noise and existence of non-overlapped 0.8usec STS

## Slide 21: AWGN, Probability of Miss-Detection 0 usec timing, max freq-offset
Combination of time-offset and freq-offset causes performance degradation as expected

## Slide 22: Probability of Miss-Detection AWGN
prob-miss at 10% point (std req) benefits from the additional energy in the 2nd packet
As interference power decreases the negative impact of freq-offset on prob-miss below ~2% diminishes

## Slide 23: Summary
Receive of a 2nd packet with different freq-offset and at different timing does not have any negative impact on 90% (std. req) probability of detection, in fact, it benefits from the additional received energy.
  It decreases the slope of the curve for prob-miss below 2% (or slope of the curve for probability of detection above %98), in particular, when two packets are received at same power level, 0.5 dB performance degradation is observed at 1% prob-miss (vs. the std. 10% req) despite the additional energy of the 2nd packet.