## Slide 1: MLME.SCAN-request
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
HanGyu Cho | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | HanGyu.Cho@lge.com
Date: 2012-11-05
Authors:

## Slide 2: Abstract
This contribution proposes the modifying the MLME.SCAN-Request primitive for supporting the fast active scan.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1, 2

## Slide 4: Motivation (1/3)
Choosing the Wi-Fi channel by APs
  Wi-Fi supports two types of channel selection mechanism.
    Dynamic Channel Assignment
      DCA allows an AP to choose autonomously its channel based on channels utilization at booting time.
      Channel number is not changed if the channel environment is not quite variable.
    Manual channel selection.
      Choosing the specific channel number manually
      Channel is not changed if the network operator does not change the channel number.

## Slide 5: Motivation (2/3)
Channel list of MLME.SCAN-request
  STA may scan the channels of channel list in consecutive order until it finds the desired AP.
    MLME.SCAN-request
      SSID, SSID list, BSSID, Channel list, ProbeDelay, MinChannelTime, MaxChannelTime, etc
If a STA knows the channel number of previously associated AP, the STA can quickly and easily find the AP when the STA tries re-access to the previously associated AP.
Inclusion of the specific channel number is helpful for the STA to discover the preferred AP more quickly

## Slide 6: Proposal
MLME.SCAN-request may include the specific channel number as well as channel list as follows.
  MLME-SCAN.request (
  BSSType, BSSID, SSID, SSID, ScanType, ProbeDelay, Channel number , ChannelList, MinChannelTime, MaxChannelTime, RequestInformation, SSID List, ChannelUsage, AccessNetworkType, HESSID, MeshID, VendorSpecificInfo)
  Channel number specifies the specific channel number of previously associated AP.

## Slide 7: Straw poll
Do you agree inserting the following text on clause 6 of the SFD (11-12/0151r13)?
6.2.11 specific channel selection for AP discovery
The MLME.SCAN-request primitive may include the specific channel number for fast AP discovery.
Yes:
No:
Abstain:

## Slide 8: Motion
    Move to add the following text to Section 6.1.10 of SFD
    6.2.11 specific channel scanning for AP discovery
    The MLME.SCAN-request primitive may include the specific channel number for fast AP discovery.
    Mover:
    Seconder:
    Result
    Yes No Abstain_______________