## Slide 1: TGai FILS Authentication Protocol and State Machine
Name | Affiliations | Address | Phone | email
Robert Sun; | Huawei Technologies Co., Ltd. | Suite 400, 303 Terry Fox Drive, Kanata, Ontario K2K 3J1 | +1-613-2871948 | Rob.sun@huawei.com
Date:
Authors:

## Slide 2: Abstract
Nov 2012
This submission is aiming at providing in depth analysis of the FILS authentication scheme and FILS state machine in respective and also providing the technical ground for proposed texts in 11-12-1282r0

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4: FILS Authentication Design
The desirable FILS authentication design should consider:
  Reusable: possibly most of the existing AKM protocols, cipher suites
  Less impact: on 802.1x and EAP state machine; no need to drastically re-design the WiFi security system.
  Cost effective: easier to implement and no tangible IPR liability.
How to design the FILS authentication scheme
  System level design: How can a system architecture help to make FILS authentication/FILS easier?
  Other relevant performance hog components: ie, DHCP/DNS, remote TTP server. How can we make them fly for FILS?
  Re-authentication vs Initial Authentication: How to make re-authentication design to be compatible with Initial Authentication

## Slide 5: What’s the main contributors of the Delay
Authentication and 4 way handshake are taking too long (in range of 100ms to 1000ms)
  12/041r1 contribution has the detailed performance analysis of 802.11EAP authentication.
  https://mentor.ieee.org/802.11/documents?is_dcn=41&is_group=00ai
  Authentication at some occasions also involves backend systems which adds significantly to the overall delay in BSS.
    Certification reading and verification
    Authentication Key initialization and generation.
    EAP interlock state machine
    Chatty EAP-TLS handshake
IP layer functions taking too long
  802.1x state machine blocks the DHCP and Other IP layer functions till the STA is authenticated.
    Can we do the piggy-back way (i.e piggy-back DHCP over other messages) ?

## Slide 6: FILS System Design
Network A:
  -TTP authentication/Authorization
  -802.1X/EAP based RSNA architecture
Network B:
  -Wall Gardened Architecture for FILS client
  - Routed FILS connectivity within Wall Gardened zone
  -802.1x (EAP is optional, ie. PSK) based RSNA architecture
  - Similar to Guest 802.1x port in implementation.
  Ref: http://www.cisco.com/en/US/docs/solutions/Enterprise/Network_Virtualization/AccContr.pdf
WiFi Host
AP
Authentication Server
Secured Network
WiFi Host
AP
Authentication
Server
Secured Network
DHCP Server
Wall –Gardened
Network
“FILS Link”

## Slide 7: For Network A
Existing IEEE 802.11 components
  802.1X PAE (including state machine and Management Entities, MIB)
  EAP (EAP-TLS, RFC 5216 and RFC 3748) (Only as reference model)
  4-way handshake
    Note: IEEE 802.11ad is reliant on 4-way handshake to delivery information??
Mandates strong WPA/WPA2 security requirements
  Mutual authentication with 4 way handshake (RSNA)
  Link Setup time requirements can not degrade the security property.

## Slide 8: IEEE 802.11 TGai FILS Authentication
Supplicant
AP /
Authenticator
AS
1) 802.11 Beacon
2) 802.11 Probe Request
3) 802.11 Probe Response
4) |802.1x EAP OL-Start with Security Parameters for FILS handshake)
Access Request (EAP Request)
EAPOL-EAP ( EAP Authentication Protocol Exchange)
AS Generates
PMK
Accept/ EAP Success/ PMK
5) msg 1: EAPOL-KEY (Anounce, Unicast))
Supplicant
Generates PMK
EAPOL-Start Triggers the 802.1X PAE
EAPOL-Start TLV carries the NID information (i.e Certificate)
Authenticator
Stores PMK
And Generate
Anounce
Supplicant
Derives PTK
State 1
State 5
State 1
State 5
Remove EAP-ID req/response
RFC 3748 states: EAP-ID Request/Response not necessarily the first message, in section 2
EAPOL-EAP ( EAP Authentication Protocol Exchange)

## Slide 9: IEEE 802.11 TGai FILS Handshake (Revising 802.11Revmb Section 4.10.3.2)
Supplicant
AP /
Authenticator
6) Msg 2: EAPOL-Key (Snounce, Unicastm MIC)
7) Msg 3: EAPOL-Key (Install PTK, unicast, MIC, Encrypt (GTK, IGTK) ))
8) Msg 4: EAPOL-Key (Unicast, MIC)
Secure Data Communication
Supplicant with
PTK
Authenticator with
PTK |GTK|IGTK
Install PTK, GTK
IGTK
Install PTK, GTK
IGTK
State 5
State 4
State 5
State 4

## Slide 10: Protocol Analysis
Pros:
  Keep IEEE 802.11 RSNA architecture (Authentication then Data Communication)
  Omit the IEEE 802.11 open authentication handshake and association handshake. (FILS association is done when the FILS authentication is completed)
  Keep the 4 way handshake intact (No need to evaluate the security property)
  Generally applicable to TTP based authentication and IBSS based authentication.
  No piggyback datagram on Frames (Piggyback datagram on frame is violating the IEEE 802.1x design principles)
  No impact on relevant Standards and implementations
Cons:
  No improvements on EAP-(TLS) multiple rounds of handshake given fragmentation could take place
    EAP based authentication with Remote AAA server still takes significant time
    IP layer functions (DHCP and DNS) is still taking its toll in making FILS authentication slow

## Slide 11: For Network B
Enable the Wall gardened FILS solution
  Enable Virtual Port on IEEE 802.1X PAE on both supplicant and Authenticator to guide the FILS specific authentication scheme into a “Wall Garden” /VLAN.
  Note: Section 12.1 of IEEE 802.1X Rev-d4.
  AP (authenticator) can choose most flexible authentication scheme (PSK, or no authentication) to provide minimum effort in authentication.
  STA and AP can still utilize the 4 way handshake to generate keying materials (PTK, GTK|IGTK) to protect the OTA communication.
  The DHCP / DNS could be arranged locally (on AP or collocating with AP)
    Or using Frame-IP-Address (Radius Attribute 8) to allocate IP address to device during the authentication process
  FILS traffic are contained within the “zone” (with Firewall or other means) which regulates the traffic which is beyond the scope of IEEE 802.11TGai

## Slide 12: What is Virtual Port
As defined in IEEE 802.1X rev d4
  A MAC Service or Internal Sublayer service access point (D.4) that is created on demand. Virtual ports can be used to provide separate secure connectivity associations over the same LAN.
  How to create and delete the Virtual ports on Authenticator’s PAE is based on section 12.7 of IEEE 802.1X.
  Within the virtual port, the FILS station can maintain different security association than “regular” association.

## Slide 13: IEEE 802.11 TGai FILS Authentication with 4 way handshake
Supplicant
AP /
Authenticator
AS
1) 802.11 Beacon
2) 802.11 Probe Request
3) 802.11 Probe Response
4) |802.1x EAP OL-Start with FILS
AP create the Virtual Port on
Receipt of EAPOL-Start
AS Generates
PMK
Authentication Scheme (TBD)
5) msg 1: EAPOL-KEY (Anounce, Unicast))
Supplicant
Generates PMK
Authenticator
Stores PMK
And Generate
Anounce
Supplicant
Derives PTK
State 1
State 5
State 1
State 5
EAPOL-EAP ( EAP Authentication Protocol Exchange)
VLAN ABC
FILS authentication Scheme (TBD)
If enable the Frame-IP-address
on EAP request, then DHCP
Can be omitted

## Slide 14: IEEE 802.11 TGai FILS Handshake (Option 1: With 4 Way handshake))
Supplicant
AP /
Authenticator
6) Msg 2: EAPOL-Key (Snounce, Unicastm MIC)
7) Msg 3: EAPOL-Key (Install PTK, unicast, MIC, Encrypt (GTK, IGTK) ))
8) Msg 4: EAPOL-Key (Unicast, MIC)
Secure Data Communication
Supplicant with
PTK
Authenticator with
PTK |GTK|IGTK
Install PTK, GTK
IGTK
Install PTK, GTK
IGTK
State 5
State 4
State 5
State 4
VLAN ABC

## Slide 15: Protocol Analysis
Utilizing the “Virtual Port” to contain the FILS traffic and regulate on the basis of backend security system design.
Enable separate FILS security association which can separate the FILS state from regular Association
Inheriting the 4 way handshake to make sure the OTA communication is secured
Local Authentication (At the proximity of the AP) which should be faster
Timer or Event triggers the FILS device to do the Full authentication/Full association.

## Slide 16: Modified 802.11 FILS Authentication and Association State Machine
State 1
Unauthenticated,
Unassociated
Class 1 Frames
State 2
Authenticated,
Unassociated
Class 1 & 2 Frames
State 3
Authenticated,
Associated
(Pending RSN Authentication)
Class 1 ,2 & 3 Frames
IEEE 802.1X Controlled Port Blocked
State 4
Authenticated,
Associated
Class 1 ,2 & 3 Frames
IEEE 802.1X Controlled Port
UnBlocked
Successful
802.11 Authentication
Successful
(Re)Association –RSNA Required
4- way Handshake Successful
Deauthentication
Deauthentication
Deassociation
Deauthentication
Unsuccessful
(Re)Association
(Non-AP STA)
Successful
802.11
Authentication
Unsuccessful
(Re)Association
(Non-AP STA)
Disassociation
Successful
802.11 Authentication
Successful
(Re) Association
No RSNA required or
Fast BSS Transitions
State 5
FILS Authenticated
Class 1, 2 &3 Frames
IEEE 802.1x controlled Port
unblocked
Successful FILS
Authentication
FILS
Deauthentication
(Timer or Event)
FILS Key Handshake
Slide 16

## Slide 17: Back Up

## Slide 18: The Security Model of RSNA
Policy
Decision
Point
Policy
Decision
Point
Policy
Enforcement
Point
Policy
Enforcement
Point
STA
AS
AP
Authenticate to derive
MSK
2: Derive PMK from MSK
3: Use PMK to enforce
802.11 channel access
Derive and use PTK
Reference: “IEEE 802.11i Overview”, 2002, Nancy Cam-Winget, et al

## Slide 19: 802.1X-REV/D4.5

## Slide 20: Questions & Comments