## Slide 1: Non-TIM Mode Negotiation
Date: 2012-11-09
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: 802.11ah Power Save Operation Overview
Low power operation mode is introduced as a new power
saving method in 802.11ah specification framework :
802.11ah draft shall define the following operation mode:
  STA may send a PS-Poll at any time
  AP shall respond immediately to a PS Poll with either
    Data for the requesting STA, or
    ACK frame with 1bit-field indicating
      1: traffic is buffered (as indicated in the TIM map), stay awake (i.e. a service period starts)
      0: no traffic is buffered, go back to sleep
      The bit used in current ACK frame format is the More Data field
11ahSTA chooses not to have a TIM entry for the DL traffic signalling when working in Non-TIM mode. For these stations, the AP will store the DL data and deliver it when the STA request it.

## Slide 5: Listen interval
  Listen interval is carried in Association REQ frames. AP may delete BUs using aging function based on listen interval.
    In PS mode, listen interval is used to indicate to AP how often a STA wakes up to listen to Beacon frames.
    In Non-TIM mode, listen interval is the max interval for a STA to send at least one trigger frame(e.g. Ps-Poll) to AP to fetch BUs.

## Slide 6: Low Power Operation Discussion (1)
  Non-TIM operation mode is suitable for sensor-like services since they have low duty cycle and DL data only makes up a very small proportion of the whole traffic. A large number of 802.11ah STAs may select to work in Non-TIM mode.
  In current scheme, listen interval is carried in (Re)association Request frames, which means this parameter is only decided by non-AP STAs
  Two issues should be considered with Non-TIM STAs:
    AP should be able to control the number of STAs working in Non-TIM mode in order to avoid excessive uncontrolled uplink channel access induced contention due to Non-TIM STAs sending unsolicited PS-Poll or trigger frame.
    Too many STAs entering Non-TIM mode will bring challenge to AP’s buffer management capability. The worst case is that AP needs a bigger buffer due to non-TIM STA’s unpredictable sending PS-Polls or trigger frame to fetch data.

## Slide 7: Low Power Operation Discussion (2)
Trade-off between TIM scheme and Non-TIM scheme
  PS mode with TIM scheme enables pre-scheduling with RAW concept, which can spread out PS-POLLs and DL traffics to avoid excessive uncontrolled channel access induced contention and reduce the buffer size needed to store the overall DL traffic.
  Non-TIM PS mode allows STAs to send PS-POLL at any time without listening to the beacon frame, which provides better power save performance.
Therefore, to allow AP to control the number of Non-TIM STAs based on AP’s buffer status by Non-TIM mode negotiation provides a trade-off between STA’s power save performance and AP’s buffer management pressure as well as excessive uncontrolled channel access induced contention.

## Slide 8: Proposed Non-TIM Mode Negotiation (1/2)
  AP and STA inform each other their capability of supporting Non-TIM mode in association procedure with a non-TIM support field in Extended Capabilities element.
  STA carries a “Non-TIM ” indication in Association Request frame to inform AP
  whether it supports Non-TIM mode.
  Upon receiving STA's Association Request frame with Non-TIM indication, AP
  confirms STA whether it allows the STA entering Non-TIM mode in
  Association Response frame.
Bit | Information | Note
 | Non-TIM support | For non-AP STA: 0: STA dose not support Non-TIM mode, it needs TIM entry as in legacy PS mode 1: STA request Non-TIM mode and it does not need TIM entry when in Non-TIM mode For AP: 0: AP does not support STA ‘s Non-TIM mode 1: AP can support STA ‘s Non-TIM mode
Kaiying Lv, ZTE

## Slide 9: Proposed Non-TIM Mode Negotiation (2/2)
  AP may recommend a value of listen interval different from that in Association Request frame based on its buffer management consideration in Association Response frame .
  If a STA is NOT allowed to be in Non-TIM mode through negotiating by association procedure, the STA shall work in TIM mode.

## Slide 10: Pre-motion 1
Do you support the proposed Non-TIM Mode Negotiation as described in slide 8 and 9?
Y
N
A

## Slide 11: Reference
[1] 11-11-1137-10-00ah-specification-framework-for-tgah
[2] 11-12-0127-01-00ah-lowe-power-medium-access