## Slide 1: PS-Poll TXOP Using RTS/CTS Protection
Date: 2012-11-09
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Abstract
In this contribution , we propose a collision avoidance mechanism when AP responses immediately to an unsolicited PS-Poll with buffered data frame to the STA.

## Slide 5: Motivation
In 802.11ah,battery-operated devices benefit from the low power operation.
In [1],A STA may send a PS-Poll at any time. AP shall responds immediately to a PS-Poll with ACK or buffered data frame to the STA.

## Slide 6: Background
According to current STD:
upon receipt of a PS-Poll frame, a STA shall update its NAV settings using a duration value equal to the time, in microseconds, required to transmit one ACK frame plus one SIFS interval.
PS-Poll frames shall be sent using the access category AC_BE (to reduce the likelihood of collision following a Beacon frame) and are exempted from any and all restrictions on transmissions arising from admission control procedures.

## Slide 7: Issue Analysis (1)
AC_BE is not optimized for a low power mode STA sending unsolicited PS-Poll
  The non-TIM STA may wake up and send a PS-Poll at any time. However, if the PS-Poll is sent using the access category AC_BE , it has lower priority to access the medium, which may lead to higher probability of longer backoff delay.
  The STAs are not likely to send unsolicited PS-Polls at the same time, which means less likelihood of collision of PS-Poll transmission. It is not necessary to use the lowest access priority to reduce collisions in this case.
AC_BE is not optimized for TIM STA or pre-scheduled STA since AP can spread out uplink transmissions over a period of time to mitigate the hidden node problem[1]
  AP may assign to each STA/group-of-STA a channel access slot at which the STA is allowed to contend through a Beacon frame
  When requested by a STA, AP may assign to the STA a channel access slot at which the STA is allowed to contend, at association or later through a management frame exchange

## Slide 8: Issue Analysis (2)
11ah has accepted fast UL/DL frame exchange to minimize power consumption
  Speed frame exchange [2]
However, there is a case where AP may send
buffered data immediately after unsolicited
PS-POLL
  Collision may be happened due to
  hidden node’s data transmission
  AP enabled protection may be needed
  avoid to avoid such collisions.

## Slide 9: Proposed scheme(1/2)
A low power mode STA shall use access category of higher priority (e.g. AC_VO ) to send PS-Poll frame.
  AP may inform or negotiate with the STA of the access category for the PS-Poll frames at Beacon frame, association request/response frame or later through a management frame exchange, overwriting the default value.
Upon receiving a PS-Poll,
  If there is buffered traffic ready for transmitting to the STA, AP may send an RTS to reserve the channel. The STA shall respond with CTS to confirm the channel reservation. Then AP starts to send buffered data until no more data or TXOP limit which comes first. The RTS shall be regarded as the immediate acknowledgement to PS-Poll.

## Slide 10: Proposed scheme(2/2)
Based on accepted concept of 2-bit Ack Indication (00: Ack; 01: BA; 10: No Ack; 11:a frame that is not ACK, BA or CTS) in SIG, speed frame exchange with RTS/CTS protection can also be realized by setting proper value of more data field and ResFrm field.

## Slide 11: Pre-motion 1
Do you support the following feature?
A low power mode QoS STA shall use AC_VO to send PS-Poll frame as the default.
Y
N
A

## Slide 12: Pre-motion 2
Do you support the following feature?
  The AP may inform the low-power mode QoS STA of the access category for sending PS-Poll frames at Beacon and Probe Response frames, overwriting the default value.
Y
N
A

## Slide 13: Pre-motion 3
Do you support the following feature?
  The AP and a low power mode QoS STA may negotiate the access category of sending PS-Poll frame through association request/response frame or later through a management frame exchange.
Y
N
A

## Slide 14: Pre-motion 4
  Do you support the following feature?
  Upon receiving a PS-Poll, AP may use RTS/CTS protection scheme to send buffered data until no more data or TXOP limit which comes first. The RTS shall be regarded as the immediate acknowledgement to PS-Poll.
Y
N
A

## Slide 15: References
[1] 11-11-1137-10-00ah-specification-framework-for-tgah.docx
[2] 11-12-0834-00-00ah-speed-frame-exchange