## Slide 1: 1MHz Dup Mode
Date: 2012-11-12
Authors:

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:

## Slide 4: Discussions
In the US, Korea or some other regions, both 1MHz and >=2MHz BSS may be co-located, resulting in OBSS issues.
It is then useful to define a 1MHz Duplicate PPDU format, and transmit it over the whole bandwidth of the wider BSS for OBSS protections.
Here we propose 1MHz Duplication Mode PHY frame format, and leave the detailed protection protocol to MAC discussions.

## Slide 5: 1MHz Duplicate Mode
Similar to legacy duplicate mode in 11n/ac, an 1MHz duplicated PPDU in 2/4/8/16MHz is modulated by repeating preamble and data portions of an 1MHz PPDU in each 1MHz subchannel.
This include duplicating both data PPDU and NDP short packets.
A TBD phase shift factor is multiplied with all tones of each duplicated1MHz subchannel to reduce PAPR.
An example tone map for 1MHz Duplicate PPDU in 2MHz:
-32
31
1MHz (non-zero tones)
-29
-3
1MHz (non-zero tones)
3
29

## Slide 6: 1MHz Non-Dup Waveform in Wider BW
A wider BW device could also transmit an 1MHz non-duplicated PPDU to gain range.
In this case, we prefer that the 1MHz non-dup waveform to be fixed at either upper or lower side of the 2MHz primary channel.
  The 1MHz primary channel is determined and announced by the AP when establishing the BSS.
  Ease the receiver PHY and MAC packet detection and decoding.
  This is similar to 20MHz primary channel in 40MHz BSS in 11n/ac.
For frequency selective transmission [1], 1MHz Non-dup waveform is allowed to be transmitted in the same pre-announced upper or lower side of any allowed 2MHz channel(s).
  Refer to [1] for the details on the frequency selective transmission.

## Slide 7: Pre-Motion-1
Do you agree to define 1MHz duplicate mode in wider bandwidth?
  Preamble and Data portions of 1MHz signal is duplicated in each 1MHz sub-channel of 2MHz/4MHz/8MHz/16MHz.
  Either 1MHz data PPDU or 1MHz NDP may be duplicated.
  Phase shift value in each 1MHz sub-channel for PAPR reduction is TBD

## Slide 8: Pre-Motion - 2
Do you agree with the following change in the spec framework in R.3.1.1.A?
  In 2MHz BSS, 1MHz waveform is only allowed at the lower side.
  In 4/8/16MHz BSS, when primary 2MHz is at lower most of the overall band, then 1MHz is only allowed at upper side of the 2MHz primary channel; when primary 2MHz is at upper most of the overall band, 1MHz is only allowed at lower side of the 2MHz primary channel; when primary 2MHz is in the middle of the overall band, 1MHz waveform position is TBD.
  When establishing a 2/4/8/16MHz BSS, the AP determines and announces the location of 1MHz primary channel located at either upper or lower side of the 2MHz primary channel.
  A 11ah STA that does not participate in the frequency selective transmission protocol shall neither transmit nor be transmitted to, a 1 MHz non-duplicated PPDU on 1MHz subchannels other than the primary 1MHz channel of a 2/4/8/16 MHz BSSs.
  A non-duplicated 1MHz transmission from a STA that participates in the frequency selective transmission protocol in a 4/8/16MHz BSS, shall use the same upper or lower 1MHz subchannel in any of the allowed 2MHz channel(s).

## Slide 9: Motion-1
Move to define 1MHz duplicate mode in wider bandwidth:
  Preamble and Data portions of 1MHz signal is duplicated in each 1MHz sub-channel of 2MHz/4MHz/8MHz/16MHz.
  Either 1MHz data PPDU or 1MHz NDP may be duplicated.
  Phase shift value in each 1MHz sub-channel for PAPR reduction is TBD

## Slide 10: Motion - 2
Move to adopt the following changes in the spec framework in R.3.1.1.A?
  In 2MHz BSS, 1MHz waveform is only allowed at the lower side.
  In 4/8/16MHz BSS, when primary 2MHz is at lower most of the overall band, then 1MHz is only allowed at upper side of the 2MHz primary channel; when primary 2MHz is at upper most of the overall band, 1MHz is only allowed at lower side of the 2MHz primary channel; when primary 2MHz is in the middle of the overall band, 1MHz waveform position is TBD.
  When establishing a 2/4/8/16MHz BSS, the AP determines and announces the location of 1MHz primary channel located at either upper or lower side of the 2MHz primary channel.
  A 11ah STA that does not participate in the frequency selective transmission protocol shall neither transmit nor be transmitted to, a 1 MHz non-duplicated PPDU on 1MHz subchannels other than the primary 1MHz channel of a 2/4/8/16 MHz BSSs.
  A non-duplicated 1MHz transmission from a STA that participates in the frequency selective transmission protocol in a 4/8/16MHz BSS, shall use the same upper or lower 1MHz subchannel in any of the allowed 2MHz channel(s).

## Slide 11: Reference
[1] 11-12-1338-00-00ah-Frequency-Selective-Transmission