## Slide 1: Traveling Pilots
Date: 2012-11-12
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Nihar Jindal | Broadcom |  |  | 
Sameer Vermani | Qualcomm |  |  | 
Tao Tian | Qualcomm |  |  | 
Eldad Perahia | Intel Corp. |  |  | eldad.perahia@intel.com
Shahrnaz Azizi | Intel Corp. |  |  | shahrnaz.azizi@intel.com
Tom Tetzlaff | Intel Corp. |  |  | thomas.a.tetzlaff@intel.com
Thomas Kenney | Intel Corp. |  |  | thomas.j.kenney@intel.com
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Yong Liu | Marvell |  |  | yongliu@marvell.com
Yongho Seok | LG Electronics | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Hangyu Cho | LG Electronics |  |  | 
Vinko Erceg | Broadcom |  |  | verceg@broadcom.com
Jun Zheng | Broadcom |  |  | 

## Slide 2
Authors continued:
Name | Affiliations | Address | Phone | email
Bin Tian | Qualcomm |  |  | 
Eugene Baik | Qualcomm |  |  | 
Lin Yang | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
Richard Van Nee | Qualcomm |  |  | 
Allert Van Zelst | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Minho Cheong | ETRI | 138 Gajeongno, Yuseong-gu, Dajeon, Korea | +82 42 860 5635 | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Hyoungjin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Jaewoo Park | ETRI |  |  | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  |  | Sk-lee@etri.re.kr
Sayantan Choudhury | Nokia | 2054 University Avenue, Suite 600, Berkeley, CA 94704 | +1 510 599 9268 | sayantan.choudhury@nokia.com
Klaus Doppler | Nokia |  |  | 
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | mori.ken1@jp.panasonic.com
Harya Wicaksana | Panasonic |  |  | Harya.Wicaksana@sg.panasonic.com

## Slide 3
Authors continued:

## Slide 4: Problem Definition and Proposed Solution
The 11ah channel model consists of a high Doppler case corresponding to an outdoor reflection from a moving car. The model consists of assigning the 4th path of the SCM channel model a speed of 60kmph
Current 802.11 systems only enable channel estimation at the beginning of the packets during the LTF.
The proposed solution takes the current pilot design (which uses a fixed set of tones and is used for phase tracking) and shifts their location such that all tones are covered, thus enabling a continuous refresh of the initial channel estimation throughout the packet.
Specifically for transmissions with Nsts=1, pilots step on all tones
    Pilot modulation stays the same as fixed pilots
For STBC transmissions with Nsts=2, pilots step on half the tones (even or odd) to prevent total periodicity from becoming too large.
    Pilots stay at one location for 2 symbols
    Pilot modulation for one location in this case is same as the one used in data tones of LTFs (P matrix) for Nsts=2
Specific travel patterns are determined such that pilots are evenly spaced throughout the bandwidth and jump from symbol to symbol such that they cover all locations

## Slide 5: Proposed Design - 32FFT
Proposal for Nsts=1
STBC proposal for Nsts=2 (cover odd tones)
Pilot Idx \ Pattern Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
0 | -2 | -10 | -5 | -13 | -8 | -3 | -11 | -6 | -1 | -9 | -4 | -12 | -7
1 | 12 | 4 | 9 | 1 | 6 | 11 | 3 | 8 | 13 | 5 | 10 | 2 | 7
Pilot Idx \ Pattern Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | -3 | -13 | -9 | -5 | -1 | -11 | -7
1 | 11 | 1 | 5 | 9 | 13 | 3 | 7

## Slide 6: Proposed Design - 64FFT
Proposal for Nsts=1
STBC proposal for Nsts=2 (cover even tones)
Pilot Idx\Pattern Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
0 | -28 | -24 | -20 | -16 | -26 | -22 | -18 | -27 | -23 | -19 | -15 | -25 | -21 | -17
1 | -12 | -8 | -4 | -2 | -14 | -10 | -6 | -11 | -7 | -3 | 1 | -13 | -9 | -5
2 | 4 | 8 | 12 | 16 | 2 | 6 | 10 | 5 | 9 | 13 | 17 | -1 | 3 | 7
3 | 20 | 24 | 28 | 26 | 14 | 18 | 22 | 21 | 25 | 23 | 27 | 11 | 15 | 19
Pilot Idx\Pattern Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | -28 | -24 | -20 | -16 | -26 | -22 | -18
1 | -12 | -8 | -4 | -2 | -14 | -10 | -6
2 | 4 | 8 | 12 | 16 | 2 | 6 | 10
3 | 20 | 24 | 28 | 26 | 14 | 18 | 22

## Slide 7: Proposed Design - 128FFT
Proposal for Nsts=1
STBC proposal for Nsts=2 (cover even tones)
Pilot Idx\Pattern Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
0 | -49 | -41 | -33 | -25 | -17 | -9 | -58 | -50 | -42 | -34 | -26 | -18 | -10 | -2 | -51 | -43 | -35 | -27 | -19
1 | -30 | -22 | -14 | -6 | -55 | -47 | -39 | -31 | -23 | -15 | -7 | -56 | -48 | -40 | -32 | -24 | -16 | -8 | -57
2 | -11 | -3 | -52 | -44 | -36 | -28 | -20 | -12 | -4 | -53 | -45 | -37 | -29 | -21 | -13 | -5 | -54 | -46 | -38
3 | 11 | 19 | 27 | 35 | 43 | 51 | 2 | 10 | 18 | 26 | 34 | 42 | 50 | 58 | 9 | 17 | 25 | 33 | 41
4 | 30 | 38 | 46 | 54 | 5 | 13 | 21 | 29 | 37 | 45 | 53 | 4 | 12 | 20 | 28 | 36 | 44 | 52 | 3
5 | 49 | 57 | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 7 | 15 | 23 | 31 | 39 | 47 | 55 | 6 | 14 | 22
Pilot Idx\Pattern Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | -50 | -44 | -38 | -32 | -26 | -20 | -14 | -8 | -2 | -56
1 | -30 | -24 | -18 | -12 | -6 | -58 | -54 | -48 | -42 | -36
2 | -10 | -4 | -58 | -52 | -46 | -40 | -34 | -28 | -22 | -16
3 | 10 | 16 | 22 | 28 | 34 | 40 | 46 | 52 | 58 | 4
4 | 30 | 36 | 42 | 48 | 54 | 58 | 6 | 12 | 18 | 24
5 | 50 | 56 | 2 | 8 | 14 | 20 | 26 | 32 | 38 | 44

## Slide 8: Proposed Design - 256FFT
Proposal for Nsts=1
STBC proposal for Nsts=2 (cover even tones)
Pattern Idx\ Pilot Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
0 | -122 | -118 | -114 | -110 | -106 | -102 | -98 | -94 | -120 | -116 | -112 | -108 | -104 | -100 | -96 | -92 | -121 | -117 | -113 | -109 | -105 | -101 | -97 | -93 | -119 | -115 | -111 | -107 | -103 | -99 | -95 | -91
1 | -90 | -86 | -82 | -78 | -74 | -70 | -66 | -62 | -88 | -84 | -80 | -76 | -72 | -68 | -64 | -60 | -89 | -85 | -81 | -77 | -73 | -69 | -65 | -61 | -87 | -83 | -79 | -75 | -71 | -67 | -63 | -59
2 | -58 | -54 | -50 | -46 | -42 | -38 | -34 | -30 | -56 | -52 | -48 | -44 | -40 | -36 | -32 | -28 | -57 | -53 | -49 | -45 | -41 | -37 | -33 | -29 | -55 | -51 | -47 | -43 | -39 | -35 | -31 | -27
3 | -26 | -22 | -18 | -14 | -10 | -6 | -2 | 2 | -24 | -20 | -16 | -12 | -8 | -4 | 2 | 4 | -25 | -21 | -17 | -13 | -9 | -5 | -2 | 3 | -23 | -19 | -15 | -11 | -7 | -3 | 2 | 5
4 | 6 | 10 | 14 | 18 | 22 | 26 | 30 | 34 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 7 | 11 | 15 | 19 | 23 | 27 | 31 | 35 | 9 | 13 | 17 | 21 | 25 | 29 | 33 | 37
5 | 38 | 42 | 46 | 50 | 54 | 58 | 62 | 66 | 40 | 44 | 48 | 52 | 56 | 60 | 64 | 68 | 39 | 43 | 47 | 51 | 55 | 59 | 63 | 67 | 41 | 45 | 49 | 53 | 57 | 61 | 65 | 69
6 | 70 | 74 | 78 | 82 | 86 | 90 | 94 | 98 | 72 | 76 | 80 | 84 | 88 | 92 | 96 | 100 | 71 | 75 | 79 | 83 | 87 | 91 | 95 | 99 | 73 | 77 | 81 | 85 | 89 | 93 | 97 | 101
7 | 102 | 106 | 110 | 114 | 118 | 122 | 120 | -120 | 104 | 108 | 112 | 116 | 120 | 122 | -2 | -122 | 103 | 107 | 111 | 115 | 119 | 121 | 2 | -121 | 105 | 109 | 113 | 117 | 121 | 121 | -2 | -121
Pilot Idx\ Pattern Idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
0 | -122 | -118 | -114 | -110 | -106 | -102 | -98 | -94 | -120 | -116 | -112 | -108 | -104 | -100 | -96 | -92
1 | -90 | -86 | -82 | -78 | -74 | -70 | -66 | -62 | -88 | -84 | -80 | -76 | -72 | -68 | -64 | -60
2 | -58 | -54 | -50 | -46 | -42 | -38 | -34 | -30 | -56 | -52 | -48 | -44 | -40 | -36 | -32 | -28
3 | -26 | -22 | -18 | -14 | -10 | -6 | -2 | 2 | -24 | -20 | -16 | -12 | -8 | -4 | 2 | 4
4 | 6 | 10 | 14 | 18 | 22 | 26 | 30 | 34 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36
5 | 38 | 42 | 46 | 50 | 54 | 58 | 62 | 66 | 40 | 44 | 48 | 52 | 56 | 60 | 64 | 68
6 | 70 | 74 | 78 | 82 | 86 | 90 | 94 | 98 | 72 | 76 | 80 | 84 | 88 | 92 | 96 | 100
7 | 102 | 106 | 110 | 114 | 118 | 122 | 120 | -120 | 104 | 108 | 112 | 116 | 120 | 122 | -2 | -122

## Slide 9: Modulation of the Traveling Pilots
For single space time stream, travelling pilots in data field are modulated the same way as fixed pilots in data field (with the exception of boosting by a factor of 1.5 as explained in the next page).
For STBC, the travelling pilots tones across two consecutive data symbols are modulated the same way as the data tones in LTF.

## Slide 10: Further Details
Traveling pilots may be useful in some use cases where both the transmitter and receiver are outdoor and experience medium to high speed traffic nearby. Hence we propose to make them optional and signal their presence in the packet using one Doppler bit that is added to the SIG field.
We further propose to define two separate receive capability bits for traveling pilot support - the first for one space time stream and the second for STBC (2 space time streams)
Pilot boosting – boosting pilot power can improve channel estimation. Boosting by 3dB (multiplying pilot value by sqrt(2)) is almost equivalent to the two LTF which are part of the preamble
  Pilot boosting will cause a fraction of a dB loss in DATA tones SNR but the improvement in channel estimation more than compensates for it (there is 1.4dB gain in PER achieved by increasing the number of LTF from one to two.
  For simplicity of implementation we propose to multiply the pilot values by a factor of 1.5 (3.5dB gain)

## Slide 11: Simulation Results – Pilot Boosting
MCS1, 1MHz and 8MHz SCM Urban Macro, 60 kmph Doppler on 4th path, 0,3,6 dB pilot boost
It can be observed that 3dB captures most of the potential gain from pilot boosting
Results in the following pages use the chosen 1.5 factor

## Slide 12: Simulation Results – Nsts=1
MCS3, SCM Urban Macro, 60 kmph Doppler on 4th path, 3.5 dB pilot boost
Ideal chanest (blue), no channel update (green), update chanest on pilots (red)
Left: 1Mhz, 256B packet. Right: 2 MHz, 512B packet.
Updating chanest on pilot tones allows channel to be tracked and maintains a gap of less than 2 dB relative to ideal chanest update
  3.5 dB pilot boost reduces inherent penalty relative to ideal chanest from 3dbB to 1.6dB

## Slide 13: Cont.
MCS3, SCM Urban Macro, 60 kmph Doppler on 4th path, 3.5 dB pilot boost
Left: 4Mhz, 1500B packet. Right: 8 MHz, 3000B packet.
Updating chanest on pilot tones allows channel to be tracked and maintains a gap of less than 2 dB relative to ideal chanest update
    3.5 dB pilot boost reduces inherent penalty relative to ideal chanest from 3dbB to 1.6dB

## Slide 14: Cont. - STBC Nsts=2
Similar assumptions as with Nsts=1 except that linear interpolation was used to estimate channel on the even (for 1MHz) and odd (for 2MHz) tones

## Slide 15: Cont.
Similar assumptions as with Nsts=1 except that linear interpolation was used to estimate channel on the odd tones

## Slide 16: Straw Poll
Do you support to add a Doppler bit to the 2MHz and 1MHz SIG field tables and to add section 3.7 Traveling pilots with the following content:
  Traveling pilots are an optional feature used to improve channel estimation under high Doppler scenarios
  Support for traveling pilots receive capability shall be indicated by two bits – the first indicating one space time stream and the second STBC with two space time streams
  Add the content in slides 5-9
Y
N
A