## Slide 1: Very Low Energy Paging
Date: 2012-11-12
Authors:

## Slide 4: Introduction (I)
In sensor networks, an important class of applications will have low duty cycle UL and DL traffic, but may have strict latency requirements in receiving DL data
  Respond to alarms with < 1s latency
  100ms latency expected for commands (e.g. gaming or actuators)
STA must check with AP if data is pending at least every ‘max latency’ interval
  Data though may be very sporadic
Regular PS mode (use the short beacon to indicate DL data) is not efficient enough to make 11ah competitive with other technologies
  Short beacon [1] is 560us preamble + (>13B+TIM @ 150Kbps) > 1.5ms
  Moreover, TIM size is not bound and additional fields/IEs can be present, making the frame longer and decoding energy consuming
To be competitive with other technologies, 802.11ah must provide a further optimized protocol for low latency DL traffic

## Slide 5: Introduction (II)
We propose an enhanced paging protocol that uses a short NDP frame as short paging message
  Provides shorter RX time, compared to receiving Beacon or TIM Frame
  Additionally enables the design of energy efficient receivers, optimized for the NDP paging message
    Other technologies use ad-hoc “wakeup receivers” for very low energy operation
    802.11ah has the chance to define a similar mechanism in native form
The protocol can coexist with existing 802.11 power save operation modes and is built on top of existing 802.11ah mechanisms (TWT with synch frame [2])

## Slide 6: Proposal (I)
When requested by a STA, the AP schedules a very short paging message at the target wake time of the STA as the next frame for transmission
    STA may indicate a max period of time after the TWT it will be still accepting the NDP paging message
  If STA receives the message, STA should
    Option1: act as if it received a TIM indicating BUs, i.e. send PS-Poll or trigger frame
    Option2: go read the next (short) beacon and proceed as in regular PS
    Option3: wait for a further poll message from AP after a certain time
The very short paging message is a NDP control frame, including
  A (partial) identifier of the STA being paged
    Same AID may identify multiple STAs (group ID)
  One bit indicating whether there is a BU for the STA
  Synchronization info, e.g. few LSBs of timestamp
  One or more bits indicating if STA need to check the beacon

## Slide 7: Proposal (II)
In regular PS mode, the STA decodes the (short) beacon at least every ‘max latency’ interval
  Short beacon > 1.5ms
In our proposal, the STA skips the beacon and instead decodes the short ‘NDP’
  NDP > 3 times shorter receive time than short beacon
Moreover, if the only paging message at the TWT is a well defined NDP, an optimized receiver can be used at the TWT, instead of the ‘full’ receiver
  PHY receiver optimized to detecting/decoding an NDP frame only
  Very limited operations upon reception: no ‘MAC’
P
Beacon
Optimized
RX ON
560us
Sleep
P
P= Short Paging message
TWT
TBTT
Sleep

## Slide 8: Energy saving computation
Assumptions on regular operation with short beacon
  STA reads a short beacon every X seconds
    Assume there is no BU, but still STA needs to check the beacon to guarantee the latency
  Beacon: 16 Bytes at MCS0 rep2 (1.4ms)
    This is an optimistic length, assuming very short TIM and no optional fields in beacon
Assumptions on operation with short NDP packet
  STA reads short paging message every X seconds
  Short paging message: 560us
Common parameters
  RX power: 100mW
  Sleep power: 10uW
  Clock drift: 20ppm [each side]
  Wakeup: 2.1ms, at 2.4mW [from an actual Zigbee product]

## Slide 9: Energy saving evaluation
Shorter paging frame provides 2.4x power consumption reduction when a 100ms latency is required
  Translates in 2x battery life
  Results are conservative in that the shortest possible length of beacon was used
Moreover, optimized receivers can be designed to further lower the energy consumption

## Slide 10: Proposal (III)
Note: The proposed operation mode is targeted at very low duty cycle data
  We target an operation mode where it is very unlikely that multiple STAs need be paged at the same time
Multiple STAs though can be paged at same or similar times
  Different STAs may be assigned different (nearby) TWTs, or
  Multiple STAs may be assigned same TWT
    A group ID can be defined to page multiple STAs
The proposed mechanism can be seen as an enhancement to the Target Wake Time with Synch frame [2]

## Slide 11: Proposed SFD text
Existing text [2]
R.4.2.E: When requested by a STA, the AP sends a UL synch frame at the slot boundary or the target wake time of the STA, if the channel is idle, to help the STA quickly synch to the medium. (optional to AP and STA) [July 2012 meeting minutes, 11-12/840r0]
  It is recommended that when requested by the STA, the AP sends a Short CTS frame defined in 4.4.2.3 as a synch frame. [12/840r1, September 2012 meeting minutes]
  [Note: Short CTS content is not defined yet]
Proposed additional text
When requested by a STA, the AP schedules a DL synch frame at the slot boundary or the target wake time of the STA as the next frame for transmission
Synch frame is an NDP frame including at least
    A (Partial) identifier of the target STA(s)/group of STAs (# bits TBD)
    BU present (1 bit)
    Partial TSF (# bits TBD)
    Check beacon (# bits TBD)

## Slide 12: Conclusions
DL traffic with stringent latency requirements is an important use case, which can cause significant power consumption due to TIM reception
  11ah is not competitive enough on this front
11ah has the chance to introduce a native support for a very efficient paging mechanism, that also allows for optimized receivers
  Other technologies use dedicated wakeup signals/receivers
We propose a short paging NDP message and a simple paging protocol that is compatible with 802.11 baseline PS and with 802.11ah mechanisms

## Slide 13: Straw polls
Do you support to define a short NDP frame for paging, that includes (at least) the following fields
    A (Partial) identifier of the target STA(s)/group of STAs (# bits TBD)
    BU present (1 bit)
    Partial TSF (# bits TBD)
    Check beacon (# bits TBD)
Do you support to define an optimized paging protocol that uses a short NDP frame as described in slide 11?

## Slide 14: References
[1] TGah SFD document, DCN 11/1137, section 4.4.1.1
[2] TGah SFD document, DCN 11/1137, section R.4.2.E

## Slide 15: Appendix
Considering the case of STA using unsolicited PS-Poll every ‘max latency’ interval
  PIFS+Short_PS_Poll+SIFS+Short_ACK
  Using same parameters as slide 7 [drift not relevant for sending PS-Poll]
  No benefits from the use of unsolicited PS-Poll for low latencies