## Slide 1: PS-Poll TXOP
Date: 2012-11-08
Authors:

## Slide 4: Introduction
STA can send a PS-Poll/trigger frame to poll the data buffered at AP. AP responds with the polled data or ACK.
STA may also have data to send to AP.
  STA contend for the medium again
  STA change its state from PS to Active
Slides [1] proposed an approach for speed frame exchange, which supports downlink and uplink transmission.
In this presentation, we propose to include PS-Poll in the Speed Frame Exchange procedure.

## Slide 5: An Example of Speed Frame Exchange
Station with Uplink Data Only [1] :
SIFS
ACK
DATA
STA wakes from sleep, e.g. at a scheduled wake time
STA returns to sleep since last MoreData from AP is 0
SIFS
ProbeDelay
AP
STA
Wake
ACK
SIFS
STA, with buffered UL traffic, starts transmission with UL DATA instead of PS-POLL.
MoreData=0
RspFrm=00
DATA
MoreData=1
RspFrm=00
MoreData=0
RspFrm=11
MoreData=0
RspFrm=10
MoreData is used to allow responder to correctly set Response Frame bits
Because of MoreData in UL, responder knows that DATA is next

## Slide 6: PS-Poll TXOP
Problem: The first UL data from the STA in PS state
  Collisions cannot be omitted
    PS-Poll / Trigger frame is allowed for the STAs that are not indicated in TIM [2]
PS-Poll can also work as the initial frame well in Speed Frame Exchange
  PS-Poll also has More Data bit in its Frame Control field
  AP can respond with Data or ACK according to the current rule [3]
  PS-Poll does not carry data
STA can choose to send UL Data or PS-Poll to get the buffered data at AP.
ACK
PS-Poll
SIFS
ProbeDelay
AP
STA
Wake
DATA
SIFS
DATA
SIFS

## Slide 7: PS-Poll Format
Release the definition of PS-Poll format
  Allow the AID field to be switched to Duration
Frame Control | Duration/ID | BSSID (RA) | TA | FCS
2 | 2 | 6 | 6 | 4

## Slide 8: Reference
[1] 12/0834r0 Speed Frame Exchange
[2] 12/0127r1 Lowe power medium access
[3] IEEE 802.11-2012

## Slide 9: Straw poll / Pre-motion 1
Do you agree to allow PS-Poll as the first Uplink frame in Speed Frame Exchange?
  Y
  N
  Abs

## Slide 10: Straw poll / Pre-motion 2
Do you agree to change PS-Poll format as in slide 7?
  Y
  N
  Abs