## Slide 1: PS-Poll for Downlink Bufferable Units
Date: 2012-11-12
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Outline
The use of More Data field in MAC header and response frame bits in SIG field for speed frame exchange is presented in [1]
In slide 6 of [1] , a procedure for retrieving downlink bufferable unit (BU) based on PS-Poll is discussed
This is a follow up presentation on that particular procedure
Note that procedure is not new, and is already part of the family of speed frame exchanges

## Slide 5: One Example of Speed Frame Exchange
D
A
MoreData=1
AckInd=00
SIFS
STA wakes
AP
PS-POLL /
DATA
STA
Wake
D
SIFS
MoreData=0
AckInd=10
STA indicates buffered UL DATA
MoreData=0
AckInd=11
SIFS
A
MoreData=0
AckInd=11
SIFS
SIFS
MoreData=0
AckInd=00
AP receives signal that STA completed UL DATA transfers, i.e. MoreData=0; continues TXOP with DL DATA
AP offer to allow STA to complete all UL DATA first
SIFS
D
SIFS
A
MoreData=1
AckInd=00
MoreData=0
AckInd=00
MoreData=1
AckInd=11
AP is done with DL DATA
STA indicates no more UL DATA
A
STA sleeps

## Slide 6: PS-Poll for Downlink BU Procedure
ACK Indication |  | Frame Types
0 | 0 | ACK
0 | 1 | BA
1 | 0 | No Response
1 | 1 | Not ACK, CTS or BA
SIFS
STA wakes from sleep
STA returns to sleep after MoreData=0 from AP
STA waits either ProbeDelay, or EDCA delay after AP-assisted sync frame [2]
AP
PS-POLL/DATA [3]
STA
Wake
DATA
ACK
MoreData=0
AckInd=00
MoreData=1
AckInd=11
ACK
MoreData=0
AckInd=00
SIFS
SIFS
MoreData=0
AckInd=10
STA has no UL DATA
AP uses ACK + SIFS time to retrieve BU for this STA
AP sends ACK with MoreData=1 to indicate DL BU present, and AckInd=11 to indicate to STA frame is sent after ACK+SIFS time. OR, AP may set AckInd=10 to default back to existing receive operation in PS mode
Notes: Slide 6 - Even if AP knows STA is waking, it does not know whether it has DATA or not

## Slide 7: PS-Poll for Downlink BU Procedure
For speed frame exchange, when AP receives More Data set to 0 from a non-AP STA and AP has remaining BU for this STA, the AP may indicate
  More Data to 1, Ack Indication to 11 in ACK, and STA shall stay awake for downlink transmissions from AP after SIFS
  More Data to 1, Ack Indication to 10 in ACK, and STA shall stay awake until AP sends downlink transmissions
  More Data to 0, Ack Indication to 10 in ACK, and STA may go back to sleep

## Slide 8: Conclusion
Compatible with existing receive operation for STAs in PS mode
Compatible with other speed frame exchanges
No separate wake times for polling and data delivery exchanges for power conscious STAs
Simple AP design since there is no need for separate schedules for polling and DATA transmissions

## Slide 9: Straw Poll
Do you support the speed frame exchange for downlink BU procedure in slide 7?
  Yes
  No
  Abstain

## Slide 10: References
[1] E. Wong et al., “Speed Frame Exchange,” IEEE 11-12/834r0
[2] M. Park et al., “AP Assisted Medium Synchronization,” IEEE 11-12/840r0
[3] T. Koskela et al., “802.11ah Channel Access Enhancement,” IEEE 11-12/877r2
[4] IEEE 802.11 REVmb D12.0

## Slide 11: Appendix

## Slide 12: Another Example of Speed Frame Exchange
D + BAR
D
MoreData=1
AckInd=00
SIFS
STA wakes
AP
PS-POLL /
DATA
STA
Wake
D
SIFS
MoreData=0
AckInd=10
STA indicates buffered UL DATA
MoreData=1
AckInd=11
SIFS
D
MoreData=1
AckInd=11
SIFS
SIFS
MoreData=0
AckInd=01
AP receives last UL DATA along with BAR, send BA plus DL DATA in A-MPDU; AP set MoreData=1 to indicate another DL DATA to follow
AP indicates buffered DL DATA, and adopt BA Ack policy
SIFS
D + BAR
SIFS
MoreData=1
AckInd=11
MoreData=0
AckInd=11
MoreData=1
AckInd=11
BA
AP is done with DL DATA, also sends BAR in A-MPDU
STA indicates no more UL DATA
STA sleeps
D + BA
STA sends buffered UL DATA, and adopt BA Ack policy for its transmissions

## Slide 13: Error Recovery
Why not PIFS after first downlink ACK?
Because a transmission failure may cause TXOP holder or RD initiator to start a PIFS recovery [4]
A transmission failure is defined as,
  No PHY-RXSTART.indication after a SIFSTime + aSlotTime + aPHY-RX-START-Delay,
  PHY-RXSTART.indication occurs but invalid frame after PHY-RXEND.indication
PIFS recovery can starts from,
  SIFSTime + aSlotTime + aPHY-RX-START-Delay
  PHY-RXEND.indication

## Slide 14: Error Recovery
PIFS
AP
PS-POLL/DATA [3]
STA
(TXOP holder/RD initiator)
DATA
ACK
RETRY
SIFS
PHY-RXEND.indication indicates transmission failure, and starts PIFS recovery
PHY-RXSTART.indication triggered
ACK is sent
PHY-RXSTART Triggered
PIFS
AP
PS-POLL/DATA [3]
STA
(TXOP holder/RD initiator)
DATA
ACK
RETRY
SIFS + SlotTime + aPHY-RX-START-Delay timeout indicates transmission failure, and STA starts PIFS recovery
ACK is sent but not heard by STA
No PHY-RXSTART
SIFS
PIFS

## Slide 15: Example of STA Regaining TXOP Entry
SIFS
MoreData=1
AckInd=01
D + BAR
SIFS
SIFS
STA wakes
AP
PS-POLL /
DATA
STA
Wake
D
A
MoreData=1
AckInd=11
BA
MoreData=0
AckInd=00
SIFS
MoreData=1
AckInd=11
STA has no UL DATA
MoreData=1
AckInd=11
SIFS
D
MoreData=1
AckInd=11
D
MoreData=1
AckInd=11
SIFS
SIFS
D
MoreData=1
AckInd=11
AP sends BAR, and gives STA an opportunity for TXOP entry
STA signals to regain TXOP entry with MoreData=1
This allows AP to set the appropriate AckInd bits for next uplink DATA