## Slide 1: Two-Hop Relay Function
Date: 2012-11-12
Authors:
Eric Wong, Broadcom

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Outline
Support for longer range in TGah has increased PPDU duration, and higher power consumption for STAs at the edge of BSS coverage
STAs (e.g. smart meters) have limited battery lifetime, and long replacement cycle
Location of STAs may have exceeded the coverage of AP, and requires additional network elements for range extension
Use of relays are considered for this problem
Consider relay on wall-powered and assume outdoor device-to-device path loss between relay and STA

## Slide 5: Problem
Servings STAs with same traffic load but poorer link budget reduces power efficiency
Particularly STAs at the edge of BSS coverage have limited MCS headroom, are prone to suffer from hidden nodes and OBSS, and are constrained on battery lifetime
STAs may be located outside AP coverage
Proposed use of relays for these STAs
Side effects of introducing relays in the network
  More contentions for channel access, i.e. effectively more STAs
  Contention between frames with same payload, i.e. source TX and relay TX
  Increased interference within home and neighboring BSS
  Complexity for relay path setup and teardown
  Require buffer management at the relays
  Increase in latency for data delivery

## Slide 6: Scenario 1
Relay positioned equal distance between AP and STA
Two paths available – Direct and Relay
Comparing to the direct path, path via relay needs more frames with shorter PPDU duration for the same number of bytes
Require separate channel access for next frame transmission over the relay-STA hop
A shorter TX-RX cycle via the relay path allows STA to operate with lesser power consumption
If STA falls outside AP coverage, there is no direct STA-AP path
STA
AP
Relay
U1
V1
V2

## Slide 7: Typical Uplink Transfer
Transmission may be hidden from other STAs
Transmission may be hidden from other STAs
SIFS
TA(U1)
TD(V1)
TA(V1)
TD(V2)
TA(V2)
TD(U1)
DATA
ACK
AP
STA
DATA
ACK
AP
STA
RELAY
DATA
ACK
Via Direct Path
Via Relay Path
Extra access delay
AckInd=00
AckInd=10
AckInd=00
AckInd=00
AckInd=10
AckInd=10
SIFS
SIFS

## Slide 8: Scenario 2
Relay positioned closer to STA than AP
STA proximity to Relay permits the use of higher MCS and consumes lesser power for hop V1
Relay requires separate channel access for next hop
Relay may be another sensor on wall-power, and path loss is outdoor device-device
STA
AP
Relay
U1
V1
V2

## Slide 9: Scenario 3
Relay positioned closer to AP and away from STA
Relay path may be suboptimal than direct path
  relay selection = path selection
If Relay is another sensor and STA-Relay hop is outdoor device-device path loss, then Relay may not be reachable by STA with the same MCSs
STA
AP
Relay
U1
V1
V2

## Slide 10: More Discussion
STA
AP
Relay
U1 (Outdoor Macro)
V1 (Outdoor Dev-Dev)
V2 (Outdoor Macro)
Suppose STA-Relay-AP are arranged in a straight line, and STA sends one uplink DATA (see slide - Uplink with Explicit ACK)
Total Medium Time,
PPDU(V1) + ACK(V1) + PPDU(V2) + ACK(V2) + 3 x SIFS
STA ON Time,
PPDU(V1) + ACK(V1) + SIFS
STA-Relay Factor,
Distance (U1)
Distance (V1)

## Slide 11: Total Medium Time for 1 Frame (200 bytes)

## Slide 12: STA ON Time for 1 Frame (200 bytes)

## Slide 13: STA ON Time Change for 1 Frame (200 bytes)

## Slide 14: Total Medium Time for 1 Frame (1400 bytes)

## Slide 15: STA ON Time for 1 Frame (1400 bytes)

## Slide 16: STA ON Time Change for 1 Frame (1400 bytes)

## Slide 17: Proposed Solution
Propose a bi-directional two-hop MAC relay function
  Route management is simpler, no forwarding tables at relays
  Multi-hop requires multiple use of the channel for each DATA frame
  Multi-hop path requires path maintenance management
Propose shared TXOP for relay
  Reduces number of contentions for channel access
Need buffer management at the relay
  Relay UL TX might fail, so relay needs to buffer MPDU for retry attempt because it already ACK’ed to the originator (see timing diagrams)
Use Probe Request for relay discovery
  Include information in PREQ on AP-STA link budget (if available) to allow reduced response

## Slide 18: Relay Discovery
Consider use of Probe Request for relay discovery
STA initiates the discovery process and decides the requirements for relaying, and sends information on U1 (if available) plus additional link requirement
Relay knows the link quality of V1 and V2, and along with requirements from STA, a relay can decide whether it is a relay candidate for this STA
Only eligible relays that meet the link budget requirements will respond to this STA, which is similar in concept to the inclusion and exclusion lists defined for Probe Response criteria defined in TGai [1]
STA selects a relay based on the Probe Responses received

## Slide 19: Downlink with Explicit ACK
AckInd=11
Relay sends ACK, and set Ack Indication bits to 11 for next outgoing frame
DATA
TD(V1)
TD(V2)
TA(V2)
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
AckInd=00
AckInd=00
AckInd=10
AP sends downlink DATA frame with Ack Indication bits set to 00 to relay
After receipt of ACK, AP removes frame from buffer, and defers MAX_PPDU + ACK + 2*SIFS before next event
ACK
SIFS
TA(V1)
In SIFS time, relay sends DATA with a different MCS and Ack Indication bits set to 00. Relay buffers frame until successful delivery or reaching of retry limit

## Slide 20: Uplink with Explicit ACK
AckInd=11
Relay sends ACK, and set Ack Indication bits to 11 for next outgoing frame
DATA
TD(V2)
TD(V1)
TA(V1)
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
AckInd=00
AckInd=00
AckInd=10
STA sends uplink DATA frame with Ack Indication bits set to 00 to relay
After receipt of ACK, STA removes frame from buffer, and defers MAX_PPDU + ACK + 2*SIFS before next event
ACK
SIFS
TA(V2)
In SIFS time, relay sends DATA with a different MCS and Ack Indication bits set to 00. Relay buffers frame until successful delivery or reaching of retry limit

## Slide 21: Buffer Management at Relay
Channel conditions may cause frames to be continuously buffered at the relay, and subsequently leading to an queue overflow
Source node is unaware of the downstream congestion, and continues to forward frames to the relay
Retransmission at the cost of MAC efficiency is undesirable
For example, use the relay can use a bit in MAC header to signal the source node to stop, and restart after some timeout

## Slide 22: Conclusion
Proposed a bidirectional two-hop MAC relay function
  Reduce power consumption on STA with battery constraints, and limited MCS range
  Sharing one TXOP for relay and reduces the number of contentions for channel access
  Address buffer overflow at relay with a flow control mechanism at the relay
  Use Probe request for relay discovery and include information on AP-STA link budget (if available) to reduce number of responses

## Slide 23: Straw Poll 1
  Do you support a simple bidirectional relay that is limited to two hops only?
  Yes
  No
  Abstain
Eric Wong, Broadcom

## Slide 24: Straw Poll 2
Do you support the concept of sharing one TXOP for relay (for explicit ACK exchange) to reduce the number of channel contentions?
  Yes
  No
  Abstain
Eric Wong, Broadcom

## Slide 25: Straw Poll 3
Do you support a flow control mechanism at the relay?
  Yes
  No
  Abstain

## Slide 26: Straw Poll 4
Do you support to use Probe Request for Relay discovery, and optionally include information on AP-STA link budget?
  The STA initiates the discovery process
  The STA selects a relay based on the Probe Responses received
  Yes
  No
  Abstain

## Slide 27: References
[1] J. Kneckt et al., “Response Criteria for Probe Response,” IEEE 11/12-553r4
[2] IEEE 802.11 REVmb D12.0