## Slide 1: Discussions On Usage Models for Portable and Mobile Devices
Date: 2012-10-23
Authors/contributor:

## Slide 2: Category 8: Portable Device Applications
Peer-to-Peer Communication Between Portable Devices
Rapid Download of Mass Data from Fixed Station (e.g. Kiosk)
Cloud Computing / Storage & Mass Data Synchronization
Wireless Peripheral Application (e.g. HD Display , printer, etc.)
Current descriptions of portable and mobile device applications do not reflect the form factor limitations of different device types
  The limitation in return affects design
  Do such limitations need to be considered in the functional requirements?

## Slide 3
Diversity of Portable and Mobile Devices
Portable and mobile devices come in various sizes and capabilities
  Category I: Laptops (notebook, ultrabook, etc.), Tablets (iPad, Kindle fire, Android tablets, Windows Surface, etc.)
  Category II: Smart Phones, iPod, etc.
Definition of Portable and Mobile devices currently in 802.11-2012
  Portable station (STA): A STA that might be moved from location to location, but that only uses network communications while at a fixed location.
    At these fixed locations, a portable device may have access to power.
    In general, a portable STA has a bigger battery and may be plugged in.
  Mobile station (STA): A STA that uses network communications while in motion.
    In general, a mobile STA has a smaller capacity battery and is smaller to fit the hand-held usage model.
Such definitions do not fully reflect the design requirements and challenges in mmWave specification.

## Slide 4
Form Factors that Affect 60GHz Design
Antenna array size is limited by device size
    Category I Devices: up to 16 antennas?
    Category II Devices: up to 4 antennas?
Battery capacity is limited by device size too
  Category I Devices are generally equipped with large battery cell
    Power consumption may be up to 50 watt
  Category II Devices are generally equipped with small battery cell
    Power consumption maybe limited to a few hundreds mW
Overall, device size has a great impact on
    link margin, throughput, cost and power consumption

## Slide 5
Recommendations
Add throughput or range limitations based on form factors of the portable and mobile devices.