## Slide 1: Dynamic TIM and Page Segmentation
Date: 2012-11-12
Authors:

## Slide 2: Abstract
The draft specification shall use a fixed length page segment per TIM segment within one DTIM beacon interval [3].
In [3], the number of blocks in each segment is fixed regardless of the amount of corresponding buffered units at AP.
  However, in some cases, it is better to let the AP adaptively determine the length of each segment by itself as desired to achieve better performance, e.g., in terms of power saving and load distribution.
  We emphasize the necessity of dynamic TIM segmentation and propose possible solutions for dynamic TIM segmentation.

## Slide 3: Introduction
In IEEE 802.11ah spec framework, the complete traffic indication bitmap shall be divided into one or more segments and transmitting in one or more TIM elements for a large network [1].
Based on the hierarchical structure of TIM [2], a page consists of multiple blocks (e.g., 32), and a page segment may refer to an ordered range of blocks (e.g., 8) out of all blocks in one Page.
The spec framework adopted a fixed length page segment per TIM segment within one DTIM beacon interval [3], which we refer to as fixed length TIM segmentation.

## Slide 4: Introduction
Fixed length TIM Segmentation proposed in [3]
  Fixed length page segment per TIM segment within one DTIM beacon interval
  Segment count IE is used to indicate assignment of STAs in TIM segments which is conveyed by DTIM beacon frame.
  Length of each page segment = (number of blocks in page bitmap / page segment count)
  STAs within the assigned TIM segment wake up at corresponding TIM segment sequentially.
  Segment count IE format:

## Slide 5: Introduction
Fixed length TIM segmentation proposed in [3]
  E.g. one page (32 blocks) are divided into 4 equal length (8 blocks) of page segments.

## Slide 6: Motivation
Deficiency of fixed length TIM segmentation
  E.g., 24 blocks divided into 4 equal length page segments.
    In order to receive the red circled downlink transmissions, corresponding stations in page segment 1 may maintain awake state until they successfully receive buffered units, which could incur power waste or extended delay.

## Slide 7: Motivation
Because the AP knows the amount of buffered units corresponding to each block and the available time for downlink transmission dedicated to each TIM segment, it can estimate the proper length of each page segment.
Fixed length TIM segmentation may restrict the AP’s resource scheduling capability.
  AP cannot arbitrarily determine the boundary of each page segment.
  It is desirable to have a dynamic TIM segmentation method, whereby the AP can arbitrarily determine the boundary of each TIM segment.
   Propose dynamic TIM segmentation
    E.g., AP can arbitrarily determine the value of N1, N2, N3 and N4 , as long as the sum of N1, N2, N3 and N4 equals to the number of blocks in one page.

## Slide 8: Dynamic TIM Segmentation
Dynamic TIM segmentation:
  Each page segment can have arbitrary number of blocks based on a proper scheduling strategy of the AP.
  E.g., the 24 blocks are divided into 4 different length of page segments to achieve proper downlink traffic distribution over multiple beacon intervals according to the available time for downlink transmission within a DTIM interval.

## Slide 9: Dynamic Segment Count IE in Beacon
Dynamic segment count IE is only transmitted in DTIM beacon.
This element indicates the length of each page segment and the assignment of STAs in each page segment.
  Indicates wake-up time for power save STAs within one DTIM interval.
The operation of the STA is the same as that of fixed length TIM segmentation

## Slide 10: Discussion on Dynamic Segment Count IE Format (1)
Option 1: The dynamic segment count IE (3-11 octets) might consist of the following fields:
E.g., Page Bitmap and Segmentation Bitmap (24 blocks divided into 4 page segments)

## Slide 11: Discussion on Dynamic Segment Count IE Format (2)
Option 1:
  Element ID (1 octet): Identification of the dynamic segment count IE
  Length (1 octet): Length of this IE
  Page Index (2 bits): Indication of page currently assigned in beacon
  Page Offset (5 bits): Field for indicating the first block in assigned page segments
  Reserved (1 bit): Reserved bits for future use
  Page Bitmap (0-4 octets): Field for indicating the buffered status of each block
  Segmentation Bitmap (0-4 octets): Field for indicating the start and end of each segment
    Each bit can be mapped to corresponding bit in page bitmap
    Bit transition means the beginning of a new segment
    Number of segments = number of bit transition + 1

## Slide 12: Discussion on Dynamic Segment Count IE Format (3)
Option 2: The dynamic segment count IE (3-11 octets) might consist of the following fields:
E.g., Page Bitmap (24 blocks divided into 4 page segments)

## Slide 13: Discussion on Dynamic Segment Count IE Format (4)
Option 2:
  Element ID (1 octet): Identification of the dynamic segment count IE
  Length (1 octet): Length of this IE
  Page Index (2 bits): Indication of page currently assigned in beacon
  Page Offset (5 bits): Field for indicating the first block in assigned page segments
  Reserved (1 bit): Reserved bits for future use
  Page Bitmap (0- 8 octets): Field for indicating the buffered status of each block, as well as the start and end of each page segment
    Block TI (Traffic Indication) (2 bits)
      (0, 0): No buffered data and belongs to the same segment with previous block
      (0, 1): Has buffered data and shall be the start of a new segment,
      (1, 0): Has buffered data and belongs to the same segment with previous block
      (1, 1): Reserved
    Number of segments = Number of (0, 1) in page bitmap

## Slide 14: Summary
  We identified the limitation of fixed length TIM segmentation and emphasized the necessity of dynamic TIM segmentation, which can let the AP assign arbitrary number of blocks in each TIM segment based on some reasonable criteria (e.g., the amount of buffered traffic of each block).
We discussed the dynamic segment count IE for the dynamic segmentation to make each page segment have an arbitrary length.

## Slide 15: Reference
[1] TGah TIM Operation, doc. IEEE 802.11-12/117r0
[2]TGah Efficient TIM Encoding, doc. IEEE 802.11-12/388r0
[3] TGah TIM and Page Segmentation, doc. IEEE 802.11-12/1084r4

## Slide 16: Straw Poll 1
Do you agree to include the dynamic TIM segmentation concept as an option of TIM segmentation method in the TGah spec framework?

## Slide 17: Straw Poll 2
Do you agree to include the dynamic segment count IE in DTIM beacons as a solution of dynamic TIM segmentation method in the TGah spec framework?