## Slide 1: Problem list for P802.1Qbz / P802.11ak point-to-point model
Date: 2013-01-15
Authors:

## Slide 2: Abstract
A list of issues and some solutions for P802.1Qbz and P802.11ak to solve, assuming that we proceed with the point-to-point model for bridging 802.11 wireless media using 802.1 techniques.

## Slide 3: Introduction
This presentation is also available at:
This presentation is also available at: http://www.ieee802.org/1/files/public/docs2012/bz-nfinn-pt-to-pt-problem-list-1112-v03.pdf
There are a number of issues that need to be solved when integrating IEEE 802.11 media into the core of the network. Some are of concern primarily to P801.Qbz, and some concern primarily 802.11ak. Some may be solved by either project.
This deck concentrates on problems that (this author thinks) could be solved by P802.11ak. (Whether the eventual solution will be in P802.1Qbz, P802.11ak, or not specified.)
There are often many possible ways to solve each problem.
This deck primarily concentrates on the problem statement, not the solution.
This deck assumes the use of the point-to-point model for 802.11 integration into the network, not the emulated LAN model. Elements of the emulated bridge model will probably be required to solve some problems.

## Slide 4: Set of point-to-point links
The Access Points and their co-resident bridging functions become integrated AP bridges (AP/Bs).
Devices with non-AP station capability(ies) and wired connections become “non-AP station bridges” (S).
Of course, not all stations are bridges. (The diamonds are non-bridge non-AP stations.)
Each wireless connection appears, to the bridge functions of the system, to be a separate instance of the MAC service.
AP/B1
AP/B2
S
S
S

## Slide 5: 802.1AC PAR REQUIRED

## Slide 6: MAC service instances
In terms of data forwarding, an 802.1Q bridge is a Relay Function attached to some number of Ports, with each Port offering an instance of the MAC service.
Port
…
Port
Port
Port
Relay Function

## Slide 7: MAC service instances
A Port can be expanded into:
  The media-independent functions;
  The media-dependent convergence functions; and
  The media-dependent functions, that vary according to the medium.
media independent functions
Port
media dependent functions
media dependent convergence functions
ISS

## Slide 8: MAC service instances
The demarcation between 802.1Q and a specific medium is a MAC Service Access Point (MSAP) offering the Intermediate Sublayer Service (ISS), defined in 802.1AC-2012.
802.1Q
802.n
802.1AC
media independent functions
Port
media dependent functions
media dependent convergence functions
ISS
802.1AC

## Slide 9: 802.11 ARCHITECTURE ISSUES

## Slide 10: IEEE Std 802.1Q-2011 Figure 8-2

## Slide 11: IEEE Std 802.11-2011 Figure 5-1

## Slide 12: Architecture
802.11-2012 Figure 5-1 seems to be largely compatible with the corresponding 802.1Q-2012 Figure 8-2.
The only real differences, at least at the diagram level, seem to be that:
  The 802.1Q “Media Access Method Independent” and “Media Access Method Dependent Convergence” functions are in the place occupied, in 802.11, by an optional “IEEE 802.1X Controlled Port Filtering” function and a blank box.
  The Bridge model seems to require replicating frames to separate ports, rather than sending one copy to multiple “ports”.
  A similar .1X CPF is also placed above the LLC in the 802.11 diagram.
The “Higher Layer Entities” in 802.1Q are not present in 802.11 because the 802.11 diagram is limited to the data plane.

## Slide 13: Architecture
Apparently, the differences regarding 802.1X filtering is merely a matter of representing the controlled and uncontrolled ports described in IEEE 802.1AE-2006. These differences do not appear to be a problem at this point.
Apparently, the individual ports in 802.11 Figure 5-1 each represent a connection to a separate non-AP station. If this is true, it represents exactly the “point to point model”.
If we apply 802.11-2012 Figure 5-1 to both Access Point stations and non-AP stations, it should not be difficult to reconcile the current 802.11 and 802.1Q standards with the point-to-point model.

## Slide 14: But …
Objections have been raised in 802.11 TGak meetings that 802.11 Fig 5-1 is not meant as a parallel to 802.1Q Fig 8-2, the “baggy pants” diagram.
To achieve the goals of the two Working Groups PARs, this author believes that, if 5-1 was not intended to be a baggy pants diagram, it must become so.

## Slide 15: Non-AP station bridges

## Slide 16: Non-AP Station / Bridges
Similarly, a station/bridge must have baggy pants diagram architecture.
This, however, is easier. A standard bridge will be perfectly able to use a non-AP station as a port just like any wired port, as long as the reflection problem (Station subset problem #1) is solved.
A non-AP station with N > 1 associations, one to its AP, and N-1 other non-AP stations, must present N instances of the MAC service to the Bridge relay function, one instance for each association, to be used by N Bridge ports.

## Slide 17: Station subset problem #1

## Slide 18: Reflected frames: normal non-AP use
A non-AP station uses its own MAC address as both the Ethernet source address and the transmitter address. The AP uses the Ethernet destination as the receiver address. Hence, three addresses are sufficient for both directions.
A broadcast UP frame (non-AP station to AP):
A broadcast DOWN frame (AP to non-AP station):
If the station sees its own MAC address in the Ether Source, it discards the frame, else it passes it up to its MAC client.
Receiver (AP)
Ether Dest. (broadcast)
rest of frame
Ether Src. / Xmitter
Receiver/Ether Dest. (broadcast)
Ether Src.
rest of frame
Xmitter (AP)

## Slide 19: Problem set-up
Imagine a network where the AP, stations, and bridges are all running either the Spanning Tree Protocol or Shortest Path Bridging.
Imagine a station X attached to bridge X, transmits a broadcast frame.
Suppose that bridge “B” is a laptop with a Wi-Fi station and two 802.3 ports, and that we turn on a standard 802.1Q bridging function implemented in software.
AP
B
X
A
(blocked)

## Slide 20: Reflected frames: the problem for bridges
CASE 1: Suppose a non-AP station/bridge B is forwarding data for attached wired device X.
Suppose X sends a frame (a broadcast, for example) up through bridge B.
Rec. = AP
Dest. = FFs.
rest of frame
Src. / Xmit = X
AP
B
X
A
(blocked)
CASE 1

## Slide 21: Reflected frames: the problem for bridges
In a wired network, the Bridge replacing the AP would not reflect the frame back down to Bridge B.
In a Wi-Fi world, the AP does reflect the frame back down to all of the AP’s stations, including X, and Bridge B needs to discard the frame. (Its portion of the network has already seen it.)
Rec./Dest. = FFs
Xmt = AP
rest of frame
Src. = X
AP
A
(blocked)
CASE 1
discard
B
X
X

## Slide 22: Reflected frames: the problem for bridges
CASE 2: Suppose instead, that the spanning tree has changed, so that X has effectively moved, and transmits that same broadcast frame.
The Access Point transmits the broadcast to all of its stations, including bridge B.
AP
A
(blocked)
CASE 2
Rec./Dest. = FFs
Xmt = AP
rest of frame
Src. = X
B
X

## Slide 23: Reflected frames: the problem for bridges
Bridge B must relay the frame down to the part of the network that hasn’t seen it, yet.
AP
A
(blocked)
CASE 2
relay
Rec./Dest. = FFs
Xmt = AP
rest of frame
Src. = X
B
X

## Slide 24: Reflected frames: the problem for bridges
The problem is that, today, Case 1 and Case 2 result in exactly the same frame sent from the AP to bridge B.
Bridge B dosn’t know whether to discard the frame (the correct action in Case 1) or to forward it and learn X’s new location (the correct action in Case 2); it cannot distinguish the two cases.
AP
B
A
(blocked)
CASE 2?
relay?
Rec./Dest. = FFs
Xmt = AP
Src. = X
rest of frame
AP
B
A
(blocked)
CASE 1?
discard?
X
X
X

## Slide 25: Two non-solutions
Question: Why can’t the bridge just discard frames based on the MAC addresses that it knows are “behind” it.
Answer: If there were no wired connections below the bridge/stations, or closing the loop between the bridge/station and the AP, that would be possible. (It is, in fact, done today in a non-standard but common behavior.) But, in the general case, it is only through learning source addresses that the bridge “knows” anything about what is or is not behind it. The problem, here, is that there is nothing in the frame to tell the bridge whether to apply its already-learned knowledge or to learn new knowledge to apply, later.

## Slide 26: Two non-solutions
Question: Why can’t the bridge just remember what frames were sent to the AP and discard them if and when they come back?
Answer: Frames have different priorities. If the frame were reflected simultaneously with transmission (as in the original Fat Yellow Coax), the device could discard it easily. But, there can be an arbitrary time delay between the UP frame and the reflection. The bridge would have to store all UP frames in a content-addressable memory and look for matches. Not only is this very expensive, but frames can be lost, and duplicate frames can be legitimately sent, which further confuses this plan.

## Slide 27: Additional constraints on any solution
Flooded unicasts: It is not only frames with multicast or the broadcast addresses that may be reflected back down by the AP, or sent to all bridges by the AP. The AP must distribute frames sent to unicast addresses that are unknown to it to all station/bridges, but the station/bridge that sent it up to the AP (if any – maybe it came through the wire to the AP) must know to discard it.
Old stations: We must know what existing non-AP stations will do with any new frame formats used. If one AP transmission can suffice for frame to be accepted or discarded by both the appropriate non-bridge stations and the appropriate bridge stations, that would be ideal. If two transmissions (in different formats) are required of the AP, we must be certain that existing stations, new simple stations, and new station/bridges, all will each pass only one of the frames to their respective MAC clients.

## Slide 28: Station subset problem #2

## Slide 29: Multicast distribution
Each device below is a bridge, wireless connections are treated as point-to-point links, and a broadcast frame is sent by bridge X.
Suppose bridge R is the spanning tree root, so that one of the AP’s “ports” is blocked.
In the standard spanning tree protocol, bridge C does not know that the AP’s link to it is blocked.
How does the AP forward the broadcast to A and B, but not to C, with a single transmission?
There are potential solutions to this problem in both the 802.1 and 802.11 spaces; there are tradeoffs to be explored.
AP/B
A
B
(blocked port)
Root bridge
C
R
X

## Slide 30: Multicast distribution
One solution would be to extend/modify MSTP and Shortest Path Bridging in P802.1Qbz to provide a handshake for bridge C to tell the AP/bridge that it knows the AP end of the link is blocked, so it is OK for the AP to send it to all; bridge C will discard it.
A parallel solution is to send multiple unicasts to the bridges, at least until the handshake (if any) is done.
A complete solution would be to provision a set of multicast Receive Addresses, in frames sent by the AP, to specify sets of bridge / stations. (In this case, “A and B but not C”.)
  This latter idea has its own problems – there are 2N possible sets of destinations.
  Perhaps we limit an AP to at most 24 bridge/stations (the number of bits available following the OUI in a MAC address), or define a protocol for distributing a mapping of vectors of stations to 24-bit IDs.
Hopefully, someone has a better idea than any of the above.

## Slide 31: Station subset problem #3

## Slide 32: 802.1Q egress tagging
Note that it is the “Media Access Method Independent Functions (6.9)” that interpret an incoming VLAN tag or generate an outgoing tag on a given port; this is outside the relay function, in the location in the 802.11 diagram occupied by an empty box.

## Slide 33: 802.1Q egress tagging
Whether a frame is tagged or not tagged on certain “ports” == “associations with other stations” certainly affects whether a given frame can be multicast to multiple stations or not, or to which stations it is to be multicast.
It will take further discussion to resolve this.
AP/B
A
B
C
X
D
tagged
untagged

## Slide 34: Summary: station subset problem

## Slide 35: Summary of station subset problem
The need is for an AP to send a single transmission to some arbitrary subset of the non-AP stations.
By extension of the “AP-AP problem”, that subset may include wireless links to other APs, as well.

## Slide 36: Multicasts and Bridge Ports

## Slide 37: Multicasts and bridge ports
In an 802.1Q Bridge, a multicast frame received on one port is often replicated and transmitted on multiple separate ports.
An Access Point can transmit a single frame to multiple non-AP stations. This seems to violate the Bridge model.
802.1 has discussed this problem in the past. My summary of these discussions is that, while some text needs to be added to 802.1Q, there is no fundamental problem, as will be explained in the following slides.

## Slide 38: IEEE Std 802.1Q-2011 Figure 8-10

## Slide 39: 802.1Q forwarding process
8.6.1: Active topology enforcement.
  Decide whether port state (blocking) allows frame to enter the relay.
  Construct a list of all active (non-blocked) ports (not including the ingress port) and attach it to this frame.
8.6.2 Ingress.
  Discard the frame if its VLAN tag is not correct.
  Learn the frame’s source MAC address.
8.6.3 Frame filtering
  Use the Filtering Database to filter the port list. That is, eliminate as many ports from the output port list as possible, based on destination MAC address.
8.6.4 Egress
  Discard frame from certain ports based on VLAN.

## Slide 40: 802.1Q forwarding process (continued)
8.6.5 Flow metering
  Yellow/green/red marking according to input port
8.6.6 Queuing frames
  Place frame in one or more queues, according to list of ports on which it is to be output.
  Discard frames based on yellow/green/red marking.
8.6.8 Transmission selection
  Select a frame to transmit on a given port.

## Slide 41: 802.1Q frame forwarding
One interesting point is that the Bridge does not replicate the frame; it constructs a list of ports on which the frame is to be transmitted.
As far as the 802.1Q Relay Function is concerned, the same identical frame is transmitted on all ports.
The differences between a wired Bridge and an Access Point can thus be buried in “8.6.6 Queuing frames”; that’s the only place it makes a difference, and that is exactly where the implementation issues are.
So, it should be easy to modify 802.1Q to refer to 802.11 in clause 8.6.6 to clear up both the broadcast replication and queuing issues.

## Slide 42: Well, almost easy
After the multicast leaves the queues, it must be tagged or not, and VLAN translation occurs.
Thus, a single frame in the queue may become multiple different frames that have to be transmitted separately.
However, this merely increases the amount of data sent; not the order in which queues are drained.
So, having a single queue for the AP’s station presents no fundamental architectural impediment to implementing 802.1Q Quality of Service (queue draining) algorithms.
Other 802.11 issues – acknowledgements/retries, sleeping stations, etc. WILL affect the Queue draining problems.

## Slide 43: VLAN tags

## Slide 44: VLAN tags
Any of an AP/bridge, a non-AP station bridge, or a VLAN-aware non-AP station can use VLAN tags.
An AP/bridge or non-AP station bridge can be in the path of a VLAN for which it has no local customers or local use.
Native 802.11 frames use the IEEE 802.2 LLC format.
Therefore, adding a VLAN tag to a frame requires adding 10 bytes to the frame (8-byte SNAP encoding + 2 byte payload), instead of the 4 bytes (2-byte EtherType + 2 byte payload) in 802.3.
Among bridges, a large fraction (typically, all) of the frames carry one or more tags.
This 6 bytes/tag penalty is particular obnoxious for wireless media.

## Slide 45: More VLAN tag problems
According to IEEE 802.1 documents, tags are added by inserting the tag (in the form appropriate to the medium, either Type/Length encoded or LLC encoded) in front of the existing mac_service_data_unit (MSDU) without changing the MSDU.
In theory, this means that each successive tag on an 802.2 medium carries a 6-byte SNAP burden (AA-AA-03-00-00-00).
This also means that, when bridging between 802.2 media and Type/Length media, the bridge has to understand every possible tag, so that it can change the first Type/Length to LLC or SNAP, and change all succeeding SNAPs (except the one encoding the data [which one is that???]) to Length/Type.
This means that no new tags can every be developed without revising all 802.2/Ethernet bridges.

## Slide 46: Unreliable links

## Slide 47: Unreliable links
Wireless media are inherently less dependable than wired media.
The effective speed and availability of a given connection can vary over a short timescale.
It is not acceptable to export volatile link conditions to the rest of the network; the result could easily be that the whole network becomes unstable.
We should discuss heuristics for reporting link conditions, and explore the capabilities of the topology control protocols (MSTP and SPB) with respect to variable links.

## Slide 48: AP-AP communications

## Slide 49: AP-AP communications
From the point of view of the Bridge part of a combined AP/Bridge device, there is no reason why a wireless connection to another AP/Bridge is any different from a connection to a non-AP client station of the AP.
This implies that a data link to adjacent APs can be offered to the Bridge part of an AP.
This slide is intended to serve as a place-holder for a discussion of this issue, if in fact there is one.
AP/B1
AP/B2
S
S
S