## Slide 1: Virtual Wireless Port based 802.11 Bridging
Date: 2012-12-16
Authors:

## Slide 2: Abstract
This presentation provides a method for addressing frames being transmitted between an AP and an associated non-AP STA Bridge so that the link between them can be used as a general 802 link inside a network. No change is required to the normal 802.11 addressing format and the reflection problem is solved.

## Slide 3: Recap of Problems
  The Reflected Frame issue:

## Slide 4: Recap of Problems
  Compatibility with Legacy STAs:

## Slide 5: Architecture of Emulated 802 LAN
AP
WLAN
STA
STA
STA
802 LAN
802 LAN
802 LAN
802.11 BSS
  WLAN associations act as transit links inside the network

## Slide 6: Our idea of the Virtual Wireless Port
AP
STA
STA-Bridge
3 virtual wireless ports
3 wired ports
Node
  Each STA-Bridge generates several MAC addresses, each of which acts as a virtual port.
  Each virtual wireless port is bound to a MAC address on the wired side network.

## Slide 7: MAC Translation based on Virtual Wireless Ports
  When frames from wired side accesses to the wireless network, the TA of the frame in 802.11 format will be translated to the MAC address of the bound virtual wireless port.
  When this bridge frame sends to the outside network, the source address will be changed back to the original MAC address.

## Slide 8: An example of transmitting a bridge frame
AP
STA-Bridge1
Node1
MAC1
MAC7
STA-Bridge2
Node2
MAC2
1
2
3
MAC3
DA = MAC2
SA = MAC1
RA = MAC7
DA = MAC2
TA = MAC3
TA = MAC7
DA = MAC5
SA = MAC3
MAC5
DA = MAC2
SA = MAC1
4
  Node 1 behind STA-B 1 transmits a frame to Node 2 behind STA-B 2.
  Note: The vMAC binds to Node 1 is MAC 3 on STA-B 1, while Node 2 is bound to MAC5 on STA-B 2.

## Slide 9: Implementation of the Virtual Wireless Port method
Process of bridge capability registration
  Bridge Capability notification/discovery
  Virtual wireless port registration
Process of virtual wireless ports binding
  Bind the MAC address of a node behind Wireless Bridge and a virtual wireless port on Wireless Bridge
  Updating ports binding tables on each wireless bridge

## Slide 10: Process of bridge capability registration
STA-Bridge
AP-Bridge
Probe Request (support bridge)
Probe response (support bridge)
Authentication request (binding control MAC: MAC0, Data MAC: MAC1 …))
Authentication response
  Use Beacon or Probe Request/Response to notify bridge capability
  Two choices for virtual MAC registration:
    Extends current management frames to bring the information of virtual MAC address of virtual ports, such as in authentication request frames
    Using a new management frame for MAC address registration
Beacon(support bridge)
…...

## Slide 11: Process of Port Binding
AP
STA-Bridge1
Node
MAC1
MAC7
STA-Bridge2
Legacy
STA
Node
MAC2
1
2
3
MAC3
MAC3
3. Send Port Binding Request <MAC3,MAC1>
2. Port Binding Request <MAC3,MAC1>
1. connect
4
6
5
4. drop
5.drop
6.STA-Bridge2 updates binding table

## Slide 12: Virtual MAC Generation
802.11 applies for a new global OUI
  No conflicts will occur
  STA/AP can immediately know whether a MAC is of a physical 802.11 device or a virtual Port by checking the top 24 bits.
  4096 vMACs automatically available at each non-AP STA bridge
  Reserved bit = 1 could be used for additional dynamically allocated addresses
  AID is technically 16 bits but top five bits are always 0b11000
  Other allocations of bottom 24 bits possible
(24bit)OUI
(11bit) AID
(12bit) vPort ID
R

## Slide 13: Discovery of the Reflected Frame
AP
STA-Bridge
Node
DA = ff
SA = MAC2
DA = ff
RA = MAC7
TA = MAC4
MAC2
MAC7
RA = ff
TA = MAC7
SA = MAC4
AP
STA-Bridge
MAC7
Bridge1
Node
MAC2
DA = ff
SA = MAC2
DA = ff
SA = MAC2
DA = ff
TA=MAC7
SA = MAC2
DA = ff
SA = MAC2
MAC4
MAC4

## Slide 14: Compatible with Legacy STAs
STA
AP
STA-Bridge1
Node
MAC1
MAC7
1
2
3
MAC3
DA = MAC2
SA = MAC1
RA = MAC7
DA = MAC2
TA = MAC3
TA = MAC7
RA = MAC2
SA = MAC3
MAC2
  When AP sends frames to associated STAs, it simply sends out one frame, all associated STAs can understand the frame, not only for STA bridges, but also for legacy STAs.

## Slide 15: Conclusions
No change to existing 802.11 data address format
Less air bandwidth consumption with 3 addresses
Compatible with legacy STA
No reflection issue
Easy implementation on AP/STA

## Slide 16: Questions & Comments
Please don't hesitate to email me if you have any questions
Thank you!