## Slide 1: BSS/Network Status Information for a Fast AP/Network Selection
Date: 2013-01-05
Authors:

## Slide 2: Abstract
This document provides further details for a feature described in Subsection 6.3.4 in the 802.11ai SFD (Specification Framework Document), 12/0151r14, for a fast AP/Network selection.
This contribution also provides supporting materials to the detailed text proposal for the TGai draft Specification document, as proposed in Contribution 13/0011 (a text proposal for TGai draft spec).

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | ??
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4
Background
A high-level feature description in Subsection 6.3.4 in TGai SFD:
  AP may include an indicator for AP availability to attachment to the Beacon and Probe Response.
  Multiple previous TGai contributions:
  KDDI: 11/1565r0, AP Status Broadcast
    include IEs, e.g., BSS load or other IEs related with AP status and performance in Beacon.
    Include WAN Status info in Beacon.
  China Mobile: 12/0545r1, Access Control Mechanism for FILS
    In 11ai management frames, e.g: beacon, probe response , GAS, carry the network load information for STA’s AP/Network selection:
    the congestion information of the AP; The available bandwidth information etc.
  HTC: 12/1051r2, Multi-channel information for AP discovery
    AP can attach the loading information of BSSs on other channels in the probe response and beacon, e.g., A condensed and aggregated loading information; Use a coarser unit to represent info such as BSS load, BSS Avg access delay, BSS Available Admission Capacity
  Joined contributions: 12/1271 and 12/1272
    Mandate BSS load IE in beacon and probe response;
    define a backhaul link status IE.

## Slide 5: Discussion on AP Availability Information
The purpose of providing AP availability information in Beacon/Probe Response:
  For a fast AP/Network selection, by avoiding selecting a congested or near-congested AP/Network and also by avoiding the query overhead.
  Note that AP Availability info in Beacon / Probe Response is not about the physical link availability, as it assumes that the STA already can receive Beacon / probe response.
AP availability information can be presented by:
  BSS/AP status/load indicators;
  Access Network link, or called Backhaul Link, status/load indicators.
BSS/AP Status/load Indicators
  Already have multiple in the current 802.11 Spec (802.11-2012); see next two slides for further discussions;
  Too many / Too much overhead
Backhaul Link Status/Load indicators
  Does not exist in the current 802.11 spec;
  Need to be defined.

## Slide 6
802.11-2012 BSS Status/Load Indicators
  5 relevant IEs in 802.11-2012 spec:
    BSS load IE: 2+5 bytes, containing the info of
      STA count: the total number of STAs currently associated with this BSS;
      Channel utilization: the percentage of time, linearly scaled with 255 representing 100%, that the AP sensed the medium was busy;
      Admission Capability: the remaining amount of medium time available via explicit admission control, in units of 32 μs/s.
    BSS Available Admission Capacity IE: 2+2+2*n bytes, containing the info of Admission Capabilities for each UP/AC (User Priority / Access Category);
    QoS Traffic Capability IE: 2+1+m bytes, containing the info of STA counts for each UP/AC ;
    BSS Average Access Delay IE: 2+1 bytes, containing the info of a scalar indication of average medium access delay;
    BSS AC Access Delay IE: 2+4 bytes; containing the info of Access Delay for each UP/AC.

## Slide 7
Discussions on BSS Status/Load Indicators
    Do we need all those 5 BSS Status/Load IEs in Beacon / Probe response for a fast AP/Network selection?
      No. Too much overhead, also redundant.
      A simple indicator or indicators for the STA to avoid selecting a congested or near-congested BSS.
    Do we need the per-UP/AC BSS Status/Load indicators?
      Not really, for overhead reduction!
      At initial link setup, the STA can use a simple indicator of LAN link loading and other parameters, e.g., PHY rates, to estimate if it should avoid the BSS/AP due to the potential LAN link congestion.

## Slide 8
Backhaul Link Status Indicator Considerations
  Backhaul Link: the communication link that connects the BSS/AP with external networks.
Backhaul Link Status descriptors / measures:
  Backhaul Link availability: available, not-available;
  Downlink / Uplink Rate: the data rate of the Backhaul link;
  Downlink / Uplink Load: the traffic load on the Backhaul link.
Downlink (DL):
  Backhaul Link direction from external network to the BSS/AP;
Uplink (UL):
  Backhaul Link direction from the BSS/AP to external network.

## Slide 9
Proposals
Propose a combined BSS/Backhaul Link Status indication field;
Include the BSS/Backhaul Link (BHL) status indication field
  As an IE in Beacon and Probe Response frames;
  As a sub-element in Neighbor report;
  As an optional field in FD frame
  As an optional field in the Reduced Neighbor Report

## Slide 10
Proposed BSS/Backhaul Link (BHL) Status Indication

## Slide 11
4-bit AP Status Indicator
  Average Access Delay, scaling down from the 8-bit code in Section 8.4.2.41 in 802.11-2012 spec into a 4-bit code below:
    0: Access Delay < 8us
    1 ≤ n ≤ 12: 2 (n+2) us ≤ Access Delay < 2(n+3)us
    13: 215us ≤ Access Delay
    14: Service unable to access the channel
    15: measurement not available
Proposed BSS/Backhaul Link Status Indication Field
– con’t

## Slide 12
4-bit Backhaul Link Status Indicator
  1-bit Backhaul Link Up/Down indicator
    0: down;
    1: up
  1-bit Relative Rate Indicator
    0: Backhaul link rate is less than the LAN link;
    1: Backhaul link rate is greater than or equal to the LAN link;
  2-bit Backhaul Link Load (BLL) Indicator
    0: BLL < 25%
    1: 25% <= BLL < 50%
    2: 50% <= BLL < 75%
    3: 75% <= BLL
Proposed BSS/Backhaul Link Status Indication Field
– con’t

## Slide 13
BSS/Backhaul Link Status Information Element / Subelement
  The BSS/Backhaul link (BHL) status IE can be included in:
    Beacon
    Probe Response
  The BSS/BHL status IE can also be included as subelement in:
    Neighbor Report IE for Neighbor BSS/Backhaul link;

## Slide 14
BSS/Backhaul Link Status in FD Frame
  Include the BSS/Backhaul link status in FD frame:
    an optional field,
    1-bit presence indicator in FD control field.

## Slide 15
 | Element ID | Length | Neighbor AP Information field #1 | Neighbor AP Information field #2 (optional) | … | Neighbor AP Information field #n (optional)
Octets: | 1 | 1 | variable | variable | variable | variable
 | TBTT Information Header | Operating Class | Channel Number | TBTT Information field #1 | … | TBTT Information field #n (optional)
Octets: | 2 | 1 | 1 | variable | variable | Variable
Neighbor AP information field
 | TBTT Info Field Type | BSS/BHL status present | Reserved | TBTT Information Count | TBTT Information Length
Bits: | B0 B1 | B2 | B3 | B4 B7 | B8 B15
TBTT Information Header subfield
BSS/Backhaul Link Status in Reduced Neighbor Report
  Include the BSS/Backhaul link status in Reduced Neighbor Report:
    Optional, with a 1-bit presence indicator in AP Info Header field
 | TBTT Offset in TUs | Optional BSS/BHL Status Field | Optional Subelements
Octets: | 1 | 1 | Variable

## Slide 16: Straw Polls
Straw-Poll-1: Do you support that 11ai-capable BSS/AP includes the BSS/BHL Status IE, as defined in Slide 10 and Slide 13 of this contribution, in the Beacon / Probe Response frame?
Result Yes No Abstain_______________

## Slide 17: Straw Polls
Straw-Poll-2: Do you support that 11ai-capable BSS/AP includes the BSS/BHL Status IE, as defined in Slide 10 and Slide 13 of this contribution, as an optional subelement in Neighbor Report element?
Result Yes No Abstain_______________

## Slide 18: Straw Polls
Straw-Poll-3: Do you support introducing to the FD frame the BSS/BHL (Backhaul Link) Status field as proposed on Slide 10 and Slide 14 in this contribution?
Result Yes No Abstain_______________

## Slide 19: Straw Polls
Straw-Poll-4: Do you support introducing to the Reduced Neighbor Report Element the BSS/BHL (Backhaul Link) Status field as proposed on Slide 10 and Slide 15 in this contribution?
Result Yes No Abstain_______________

## Slide 20
References:
IEEE Std 802.11™-2012
Draft-P802.11ai_D0.1
11-12-0151-14-00ai-proposed-specification-framework-for-tgai
11-11-1565-00-00ai-ap-status-broadcast
11-12-0545-01-00ai-access-control-mechanism-for-fils
11-12-1051-02-00ai-multi-channel-information-for-ap-discovery
11-12-1272-00-00ai-bss-network-status-information-for-a-fast-ap-network-selection
11-12-1271-00-00ai-tgai-spec-text-proposal-for-ap-network-status-information
11-13-0011-00-00ai-spec-text-for-AP-Network-Status-Info