## Slide 1: Setting of ProbeTimer
Authors:
Name | Affiliations | Address | Phone | email
Lin Cai | Huawei | 3601 Algonquin Road, Suite 1000, Rolling Meadows, IL 60008 | 1-847-848-1778 x 379 | Lin.cai@huawei.com
George Calcev | Huawei | 3601 Algonquin Road, Suite 1000, Rolling Meadows, IL 60008 |  | George.Calcev@huawei.com
01/02/2013

## Slide 2: Active Scanning[1]
PHY-CCA.indication (busy) primitive is not detected, scan the next channel when ProbeTimer reaches MinChannelTime
Otherwise, when ProbeTimer reaches MaxChannelTime, process all received probe responses
[1] 11REVmb-D12, Cls 10.1.4.3.3

## Slide 3: Active Scanning (Cont’d)
If CCA busy primitive is detected but no AP exists in the scanned channel, STAs have to scan for MaxChannelTime before switching to the next channel
  MinChannelTime = 0.67 ms [2,3]
  MaxChannelTime = 15 ms [2,3]
[2] M. Ryong Jeong, et.al., ”Fast Active Scan for Measurement and Handoff,” DoCoMo USA Labs, Contribution to IEEE802, May 2003.
[3] M. Emmelmann, “Achievable gains in AP Discovery,” FOCUS, doc. IEEE 802.11-10/0922r1
Probe
MinChannelTime
MaxChannelTime

## Slide 4: Problem
CCA is based on energy detection technique
In a WiFi channel without an AP, it is possible that a STA may sense the channel busy due to transmissions of
  Probe requests from other STAs
  Non-Wifi devices such as microwave, cordless phone, etc.
If PHY-CCA.indication (busy) primitive invoked by probe requests or non-WiFi devices, a STA needs to wait for a MaxChannelTime, which causes long delay

## Slide 5: Delay of Active Scanning
M APs uniformly distributed over N channels
  The probability that there is at least one AP in any given channel is
    P=1-(1-1/N)^M
  Given an AP exists in a given channel, the expected time a STA spends in scanning this channel is
    T1= ProbeDelay + Tx_ProbeReq + MaxChannelTime
  Given no AP exists in a given channel
    CCA busy primitive is not detected (ideal case):
    T2_{ideal}=ProbeDelay + Tx_ProbeReq + MinChannelTime
    CCA busy primitive is detected due to interference/requests (non-ideal case):
    T2_{Non-ideal}=ProbeDelay + Tx_ProbeReq + MaxChannelTime
  Expected scanning delay in one channel: D=T1*P + T2 *(1-P)

## Slide 6: Delay of Active Scanning (Cont’d)
Parameters[3]:
  ProbeDelay = 0.1 ms
  MinChannelTime = 0.67 ms
  MaxChannelTime = 15 ms
  Tx_ProbeReq = 0.4 ms
  N=14 channels
Chart: 
Ideal Case | 2.1936 | 3.144 | 4.0266 | 4.8461 | 5.6071 | 6.3138 | 6.9699 | 7.5792 | 8.145 | 8.6703 | 9.1582 | 9.6112 | 10.0318 | 10.4224 | 10.7851 | 11.1218 | 11.4346 | 11.725 | 11.9946 | 12.245
Non-ideal Case | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5
Number of APs M
Expected scanning delay over each channel (ms)
[3] M. Emmelmann, “Achievable gains in AP Discovery,” FOCUS, doc. IEEE 802.11-10/0922r1

## Slide 7: Proposed Solution
If CCA busy primitive is not detected, a STA sets its ProbeTimer to MinChannelTime
If CCA busy primitive is detected, a STA processes the received information; if the STA found it is only invoked by Probe Request messages or non-decodable messages, STA may set the ProbeTimer to MedChannelTime, which is not necessarily as large as MaxChannelTime, as there is no hard evidence of APs’ presence

## Slide 8: Proposed Solution
If CCA busy primitive is detected, a STA processes the received information; the STA sets their ProbeTimer to MaxChannelTime if it receives messages with implicit or explicit evidence of APs’ existence, including data frames, management frames (association, authentication, etc.), and control frames (CF-End, CF-End+ACK frames, PS-poll, etc.)
Probe
MinChannelTime
MaxChannelTime
Idle channel
Channel busy invoked by probe requests or non-decodable messages
Channel busy invoked by other data/management/control messages
MedChannelTime

## Slide 9: Delay Comparison
Expected delay with proposed timer
  D=T1*P + T2_{proposed} *(1-P), where
  T2_{proposed} = ProbeDelay + Tx_ProbeReq + ProbeTimer (e.g., 2ms or 5ms)
Number of APs M
Expected scanning delay over each channel (ms)
Chart: 
Ideal Case | 2.1936 | 3.144 | 4.0266 | 4.8461 | 5.6071 | 6.3138 | 6.9699 | 7.5792 | 8.145 | 8.6703 | 9.1582 | 9.6112 | 10.0318 | 10.4224 | 10.7851 | 11.1218 | 11.4346 | 11.725 | 11.9946 | 12.245
Non-ideal Case | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5
MedChannelTime=2ms | 2.9643 | 3.8597 | 4.6911 | 5.4632 | 6.1801 | 6.8458 | 7.464 | 8.038 | 8.571 | 9.0659 | 9.5255 | 9.9522 | 10.3485 | 10.7165 | 11.0582 | 11.3754 | 11.67 | 11.9436 | 12.1976 | 12.4335
MedChannelTime=5ms | 5.75 | 6.4464 | 7.0931 | 7.6936 | 8.2512 | 8.769 | 9.2498 | 9.6962 | 10.1108 | 10.4957 | 10.8532 | 11.1851 | 11.4933 | 11.7795 | 12.0452 | 12.292 | 12.5211 | 12.7339 | 12.9315 | 13.115

## Slide 10: Conclusion
In current standard, energy detection based CCA is used for determining the ProbeTimer, which may cause long scanning delay when no AP exists in the scanned channel
To reduce unnecessary scanning delay, STAs should be able to decide its ProbeTimer based on the detection of an identifiable AP transmissions rather than CCA only

## Slide 11: Straw Poll
Do you agree to: “Add a new ProbeTimer called MedChannelTime that allows a STA during the active scanning procedure to move to the next channel when MedChannelTime expires if only Probe Requests or non-decodable energy is sensed in the scanned channel?”
Yes
No
Need more information

## Slide 12: Motion
Move to: “Add a new ProbeTimer called MedChannelTime that allows a STA during the active scanning procedure to move to the next channel when MedChannelTime expires if only Probe Requests or non-decodable energy is sensed in the scanned channel”
Yes
No
Abstain