## Slide 1: Higher Layer Packet Container Proposal Presentation
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@trans-nt.com
Date: 2013-01-15
Authors:

## Slide 2: Abstract
This document is presentation material about 11-13/0040r2.

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: Background
We discussed about higher layer setup. Such as,
  11-11/977r6
  11-11/1047r5
  11-11/1108r1
  11-11/1167r0
In these discussions, I proposed DHCP proxy protocol but some issues are found through the discussion.
  Delayed server response
    Require to define new management frames
  Roaming between FILS and non-FILS APs.
Generic Container for higher layer is better.

## Slide 5: Issues
How to fragment large higher layer packet?
How long to wait the response from the servers?
How to protect the higher layer packets?

## Slide 6: Proposal
Higher Layer Packets (HLPs) are piggy-backed in Authentication and Association Request/Response as IE(s).
  They can be protected.
Define 3 new primitives.
  dot11HLPTransportDuringAssoc
  dot11HLPMaxWaitTime
  dot11HLPWaitTime
Define 3 new IEs.
  HLP Max Wait Time IE
  HLP Wait Time IE
  HLP Container IE

## Slide 7: Primitives
dot11HLPTransportDuringAssocActivated
  Truth Value
dot11HLPMaxWaitTime
  Integer (millisecond)
  This primitive indicates the maximum time that the AP allows to wait the HLP after the AP receives Association Request.
dot11HLPWaitTime
  Integer (millisecond)
  This primitive indicates the time that the non-AP STA requests to wait the HLP after the AP receives Association Request.
  dot11HLPWaitTime <= dot11HLPMaxWaitTime
  dot11HLPWaitTime < dot11AssociationResponseTimeOut

## Slide 8: HLP Max Wait Time IE
Max wait time in unit of millisecnd.
Transmitted in Beacon and Probe Response.

## Slide 9: HLP Wait Time IE
Wait time in unit of millisecnd.
Transmitted in Association Request.

## Slide 10: HLP Container IE
Type 1
  Used for non-fragmented HLP and the first element of fragmented HLP.
Type 2
  Used for the subsequent elements of fragmented HLP.

## Slide 11: Flags

## Slide 12: Encapsulation 1 (1 HLP, non-fragmented)
HLP length: 200 octets, LLC/SNAP length: 8 octets
200 octets
200 octets
IE Header (NFrag = 0)
Type 1

## Slide 13: Encapsulation 2 (1 HLP, fragmented)
HLP length: 600 octets, LLC/SNAP length: 8 octets
  Split to 3 elements, 234 octets (A), 255 octets (B) and 111 octets (C) in order.
600 octets
A: 234 octets
B: 255 octets
C: 111 octets
A: 234 octets
IE Header (NFrag = 2)
B: 255 octets
IE Header
IE Header
C: 111 octets
Type 1
Type 2
Type 2

## Slide 14: Encapsulation 3 (2 HLPs, non-fragmented)
HLP A length: 200 octets, LLC/SNAP length: 8 octets
HLP B length: 200 octets, LLC/SNAP length: 8 octets
A: 200 octets
A: 200 octets
IE Header (NFrag = 0)
Type 1
B: 200 octets
B: 200 octets
IE Header (NFrag = 0)
Type 1

## Slide 15: Encapsulation 4 (2 HLPs, fragmented)
HLP A length: 600 octets, LLC/SNAP length: 8 octets
HLP B length: 600 octets, LLC/SNAP length: 8 octets
A1: 234 octets
IE Header (NFrag = 2)
Type 1
A: 600 octets
Type 1
B: 600 octets
A2: 255 octets
A3: 111 octets
B1: 234 octets
B2: 255 octets
B3: 111 octets
A1: 234 octets
IE Header
A2: 255 octets
IE Header
A3: 111 octets
IE Header (NFrag = 2)
B1: 234 octets
IE Header
B2: 255 octets
IE Header
B3: 111 octets
Type 2
Type 2
Type 2
Type 2

## Slide 16: Protection
AP derives the key after receiving Authentication from STA.
STA derives the key after receiving Authentication from AP.
“The Association Request and Association Response shall be protected using the KEK2 according to 11.11.2.5 and 11.11.2.6.” – 11.11.2.4, D0.2.

## Slide 17: FILS Authentication/Association (D0.2)
STA
AP
Authentication
Authentication
Association Request
Association Response
Key Derivation
Key Derivation
Protected
Piggy backed part can be protected
Key Confirmation

## Slide 18: Encrypt HLP in Authentication
Encryption in Association frames is already described in D0.2.
But encryption in Authentication frames is not described yet.
Encrypt the HLP by AES-CCM with KEK2.
Encryption method is almost same as the method for Association Response described in 11.11.2.4, D0.2.
If fragmentation is required,
  Encrypt the HLP first,
  Fragment

## Slide 19: Forward Sequence 1 (Successful Key Confirmation, HLP from 3rd party in time)
The AP forwards HLP-A from non-AP STA after successful authentication.
If the AP receives HLP-B from 3rd Party in dot11HLPWaitTime, the AP forwards it in Association Response.
STA
AP
Association Request
(dot11HLPWaitTime, HLP-A)
Association Response (HLP-B)
3rd Party
Successful Key Confirmation
HLP-A
HLP-B
dot11HLPWaitTime
Beacon/Probe Resp.
(dot11HLPMaxWaitTime)
Authentication

## Slide 20: Forward Sequence 2 (Authentication Failure)
The AP silently discards HLP-A after authentication failure.
Key Confirmation Failure
Silently discards HLP-A
STA
AP
Association Request
(dot11HLPWaitTime, HLP-A)
3rd Party
Beacon/Probe Resp.
(dot11HLPMaxWaitTime)
Authentication

## Slide 21: Forward Sequence 3 (Successful Authentication, HLP from 3rd party NOT in time)
The AP forwards HLP-A from non-AP STA after successful authentication.
If the AP receives HLP-B from 3rd Party after dot11HLPWaitTime, the AP forwards it as a Data Frame.
STA
AP
Association Request
(dot11HLPWaitTime, HLP-A)
Association Response
3rd Party
Successful Key Confirmation
HLP-A
HLP-B
dot11HLPWaitTime
Beacon/Probe Resp.
(dot11HLPMaxWaitTime)
Authentication
HLP-B as Data Frame

## Slide 22: Example Usage for DHCPv4
STA
AP
Association Request
DHCPDISCOVER w/RCO
Association Response
DHCPACK w/RCO
DHCP
Server
DHCPDISCOVER w/RCO
DHCPACK w/RCO

## Slide 23: Example Usage for IPv6 Stateless Configuration
STA
AP
Association Request
Association Response
(RA)
Router
RA
Authentication
Authentication
RA

## Slide 24: Example Usage for IPv6 Stateful Configuration
STA
AP
Association Request
DHCP Solicit w/RCO
Association Response
DHCP Reply w/RCO
DHCP
Server
RA
Authentication
Authentication
RA
Router
DHCP Solicit w/RCO
DHCP Reply w/RCO

## Slide 25: Aggressive Example Usage
STA can start communication beyond the router immediately after association in both IPv4 and IPv6.
STA
AP
Association Request
DHCPDISCOVER w/RCO (v4)
DHCP Solicit w/RCO (v6)
Association Response
DHCPACK w/RCO (v4)
DHCP Reply w/RCO (v6)
Gratuitous proxy ARP of the Router
DHCPv4
Server
RA
Authentication
Authentication
RA
Router
DHCPDISCOVERw/RCO
DHCP Reply w/RCO
DHCPv6
Server
DHCP Solicit w/RCO
DHCPACK w/RCO

## Slide 26: Questions & Comments

## Slide 27: Motion
Move to include the text in 11-13/0040r2 into the TGai Draft Specification Document.
Moved:
Second:
Result (Y/N/A):