## Slide 1: Criteria to respond probe
Name | Affiliations | Address | Phone | email
Jing-Rong Hsieh | HTC Corp. | 1F, 6-3 Baoqiang Road, Xindian district, New Taipei City, Taiwan |  | jing_hsieh@htc.com
Date: 2013-01-07
Authors:

## Slide 2: Abstract
This contribution introduces further considerations regarding “6.2.6 Omission of Probe Response” of TGai SFD to reduce nonqualified Probe Responses by posing DL signal qualification.

## Slide 3: Background
Goal: Reduce probe responses from (probe request decodable) APs
  Fulfill connection requirement without or minimizing
    Overkill (lost some APs which may also fulfill the requirement)
    Loose control
STA has a need to find more qualified APs rather than those barely communicable
  Application/Services ↔ Connection rate ↔ Signal quality
  Connection manager on user device shows the SSID with best DL signal
  Driven by smartphone use, the traffic is more DL-centric
The product spec (Max TX power, RX sensitivity) varies between vendors
  The exact TX power and RX sensitivity of the responding side is unknown initially
  AP: 18 ~ 28dBm
  STA: 12 ~ 26dBm

## Slide 4: Setting the quality indicator
Asymmetric traffic application dominates [3][5]
  DL-centric applications have reached a total of 92% in H2-2011
  Better DL quality helps traffic delivery in this direction
    Better spectrum usage and higher transmission speed or robustness
  How to set the quality requirement of DL/UL?
    If only using UL indicator (indirect setting)
      Too high – overkill (DL can be fulfilled but some APs may be filtered)
      Too low – every decodable AP responds; the indicator becomes useless overhead
    If using DL indicator
      Need additional info of TX power (overhead vs accuracy)

## Slide 5
DL Requirement
overkill
Received signal
Distance
These APs can fulfill the DL requirement but will be filtered if the threshold is set according to itself (TX power and sensitivity)
Transmit power

## Slide 6
DL Requirement
Loose control
Received signal
Distance
These APs can fulfill the UL requirement but not the DL requirement if the threshold is set according to a higher expectation of AP transmit power
Lower down the UL requirement
Transmit power

## Slide 7
RX_PWR >? UL signal quality threshold
  Path loss, TX_PWRAP, Sensitivity of AP are unknown
  Setting for UL signal quality threshold
    According to self-sensitivity/standardized-sensitivity
    APs in the market usually have better sensitivities (but unknown to STA)
  Hard to precisely assure downlink signal quality
TX_PWRAP − (TX_PWRSTA − RX_PWR) >? DL signal quality threshold
  TX_PWRAP − TX_PWRSTA + RX_PWR >? DL signal quality threshold
  Sensitivity on STA-side is known → easier to set the threshold
Simplified encoding to ease calculation complexity and reduce overhead
  4-bit for TX_PWR_level, 0 ~ 30dBm
  4-bit for Signal quality, -90~-60dBm

## Slide 8: Proposed changes to FILS Request Parameters element
Element ID | Length | Parameter Control Bitmap | FILS Criteria | Max Delay Limit | Minimum Data Rate | Link Quality Parameter Received Signal Strength Limit | OUI Response Criteria
Octets: 1 | 1 | 1 | 0 or 1 | 0 or 1 | 0 or 3 | 0 or 1 | 0 or 2
 | B0 B3 | B4 B7
 | Transmit Power | Desired Signal Quality Indicator
Bits: | 4 | 4
B0 | B1 | B2 | B3 | B4 | B5 B7
FILS Criteria | Max Delay Limit | Minimum Data Rate | Link Quality Parameter Received Signal Strength Limit | OUI Response Criteria | Reserved
1 | 1 | 1 | 1 | 1 | 3
Bits:

## Slide 9: 4 bits for Transmit Power
Code | Description | Code | Description
0 | 0 dBm (1mW) | 8 | 16dBm
1 | 2 dBm | 9 | 18dBm
2 | 4 dBm | 10 | 20dBm (100mW)
3 | 6 dBm | 11 | 22dBm
4 | 8 dBm | 12 | 24dBm
5 | 10dBm (10mW) | 13 | 26dBm (400mW)
6 | 12dBm | 14 | 28dBm
7 | 14dBm | 15 | 30dBm (1W)
Rounded up to the corresponding code.
The increase steps may be set as 5dB and then 3 bits are sufficient. One more bit may be reserved for indication of DL or UL requirement.
Notes: Max TX power: One X+ 15~26dBm; iPhone 13~16dBm.

## Slide 10: 4 bits for Desired DL Signal Quality
Code | Description | Code | Description
0 | -90dBm | 8 | -74dBm
1 | -88dBm | 9 | -72dBm
2 | -86dBm | 10 | -70dBm
3 | -84dBm | 11 | -68dBm
4 | -82dBm | 12 | -66dBm
5 | -80dBm | 13 | -64dBm
6 | -78dBm | 14 | -62dBm
7 | -76dBm | 15 | -60dBm
Rounded up to the corresponding code.
Or starts from -85 or -80 since the requirement should be more than barely communicable

## Slide 11: Conclusion
The probe responses can be reduced by setting the link quality requirement
It does not introduce additional overhead and can better assure desired DL signal quality when filtering unqualified APs

## Slide 12: References
11-12-1053-04-00ai-combined-active-scanning-text
11-12-0151-13-00ai-proposed-specification-framework-for-tgai
“A First Look at Trafﬁc on Smartphones”, Hossein Falaki et.al, IMC’10, November 1–3, 2010
Draft P802.11ai_D0.2
“Asymmetry of mobile backhaul networks”, Ceragon, CEPT ECC meeting, September 4-5, 2012