## Slide 1: 2MHz Dup Mode
Date: 2013-01-14
Authors:

## Slide 2
Authors continued:
Slide 2
Jan 2013

## Slide 3
Authors continued:

## Slide 4: Background
As in 11ac, BW protection is needed during RTS/CTS and other Ctrl frame exchanges.
  There are some Ctrl frames squeezed into an NDP, but some other frames (RTS, NDPA) are still carried by regular data PPDUs.
There is no legacy format being defined in 11ah, hence no “legacy duplicate mode” is possible.
Here we propose to define “2MHz Duplicate” mode in 11ah for BW protection purpose.
  Duplicate the 2MHz signal in each 2MHz sub-channel.
  Equivalent to duplicate 20MHz (V)HT packet in 11n/11ac.
  Different from legacy-dup mode on their tone maps.

## Slide 5: Proposed 2MHz Duplicate Mode
The number of guard tones (4/3) is less than number of guard tones of true 4/8/16MHz signal (6/5).
  Filter design is more stringent, but we have to support a single 2MHz in wider BW Tx and/or Rx anyway!
Preamble (LTF) is also duplicated.
  Different from the true 4/8/16MHz LTF, also different from 11n MCS32.
Phase shift (“Gamma”) is applied in each 2MHz subband to reduce PAPR—same as 11ac Non-HT dup mode.
STF
LTF1
SIG
DATA
LTF2
…
LTF_NLTF
STF
LTF1
SIG
DATA
LTF2
…
LTF_NLTF
(2MHz)
(2MHz)
(×1)
(×j)

## Slide 6: Tone Plans
4MHz: 108 Data, 6 Pilot, 3 DC tones
0
-58
-64
58
63
(6 guard tones)
(5 guard tones)
True 4MHz Signal:
2MHz Signal
0
-60
-64
63
(4 guard tones)
(3 guard tones)
2MHz-Dup Signal
in 4MHz (both Data
and LTF):
-4
2MHz Signal
4
60
BW = 4MHz
BW = 8MHz
8MHz: 234 Data, 8 Pilot, 3 DC tones
0
-122
-128
122
127
(6 guard tones)
(5 guard tones)
True 8MHz Signal:
2MHz Signal
-124
-128
127
(4 guard tones)
(3 guard tones)
2MHz-Quad Signal
in 8MHz (both Data
and LTF):
-68
2MHz Signal
0
-60
-4
2MHz Signal
4
60
(7 DC tones)
2MHz Signal
68
124

## Slide 7: NDP Short Control Frames
Some Control Response Frames may use the NDP short frame format.
Current 4MHz/8MHz/16MHz NDP format is sufficient for BW protection.
  LTF has 6/5 guard tones—same as SIG field
  No data portion, hence the LTF is sufficient for decoding the 2MHz SIG field in each 2MHz sub-channel
No need to define 2MHz dup mode for NDP.

## Slide 8: Pre-Motion
Do you agree to define 2MHz Dup Mode in the spec framework as below?
  Preamble and Data portions of 2MHz signal is duplicated in each 2MHz sub-channel of 4MHz/8MHz/16MHz.
  Phase shift is applied in each 2MHz sub-channel of the duplicate signal.
    4MHz: [1, j]
    8MHz: [1 -1 -1 -1]
    16MHz: each 8MHz half is identical to a stand-along 8MHz signal.

## Slide 9: Motion
Move to define 2MHz Dup Mode in the spec framework as below?
  Preamble and Data portions of 2MHz signal is duplicated in each 2MHz sub-channel of 4MHz/8MHz/16MHz.
  Phase shift is applied in each 2MHz sub-channel of the duplicate signal.
    4MHz: [1, j]
    8MHz: [1 -1 -1 -1]
    16MHz: each 8MHz half is identical to a stand-along 8MHz signal.