## Slide 1: Receiver Sensitivity Levels
Date: 2013-01-14
Authors:

## Slide 2
Authors continued:
Slide 2
Jan 2013

## Slide 3
Authors continued:

## Slide 4: Discussions
Propose to scale the 11ac sensitivity levels based on the BW differences between 11ac and 11ah.
Assume 3dB sensitivity improvement is achieved by the 2x repetition in 1MHz MCS0.
Proposed sensitivity calculation equations;
  For 2/4/8/16MHz, and the same MCS as 11ac:
    Sensitivity_11ah = truncate (Sensitivity_11ac – 10log(10))
  For 1MHz MCS0~9:
    Sensitivity_11ah = truncate (Sensitivity_11ac_20MHz – 10*log(20) – 0.16),
      Where 0.16 is the dB of percentage decrease of (populated_tones/FFT_tones).
  For 1MHz MCS10:
    Sensitivity_1MHz_MCS10 = truncate (-82 – 10*log(20) – 3 – 0.16) = -98dBm

## Slide 5: The Corresponding Sensitivity Table
Modulation | Rate (R) | Minimum Sensitivity (1MHz PPDU) (dBm) | Minimum Sensitivity (2MHz PPDU) (dBm) | Minimum Sensitivity (4MHz PPDU) (dBm) | Minimum Sensitivity (8MHz PPDU) (dBm) | Minimum Sensitivity (16MHz PPDU) (dBm)
BPSK | 1/2 & 2x repetition | -98 | n.a. | n.a. | n.a. | n.a.
BPSK | 1/2 | -95 | -92 | -89 | -86 | -83
QPSK | 1/2 | -92 | -89 | -86 | -83 | -80
QPSK | 3/4 | -90 | -87 | -84 | -81 | -78
16-QAM | 1/2 | -87 | -84 | -81 | -78 | -75
16-QAM | 3/4 | -83 | -80 | -77 | -74 | -71
64-QAM | 2/3 | -79 | -76 | -73 | -70 | -67
64-QAM | 3/4 | -78 | -75 | -72 | -69 | -66
64-QAM | 5/6 | -77 | -74 | -71 | -68 | -65
256-QAM | 3/4 | -72 | -69 | -66 | -63 | -60
256-QAM | 5/6 | -70 | -67 | -64 | -61 | -58

## Slide 6: Pre-Motion
Do you agree to add the sensitivity levels on slide 5 into the spec framework?

## Slide 7: Motion
Move to add the sensitivity levels on slide 5 into the spec framework