## Slide 1: NDP Type PS-Poll Frame Follow-Up
Date: 2013-01-14
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Background
TGah accepted to define a NDP type PS-Poll frame format as [1]
  However, details on each subfield are TBD.
In this contribution, we propose to define each subfields for NDP PS-Poll frame.
STF
LTF1
SIG

## Slide 5: NDP PS-Poll Frame
Based on current discussion, following subfields are considered for NDP PS-Poll frame [2, 3]
  Message type indication
  RA
  TA
  Preferred MCS level
  Uplink data indication
  Tail bits
  CRC

## Slide 6: Issues on Address Fields
Reception of NDP PS-Poll at the AP side can be divided into two categories:
  At scheduled time
    Poll at designated time slot from designated STA
    both TIM (RAW based) and non-TIM (TWT based) STAs
  At non-scheduled time
    Poll from non-TIM (unscheduled active polling) STAs
    Sometimes from TIM STAs when its designated slot is busy or at the time of retransmission, etc
If NDP PS-Poll is received at scheduled time
  AP knows exactly who is supposed to send at the given time window.
  Therefore, AP considers the PS-Poll is coming from the designated STA only when both TA & RA match.
  If we use 9bit PBSSID & 9bit PAID, chance of address collision becomes negligible (2^18).
If NDP PS-Poll is received at non-scheduled time
  When RA matches with AP’s PBSSID, it will send ACK back as long as there’s an associated STA using the indicated PAID.
  In this case, the chance of address collision is not low enough (2^9), which was shown in the previous contribution [2].

## Slide 7: Issues on Address Fields
Therefore, we need a mechanism to protect wrong data delivery for the case that NDP PS-Poll is received at non-scheduled time, which has to be
  Simple protocol
  Need to have unique ID check before data delivery
Simple solution for this ambiguity under currently defined TGah spec.
  If NDP PS-Poll is received at the scheduled time from scheduled STA, AP sends back response frame normally.
  However, if NDP PS-Poll is received at non-scheduled time, AP sends back response frame with additional RTS/CTS protection.
    As RTS frame contains full MAC address fields, it can further resolve address collision issue.
  Unscheduled active polling STAs may use normal PS-Poll frame.
  Or, if a STA doesn’t receive proper response from the AP for multiple consecutive NDP PS-Poll frame transmission, it may switch to normal PS-Poll frame.

## Slide 8: Subfields for NDP PS-Poll Frame
Message type indication
  Currently 7 NDP MAC frames are defined.
    Management: Probe request, BF report poll, Paging
    Control: ACK, Block ACK, CTS, PS-Poll
  Unless we want to include any further NDP frame format, Message type indication needs at least 4 bits.
    NDP Indication: 1bit
    NDP sub-type indication: 3bits
RA and TA
  In current 2MHz SIG field, 9bit PBSSID/PAID is defined.
  This can be a good candidate for RA and TA.
    RA: 9bit PBSSID
    TA: 9bit PAID

## Slide 9: Subfields for NDP PS-Poll Frame
Preferred MCS level
  Goal: To let AP know STA’s preferred downlink MCS level for DL transmission
  2MHz frame format
    Full 4bit MCS information
  1MHz frame format
    Due to limited SIG field space, use of full 4 bit information may not be available.
    Need further discussion for possible solution.

## Slide 10: Subfields for NDP PS-Poll Frame
Uplink Data Indication (UDI) field
  In [3], it was proposed to introduce an uplink data indication (UDI) signaling field in NDP PS-Poll frames to assist the APs in scheduling uplink channel access
  UDI field
    Amount of uplink data specified in number of symbols
    1 bit for 1 MHz
    9 bits for >= 2 MHz

## Slide 11: Subfields for NDP PS-Poll Frame
1MHz mode frame format
Field | Bit width | Comments
Message type indicator | 4 | 1 bit: NDP indication 3bits: sub-type indication
RA | 9 | PBSSID
TA | 9 | PAID
Preferred MCS | 2 | TBD
UDI | 1 | 0: no data, 1: data
Reserved bit | 1 | 
Tail bits | 6 | 
CRC | 4 | 
TOTAL | 36 | 

## Slide 12: Subfields for NDP PS-Poll Frame
2MHz mode frame format
Field | Bit width | Comments
Message type indicator | 4 | 1 bit: NDP indication 3bits: sub-type indication
RA | 9 | PBSSID
TA | 9 | PAID
Preferred MCS | 4 | Explicit MCS indication
UDI | 9 | 0: no data, Non-zero value indicates duration of uplink data in number of symbols
Reserved bit | 3 | 
Tail bits | 6 | 
CRC | 4 | 
TOTAL | 48 | 

## Slide 13: Straw Poll
Do you support to define SIG field format for NDP PS-Poll frame for 1MHz mode and 2MHz mode as shown in slides 11 & 12?
  Bitwidth for all subfields is TBD.
  Preferred MCS subfield for 1MHz is TBD.

## Slide 14: References
[1] IEEE 802.11-11/1137r12 Proposed Specification Framework for TGah, November, 2012
[2] IEEE 802.11-12/0848r0 NDP type PS-Poll frames, July, 2012
[3] IEEE 802.11-12/1308r0 Uplink Data Indication in NDP PS-Poll, November, 2012