## Slide 1: Reachable Address Message for Relay
Date: 2013-01-14
Authors:

## Slide 4: Introduction
The concept of Relay was introduced in the last meeting [1]
  Quick recap in next slide
Backward learning bridge is used for populating the forwarding tables
However, in some conditions, backward learning is not possible
  Due to the absence of data frames to be used for learning
We propose to define a ‘Reachable Address’ Frame to be used for explicitly updating the forwarding tables

## Slide 5: Recap
R-STA is a non-AP STA with the following capabilities
  4 address support
  Supports forwarding and receiving frames from the R-AP
R-AP is an AP with the following additional capabilities
  4 address support mandatory, i.e.,
  Supports forwarding and receiving frames to/from the R-STA
Root AP (Rt-AP)
  Backward learning bridge principle may be used to set up the forwarding tables

## Slide 6: Issue with backward learning bridge
Issues:
  When STA moves to another Relay, MAC solution may not rely on higher layer protocols to send an MSDU to AP; if no MSDU is sent, backward learning is not possible; we need a fallback mechanism for a robust MAC solution
    Nowadays, ARP is commonly used and when associating with an AP, STA usually starts ARP; but when moving between two relays in same subnet, STA need not re-do ARP and may not send any frame to AP
    Also, MAC-only or other new protocols other than ARP may be used in the future for new IoT applications
  When a Relay moves to another AP, it needs to update the parent AP with its children MAC addresses
  Upon moving Relays and STAs, we need to guarantee the consistency of forwarding tables

## Slide 7: Solution
R-STA to use a Layer 2 “ReachableAddress” message to update root AP about new STAs, if the STAs do not send frames to root AP that allow for backward learning
  Message may include a list of MAC addresses and other fields that help the AP to update its forwarding tables and resolves conflicts

## Slide 8: Straw poll
Move to include in the SFD the ReachableAddress message that is used to update the forwarding tables?
  Content and format TBD

## Slide 9: References
[1] 11-12-1323-00-00ah-relay.pptx