## Slide 1: EIFS Issues
Author:
Name | Affiliation | Address | Phone | Email
Menzo Wentink | Qualcomm | Straatweg 66-s, Breukelen, The Netherlands | +31-65-183-6231 | mwentink@qualcomm.com

## Slide 2: CID 287
This contribution is related to Revmc pre-ballot CID 287
  11-12-1082-11-000-revmc-pre-ballot-comments.xls
  CID 287:
    “EIFS is intended to protect a hidden ACK, but it may also get started after an ACK that is sent at a higher PHY rate than its PLCP header. This may cause unwanted deferral after a TXOP, resulting in major channel access unfairness and in some cases even a capture effect. A similar issue may occur at hidden nodes that do EIFS for a hidden ACK that is shorter than what is assumed in the EIFS.”

## Slide 3: Introduction
There are two design issues with EIFS
  EIFS can be started after an Ack frame
  EIFS can be (much) longer than a hidden Ack
The proposed resolution is as follows:
  allow EIFS=DIFS for PPDUs that look like an ACK
  allow EIFS to be based on the PPDU’s Rate/MCS

## Slide 4: Definition of EIFS
EIFS is defined as aSIFSTime + DIFS + ACKTxTime
  EIFS = SIFS+ACK+DIFS
2.4 GHz
  EIFS = 10+304+10+2*9 = 342 us
5 GHz
  EIFS = 16+44+16+2*9 = 94 us

## Slide 5: EIFS-after-Ack Issue (1)
EIFS is intended to avoid that STAs interfere with an ACK from a hidden STA, by deferring for EIFS when a valid packet is detected but a Duration field could not be decoded (i.e. the FCS fails)
However, EIFS may also get started after ACK frames, when the MPDU MCS is higher than the L-SIG MCS
  an ACK MPDU at 24 Mbps can only be received correctly at about half the distance of its L-SIG
EIFS deferral after a TXOP causes major unfairness between contending devices, and in some cases even a capture effect

## Slide 6: EIFS-after-Ack Issue (2)
MPDU range of the Ack
Ack
STA
AP
Area where the EIFS-after-Ack issue occurs
L-SIG range of the Ack from the AP to STA2

## Slide 7: EIFS-after-Ack Issue (3)
Assuming channel D and certain path loss conditions, an ACK MPDU at 24 Mbps can only be received correctly at about half the distance of its L-SIG
  this means that EIFS is started in 90% of the region where the L-SIG of the ACK is received, assuming spherical range
For higher attenuation, for instance through walls, the EIFS-after-ACK issue starts much closer to the device sending the ACK
  therefore, the issue can be caused by devices in the home network or in a neighboring network

## Slide 8: EIFS-after-Ack Issue (4)
EIFS duration
  2.4 GHz
    EIFS = 342 us
      in terms of AIFSN: 36 slots
      36 slots is extremely long when CWmin is 15 or even 31 slots
  5 GHz
    EIFS = 94 us
      in terms of AIFSN: 9 slots
      by comparison, the AIFSN for background traffic is ‘only’ 7 slots

## Slide 9: Simulation Setup for EIFS-after-ACK
STA1
UDP
UDP
STA2
AP
STA1 starts EIFS after ACKs from the AP to STA2
L-SIG range of the Ack from the AP to STA2
MPDU range of the Ack
Area where the EIFS-after-Ack issue occurs

## Slide 10
EIFS-after-ACK - Best Effort Traffic (2.4 GHz)
STA1
STA2
Capture Effect
Time
%
TXOPs
A capture effect occurs because CWmin=15 at STA2 results in a backoff that is always less than EIFS at STA1
Channel access becomes fair when STA1 no longer starts EIFS after ACKs

## Slide 11
EIFS-after-ACK - Best Effort Traffic (5 GHz)
STA1
STA2
Time
%
TXOPs
Channel access is unfair because STA1 starts an EIFS after ACKs sent by the AP to STA2
Channel access becomes fair when STA1 no longer starts EIFS after ACKs

## Slide 12
EIFS-after-ACK - Video Traffic (5 GHz)
STA1
STA2
Time
%
TXOPs
A capture effect occurs because CWmin=7 at STA2 results in a backoff at STA2 that is always less than EIFS at STA1
Channel access becomes fair when STA1 no longer starts EIFS after ACKs
Capture Effect

## Slide 13: Proposed Solution for EIFS-after-ACK Issue (1)
Allow EIFS=DIFS PPDUs that contain a 14 or 32 Byte MPDU
  ACK/CTS = 14 Bytes, Block Ack = 32 Bytes
  These MPDU sizes are unique amongst the 802.11 control frames
  There is a hypothetical case that a 4 Byte data packet is sent without encryption and without A-MPDU, which results in a 32 Byte MPDU
  There are also 2 action frames that are exactly 32 Bytes
    WNM Notification Request/Response frame
    EIFS protection can be realized by adding a (reserved) optional subelement or by sending the frame at 6 Mbps
Can be limited to non-HT(-duplicate) and (HR-)DSSS packets
  These capture the majority of the CTS, ACK and Block Ack packets

## Slide 14: Proposed Solution for EIFS-after-ACK Issue (2)
The MPDU size can be determined from the PLCP header
  non-HT(-dup): L-SIG
  DSSS: SIGNAL and LENGTH
  HR-DSSS: SIGNAL, SERVICE and LENGTH
The L-SIG length of HT and VHT packets is always a multiple of 3, so there will be no confusion at devices that receive only the L-SIG of an HT/VHT packet

## Slide 15: EIFS-too-Long Issue (1)
EIFS is based on the longest possible ACK duration, but the actual ACK can be a lot shorter
  2.4 GHz
    SIFS+ACK(1Mbps)+DIFS = 10+304+10+2*9 = 342 us
    SIFS+ACK(24Mbps)+DIFS = 16+28+16+2*9 = 78 us
      Difference = 264us = 29 slots
  5 GHz
    SIFS+ACK(6Mbps)+DIFS = 16+44+16+3*9 = 94 us
    SIFS+ACK(24Mbps)+DIFS = 16+28+16+3*9 = 78 us
      Difference = 16us = 2 slots

## Slide 16: Simulation Setup for EIFS-too-Long
STA1
UDP
UDP
STA2
AP
STA1 is hidden from ACKs sent by STA2, but not for the Data PPDUs sent by the AP. EIFS by STA1 can be too long in this case.
L-SIG range of the Ack from STA2 to the AP

## Slide 17
EIFS-too-Long - Best Effort Traffic (2.4 GHz)
STA1
STA2
Capture Effect
Channel access becomes fair when EIFS at STA1 adapted to the expected ACK time
Time
%
TXOPs
A capture effect occurs because EIFS at STA1 is always longer than the OFDM ACK + backoff at STA2

## Slide 18
EIFS-too-Long - Best Effort Traffic (5 GHz)
STA1
STA2
Time
%
TXOPs
Channel access is unfair because EIFS at STA1 is longer than SIFS+ACK+DIFS at STA2
Channel access becomes fair when EIFS at STA1 adapted to the expected ACK time

## Slide 19
EIFS-too-Long - Video Traffic (5 GHz)
STA1
STA2
Time
%
TXOPs
Channel access is unfair because EIFS at STA1 is longer than SIFS+ACK+DIFS at STA2
Channel access becomes fair when EIFS at STA1 adapted to the expected ACK time

## Slide 20: Proposed Solution for EIFS-too-Long Issue (1)
Dynamic EIFS
  EIFS is based on a predicted duration of the expected response frame
    the response rate/MCS is determined using the PHY mandatory MCSs (see tables on next slide)
    assume Block Ack for VHT packets and for HT packets with Aggregation = 1
    otherwise, assume an ACK
      VHT single MPDU is undetectable in the PLCP, in which case the EIFS will be too long (which is probably acceptable)
The dynamic EIFS values should be minimum values, so that the existing (static) EIFS implementations are also still compliant

## Slide 21: Proposed Solution for EIFS-too-Long Issue (2)
Example dynamic EIFS tables based on the received PPDU’s Rate/MCS and expected response frame (BA or ACK)
DSSS / HR-DSSS (always ACK) |  |  |  | 
Rate of received frame | Response Rate | ACK Tx Time | Dynamic EIFS (for ACK) | EIFS
1 Mbps | 1 Mbps | 304 us | 342 us | 342 us
≥ 2 Mbps | 2 Mbps | 152 us | 190 us | 342 us
OFDM / ERP-OFDM / HT / VHT (BA or ACK) |  |  |  |  |  | 
Modulation of received frame | Response Rate | BA Tx Time | Dynamic EIFS for BA | ACK Tx Time | Dynamic EIFS for ACK | EIFS
BPSK | 6 Mbps | 68 us | 118 us | 44 us | 94 us | 94 us
QPSK | 12 Mbps | 44 us | 94 us | 32 us | 82 us | 94 us
≥16-QAM | 24 Mbps | 32 us | 82 us | 28 us | 78 us | 94 us

## Slide 22: Summary
There are two design issues with EIFS
  EIFS may get started after an Ack frame
  EIFS may be (much) longer than a hidden Ack
Proposed solutions
  allow EIFS=DIFS for 14 or 32 Byte packets
  allow EIFS to be based on the PPDU’s Rate/MCS